## Slide 1
Introduction to Spectrogram Analysis
Bioacoustics Research Program
© 2007-17, Cornell Bioacoustics Research Program
Sound Analysis Workshop Ithaca, NY 3 – 7 Apr 2017

## Slide 2
Time-domain and frequency domain representations of sound
Converting time-domain to frequency-domain: the DFT as a black box
Representing time-varying spectra: the spectrogram
Analysis resolution: the time-frequency tradeoff
Introduction to spectrograms

## Slide 3
Time-domain and frequency-domain representations of sound
Pure tone (sinusoid)
infinitely long sound, not changing over time
Notes: pure sinusoid, infinitely long (IMPORTANT LATER)
- note what the axes are!

## Slide 4
Time-domain and frequency-domain representations of sound
Pure tone (sinusoid)
infinitely long sound, not changing over time
Notes: pure sinusoid, infinitely long (IMPORTANT LATER)
- note what the axes are!

## Slide 5
490 Hz + 800 Hz
Time-domain and frequency-domain representations of sound
Multiple tones
infinitely long sound, not changing over time
Notes: sound may have multiple frequencies present at once;
when more than one frequency is present at once, to completely describe the sound in the freq domain you need two things: relative amplitudes of sounds (amplitude spectrum) and their relative phase or time relationship (phase spectrum)
we generally use only the amplitude spectrum
why the frequency domain representation is useful-- it’s what we hear

## Slide 6
Time-domain and frequency domain representations of sound
Converting time-domain to frequency-domain: the Fourier transform as a black box
Representing time-varying spectra: the spectrogram
Analysis resolution: the time-frequency tradeoff
Introduction to spectrograms

## Slide 7
Converting from the time domain to the frequency domain
Joseph Fourier (1768 – 1830)
Any constant sound can be represented as a sum of a series of sinusoids (pure tones).
DFT
Black box: a device, system, or object which can be viewed solely in terms of its input, output and transfer characteristics without any knowledge of its internal workings.
. . !
Any
Discrete Fourier Transform
Notes: (insert cake chemistry slide after this)

## Slide 8
Time-domain and frequency-domain representations of sound
L. V. Barbosa via Wikipedia
What M. Fourier taught us...
Any constant sound can be represented as a sum of a series of sinusoids (pure tones).

## Slide 9
Time-domain and frequency-domain representations of sound
Time
Frequency
Sound pressure
Sound power

## Slide 10
DFT
The Discrete Fourier Transform (DFT)
The DFT converts a time-domain representation (waveform) of N samples from a signal to a frequency-domain representation (spectrum).
The spectrum is quantized: it shows powers at N/2 + 1 discrete frequencies, evenly spaced between 0 Hz and the Nyquist frequency (Fs/2).
amplitudes (∝ sound pressures) at discrete times
power values at discrete frequencies
Notes: Note what the axes are!

## Slide 11
Digital representation of sound
Time-domain and frequency domain representations of sound
Converting time-domain to frequency-domain: the DFT as a black box
Representing time-varying spectra: the spectrogram
Analysis resolution: the time-frequency tradeoff
Introduction to spectrograms

## Slide 12
Representing time-varying spectra
PROBLEM:
Most biological sounds change in spectrum over time.
A spectrum has no time dimension, so we can’t see these interesting changes if we make a single spectrum of a sound.
BUT...
Notes: Remember the idealized transformation between time and freq domains– signal is infinitely long, and doesn’t vary over time.

## Slide 13
Representing time-varying spectra
SOLUTION:
Chop the signal up into very short time segments, use the DFT to compute the power spectrum of each segment (or “window”, “slice”).
The sequence of power spectra is called the spectrogram.
Spectrograms are usually displayed with successive spectra side by side, using color to indicate relative power.
PROBLEM:
Most biological sounds change in spectrum over time.
A spectrum has no time dimension, so we can’t see these interesting changes if we make a single spectrum of a sound.
BUT...
Notes: Remember the idealized transformation between time and freq domains– signal is infinitely long, and doesn’t vary over time.
[simplification– the spectrogram is just the magnitude portion of the STFT; but we ignore and don’t mention the phase spectrum]

## Slide 14
Representing time-varying spectra
Notes: Note the axes in the spectrum: X= frequency, Y = amplitude. Note– NO TIME AXIS!

## Slide 15
Representing time-varying spectra

## Slide 16
Representing time-varying spectra

## Slide 17
Representing time-varying spectra

## Slide 18
Representing time-varying spectra
Notes: Notice that this is discrete, quantized– discrete time slice w/ particular duration, and frequency bins w/finite height.

## Slide 19
Spectrograms
Each column or time bin contains one spectrum, the output of a single DFT.
By default, Raven displays smoothed spectrograms that obscure the true discrete structure of the spectrogram:
A spectrogram is a matrix of numbers.
Each number represents the intensity in a discrete (short) time period and a discrete (narrow) frequency band.
The matrix is usually visualized as a spectrogram image.
Notes: DO IT:
(1) export samples to Excel, do color coding.

## Slide 20
Spectrograms
Raven’s spectrogram slice view shows one individual spectrum from a spectrogram.
Notes: DO IT:
(1) open a signal in Raven, turn off smoothing, zoom in, make a slice, drag position marker around.

## Slide 21
There is no such thing as the spectrogram of a signal; many different spectrograms can be made of a signal.
There is (often) no such thing as the best spectrogram of a signal.
Making spectrograms involves tradeoffs.
Spectrograms
Notes: There are lots of ways to vary a a spectrogram; for now, let’s look at just one...

## Slide 22
Spectrograms
How long? (How many samples?)
Notes: Note the axes in the spectrum: X= frequency, Y = amplitude. Note– NO TIME AXIS!
** we can take a longer or shorter piece to make the spectrum; let’s see what happens when we vary that...

## Slide 23
Spectrograms
number of samples used to make each spectrum (“window size”)
Notes: go to Raven, have them play w/window size slider– what happens? describe effect

## Slide 24
Spectrograms
There is an inescapable tradeoff between a spectrogram’s sharpness (or resolution) in time and frequency.

## Slide 25
Time-frequency tradeoff
Spectrogram too smeared in time  smaller window size
Spectrogram too smeared in frequency  larger window size
Rules of thumb for adjusting spectrogram parameters
Spectrograms

## Slide 26
Questions?
Spectrograms