## Slide 1
Spectrogram Parameters
Bioacoustics Research Program
© 2007-17, Cornell Bioacoustics Research Program
Sound Analysis Workshop Ithaca, NY 3 – 7 April 2017

## Slide 2
Spectrogram parameters
Why not just use the defaults?

## Slide 3
Chipping sparrow
1/10 speed:
Spectrogram parameters
© Michael Hogan, 2006
Why not just use the defaults?
Notes: (need additional examples; CHSP?)

## Slide 4
How is a spectrogram like a pair of shoes?

## Slide 5
Window Size
Spectrogram parameters
Window Size controls the tradeoff between time and frequency sharpness in spectrum analysis.
Notes: Note “Record Length” used in Raven manual

## Slide 6
Window Size: the length of the audio segment used to make each individual spectrum.
Window Size controls the tradeoff between time and frequency sharpness in spectrum analysis.
Window Size (aka Window Length)
Spectrogram parameters
Window Size can be expressed either in samples or in time units (s, ms).

## Slide 7
Window Size and the time-frequency resolution tradeoff (aka “uncertainty principle”)
Spectrogram parameters
Window length = 256
Hop Size = 128 samples
DFT Size = 8192
Freq Grid = 2.7 Hz
Window length = 8192
Hop Size = 128 samples
DFT Size = 8192
Freq Grid = 2.7 Hz
Gap = 51 ms = 1125 samples
Notes: DO IT:
- open “Time-Frequency tradeoff.wav”

## Slide 8
Time-frequency tradeoff
Spectrogram too smeared in time  smaller window size
Spectrogram too smeared in frequency  larger window size
Rules of thumb for adjusting spectrogram parameters
Spectrograms

## Slide 9
Western Wood Peewee
Ryan Houston, utahbirds.org
Recording by Laura Gooch
Window Size and the time-frequency resolution tradeoff (aka “uncertainty principle”)
Spectrogram parameters
Notes: DO IT:
- open and work through in Raven; CHANGE ONLY WINDOW SIZE

## Slide 10
Spectrogram parameters
T-F sharpness tradeoff
Window Size and the time-frequency resolution tradeoff

## Slide 11
Spectrogram parameters
3 dB Filter Bandwidth
Window Size = 1500 pts
Window Size = 5000 pts
3 dB Filter Bandwidth is a measure of the “sharpness” of frequency lines in a spectrum
Notes: (illustrate on whiteboard)

## Slide 12
specify Filter Bandwidth directly, and Raven will choose the appropriate Window Size
Spectrogram parameters
3 dB Filter Bandwidth
measures the “sharpness” of frequency lines in a spectrum
depends on Window Size and Window Function
peak
peak–3 dB
3 dB BW
a measure of the “sharpness” of frequency lines in a spectrum

## Slide 13
Spectrogram parameters
T-F sharpness tradeoff
Window Size and the time-frequency resolution tradeoff
Notes: – in Raven, notice that:
(1) DFT options are powers of 2

## Slide 14
Questions?
Spectrograms

## Slide 15
Spectrogram Parameters
Bioacoustics Research Program
© 2007-17, Cornell Bioacoustics Research Program
Sound Analysis Workshop Ithaca, NY 3 – 7 April 2017
PART 2

## Slide 16
Spectrogram parameters: grid resolution
Frequency Grid Spacing (freq. bin size)
Notes: – freq grid spacing not only affects how the image looks zoomed in; also affects measurement precision
– in Raven: zoom way in, notice that
(1) power value shown for mouse position don’t change within a spectrogram cell
(2) freq grid resolution changes in discrete jumps as you change window size; why is this?

## Slide 17
Spectrogram parameters
freq resolution (measurement precision)
Frequency Grid
Notes: – in Raven, notice that:
(1) DFT options are powers of 2
(2) DFT values change as you change window size, but not smoothly; they jump:
> Raven by default chooses the smallest DFT ≥ Window Size
(3) each time DFT Size changes,

## Slide 18
Spectrogram parameters
Frequency Grid
Grid Spacing dropdown lets you directly choose
Grid Spacing depends on DFT Size
Available DFT sizes are powers of 2
By default, Raven uses the smallest DFT Size that is ≥ Window Size
You can improve measurement precision by choosing a smaller Frequency Grid Spacing
Larger DFT  finer “frequency grid spacing”, hence finer precision of frequency measurements; all measurements are ± gridSpacing/2
DFT Size determines the number of frequency bins in the spectrogram: N = DFT/2 + 1
height of each frequency bin = Fs / DFT; units: Hz;
Notes: – in Raven, notice that:
(1) DFT options are powers of 2
(2) DFT values change as you change window size, but not smoothly; they jump:
> Raven by default chooses the smallest DFT ≥ Window Size
(3) each time DFT Size changes,

## Slide 19
Spectrogram parameters
DFT Size determines how many bins the total frequency space is divided into
Remember:
frequency measurements are quantized into discrete bins
Frequency Grid Spacing (freq. bin size)
larger DFT  more (hence smaller) frequency bins, greater precision in frequency measurements
DFT Size / Frequency Grid (aka FFT Length, Transform Size)

## Slide 20
Time-frequency tradeoff
Spectrogram too smeared in time  smaller window size
Spectrogram too smeared in frequency  larger window size
Rules of thumb for adjusting spectrogram parameters
Spectrograms
Spectrogram smoothness (measurement precision)
Spectrogram too coarse in frequency  larger DFT size (smaller frequency grid (bin) size)

## Slide 21
Western Wood Peewee
Ryan Houston, utahbirds.org
Recording by Laura Gooch
DFT Size and frequency “smoothness”
Spectrogram parameters
Notes: DO IT:
- make 2 spgs; unlink spectrogram parameters
open and work through in Raven;
UNSMOOTH
CHANGE ONLY DFT

## Slide 22
Hop Size (time bin size)
Spectrogram parameters: grid resolution

## Slide 23
Spectrogram parameters
time resolution (measurement precision)
Time Grid

## Slide 24
Spectrogram parameters
Time Grid
Hop Size is the width of each time bin or column in the spectrogram; units: samples, ms, or s.
Determined by Window Size and Overlap between successive windows: hop size = (100% - overlap%) * WindowSize
Raven lets you specify hop size directly (in either ms or samples) or by setting % window overlap.
Hop Size determines the precision of time measurements: measurements are ± HopSize/2
You can improve time measurement precision by specifying a higher Overlap (Raven’s default is 50% Overlap).

## Slide 25
Representing time-varying spectra
Notes: • Remember this?

## Slide 26
Representing time-varying spectra
Notes: • this was an oversimplification; this would suggest that the hop size equals the window length
• but in fact, we usually overlap successive windows/slices; let’s take a look at how this works...

## Slide 27
window length = 10 overlap = 0, hop size = 10
Window Overlap and Hop Size
Spectrogram parameters

## Slide 28
Window Overlap and Hop Size
Spectrogram parameters
window length = 10 overlap = 3, hop size = 7

## Slide 29
Spectrogram parameters
Window Length and Overlap together determine Hop Size
Remember:
time measurements are quantized into discrete bins
higher Overlap  smaller time bins, greater precision in time measurements
Window Overlap / Hop Size (aka Hop Length)
Hop Size (time bin size)

## Slide 30
Time-frequency tradeoff
Spectrogram too smeared in time  smaller window size
Spectrogram too smeared in frequency  larger window size
Rules of thumb for adjusting spectrogram parameters
Spectrograms
Spectrogram smoothness
Spectrogram too grainy in frequency  larger DFT size (smaller frequency grid (bin) size)
Spectrogram too grainy in time  higher overlap (smaller hop size)

## Slide 31
Western Wood Peewee
Ryan Houston, utahbirds.org
Recording by Laura Gooch
Hop Size and time “smoothness”
Spectrogram parameters
Notes: DO IT:
- make 2 spgs; unlink spectrogram parameters
- open and work through in Raven; CHANGE ONLY OVERLAP

## Slide 32
Questions?
Notes: BREAK HERE

## Slide 33
Time bin (hop) size
Determined by parameters
DFT (FFT) size
Window Size (Length)
Overlap relative to Window Size
Frequency bin size
Time-Frequency smearing tradeoff
Visible features of the spectrogram
Spectrogram parameters
Summary

## Slide 34
Oriente Warbler
surfbirds.com
Spectrogram parameters in practice
Notes: “Now you try...”

## Slide 35
Spectrogram parameters
T-F sharpness tradeoff
freq resolution (measurement precision)
time resolution (measurement precision)
Window Function

## Slide 36
The spectrum of a rectangular chunk of a sinusoid contains large sidelobes: energy appears at frequencies below and above the center frequency:
If we taper the amplitude values at the start and end of the chunk, the sidelobes become smaller:
To taper the signal, we multiply the samples in it by a window function.
Window Functions
Spectrogram parameters
sidelobes
rectangular window
tapered window

## Slide 37
Different window functions (types) are characterized by different bandwidths and sidelobe heights relative to the height of the main lobe (sidelobe rejection).
Remember that bandwidth varies with window size; larger window size  narrower bandwidth.
Window Functions
Spectrogram parameters
Notes: REVISE THIS SLIDE:
There are two measurements we can use to describe this spectrum: BW and sidelobe rejection

## Slide 38
Window types differ in main-lobe bandwidth, and in height and width of sidelobes.
Window Functions
Spectrogram parameters

## Slide 39
(Sidelobes can often be suppressed or minimized in spectrogram images by adjusting brightness and contrast.)
Effects of window type in spectrograms
Spectrogram parameters

## Slide 40
Spectrogram parameters
That’s all, folks!
T-F sharpness tradeoff
freq resolution (measurement precision)
main lobe- sidelobe tradeoff
time resolution (measurement precision)
Summary

## Slide 41
Spectrogram parameters
A puzzle...
Notes: long window gives very sharp frequency resolution, but sloppy time– look at edges
in long window, a single window is longer than the gap
do exercise with 1000 Hz tones by +50

## Slide 42
Spectrogram parameters
A puzzle...