## Slide 1
Raven Measurements
© 2007-17, Cornell Bioacoustics Research Program
Sound Analysis Workshop Ithaca, NY April 2017

## Slide 2
Raven Selection and Measurements
Basic Measurements
How to make selections and add measurements
Sort or reorder selections
How to plot measurements
Export and import selection tables
How to add annotations
. . .

## Slide 3
Limitations of basic Raven measurements
Basic Raven measurements are based on everything in the selection box
Variability of manually drawn boxes:
signal-to-noise ratio
brightness and contrast settings
distance between animal and mic
human subjectivity
reverberation
. . .

## Slide 4
Limitations of basic Raven measurements
Inter-observer variation
Notes: 6 sound analysis “experts” with decades of experience can’t agree on simple measurements!

## Slide 5
Mitigating measurement limitations
“Robust” measurements
Measurements based on Peak Frequency Contour

## Slide 6
“Robust” measurements of energy distribution
Based on percentile distributions of energy in time and frequency
Measurements that are less sensitive to (“robust” against) variation in:
signal-to-noise ratio
brightness and contrast settings
distance between animal and mic
human subjectivity
reverberation
. . .
http://commons.wikimedia.org

## Slide 7
“Robust” measurements of energy distribution
50% energy
50% energy
50% energy
50% energy

## Slide 8
“Robust” measurements of energy distribution
90% Duration
90% Bandwidth

## Slide 9
Limitations of basic Raven measurements
Inter-observer variation

## Slide 10
Limitations of basic Raven measurements
Inter-observer variation
“basic”
“robust”

## Slide 11
Peak Frequency Contour measurements
Measurements based (hopefully) on just the signal
Basic Raven measurements are based on everything in the selection box
but we’re only really interested in some of what’s in the box: the signal
Peak Frequency Contour (PFC) measurements may help
based on peaks in each spectral slice in a selection

## Slide 12
Peak Frequency Contour measurements
Based on peaks in each spectral slice in a selection

## Slide 13
Peak Frequency Contour measurements
Based on peaks in each spectral slice in a selection

## Slide 14
Peak Frequency Contour measurements
Measurements derived from PFC

## Slide 15
...
?