## Slide 1
What are decibels (and why are they confusing)?
Bioacoustics Research Program
© 2007-17, Cornell Bioacoustics Research Program
Sound Analysis Workshop Ithaca, NY 3 – 7 April 2017

## Slide 2
What are decibels (and why are they confusing)?
© 2007-16, Cornell Bioacoustics Research Program
North American Ornithological Conference Washington, DC 15 – 16 August 2016
Analysis of Biological Sounds Using Raven Pro
Bioacoustics Research Program

## Slide 3
What is a decibel?
Decibels seem to mean different things depending on the situation...

## Slide 4
Measuring sound: decibels
What is a decibel?
A decibel is not a physical unit!
A decibel is a logarithmic unit for expressing the ratio of two quantities: a quantity being measured and a reference quantity
In acoustics, the two quantities being compared are typically acoustic power or intensity.
“The decibel confers a number of advantages, ... . On the other hand, even some professionals find the decibel confusing and cumbersome.”
–– Wikipedia
(like percentage)
Notes: - familiar-- like a percentage

## Slide 5
A logarithmic unit for expressing the ratio between a measured quantity of interest, and a reference value.
Measuring sound: decibels
What is a decibel?
(where P represents pressure)
Pref depends on the context, and should always be stated (unless the context makes it clear)
Notes: - familiar-- like a percentage;
TO DO: add explanation of RMS

## Slide 6
Measuring sound: decibels
Sound Pressure Level (SPL)
By convention, use threshold pressure of human hearing as Pref: 20 µPa
Average sound pressure of a jet engine at 50 m:
Average background sound pressure in typical quiet library:
dB SPL is a common way of expressing the absolute intensity of a sound
Examples:
Notes: SPL is one context where dB are used

## Slide 7
Measuring sound: decibels
http://www.sengpielaudio.com/TableOfSoundPressureLevels.htm
“dB SPL” means “dB re 20 µPa”
Notes: So, one convenient property of dB is that they compress an awkward range of measurements into something manageable

## Slide 8
Measuring sound: decibels
Useful properties of decibels
Make large numerical ranges of measurements more manageable
The sign of a dB value indicates whether the measured value is greater or less than the reference value:
positive dB: measurement > reference
negative dB: measurement < reference
0 dB: measurement = reference
The just-noticeable difference (jnd) in sound pressure between two sounds remains ≈ 1~2 dB irrespective of absolute sound pressures.
Notes: RAVEN: dB tone pairs

## Slide 9
Measuring sound: decibels
Sound pressure level: (almost) always > 0
Recording level (dBFS = dB full scale = dB re the maximum sample value): always ≤ 0
Uncalibrated power re arbitrary reference (Raven: always > 0)
standard reference pressure in air: 20 µPa (ALWAYS STATE!) in water: 1 µPa
BEWARE! most sound level meters by default report sound levels with different frequencies weighted by human frequency-dependent hearing sensitivity! (dBA, dBB, dBC)
if you report sound level measurements of a particular sound source, ALWAYS STATE the microphone’s distance from the source!
How are decibels used?
Signal-to-noise ratio (SNR): either ≤ 0 or ≥ 0

## Slide 10
Measuring sound: decibels
A-, B-, C-, and Z-weighting
By default, most sound level meters report spectrally weighted levels based on human hearing sensitivity: “A-weighted” decibels, or dBA
dBA may not be appropriate in contexts unrelated to human perception!

## Slide 11
Measuring sound: decibels
One of the most widely read papers in 2014 in the Journal of the Acoustical Society of America:
Is that a sound level meter in your pocket?
“ This study showed that certain sound measurement apps for Apple smartphones and tablets may be considered accurate and reliable to be used to assess occupational noise exposures.”

## Slide 12
Are Raven’s dB measurements SPL?
By default, Raven’s dB measurements are relative to an arbitrary reference and cannot be related to “real-world” measurement units (like SPL).
You can make true calibrated (SPL) measurements in Raven if you have additional information available about the recording system.

## Slide 13
Why Raven’s dB measurements aren’t dB SPL
The digital recording chain
1. microphone
2. preamplifier
3. analog / digital converter
sound pressure (µPa) vs. time
voltage (mV) vs. time
(bigger) voltage (mV) vs. time
sample values vs. time
e.g., 16 bit: [-32768, 32767]

## Slide 14
Why Raven’s dB measurements aren’t dB SPL
sound pressure (µPa) vs. time
sample values vs. time
e.g., 16 bit: [-32768, 32767]
Sample units are proportional to µPa
But what’s the proportionality constant?
What we want: µPa
What Raven knows: sample units

## Slide 15
1. microphone
2. preamplifier
3. analog / digital converter
sound pressure (µPa) vs. time
voltage (mV) vs. time
(bigger) voltage (mV) vs. time
sample values vs. time
e.g., 16 bit: [-32768, 32767]
Why Raven’s dB measurements aren’t dB SPL
proportionality constant depends on these

## Slide 16
What you need to make true SPL measurements with Raven
1. Microphone sensitivity:
How much voltage does the mic output for a given sound pressure?
2. Preamp gain:
How much is the output voltage from the mic amplified?
3. Digitizer sensitivity:
What input voltage does the maximum sample value represent?
Method 1: stepwise calibration
For field recordings, we often don’t know any of this!

## Slide 17
What you need to make true SPL measurements with Raven
Method 2: end-to-end system calibration
1. microphone
2. preamplifier
3. analog / digital converter
sound pressure (µPa) vs. time
voltage (mV) vs. time
(bigger) voltage (mV) vs. time
sample values vs. time
e.g., 16 bit: [-32768, 32767]

## Slide 18
1. microphone
2. preamplifier
3. analog / digital converter
“Black Box” recording system [ mic + preamp + digitizer ]
What you need to make true SPL measurements with Raven
Record a calibration sound of known SPL, use that known value to determine the proportionality constant to convert sample values to sound pressure.
For field recordings, we often don’t have this!
Method 2: “end-to-end” system calibration
sound pressure (µPa) vs. time
sample values vs. time
e.g., 16 bit: [-32768, 32767]

## Slide 19
What you need to make true SPL measurements with Raven
Method 1: stepwise calibration
Method 2: end-to-end system (black box) calibration
need detailed information on how the signal is transformed by: (1) the microphone (sound pressure → voltage) (2) the preamplifier (small voltage → bigger voltage) (3) the A/D converter (voltage → sample units)
need a recording of a signal with a known SPL that can be used
to calibrate other recordings made with the same system (including the same gain setting)
• By either method, we need to take extra steps before and/or while making field recordings in order to make true SPL measurements with Raven.
• Without calibration info, we can make relative comparisons of dB within a recording, but not absolute dB measurements.

## Slide 20
Making true SPL measurements with digital recordings

## Slide 21
Measuring sound: decibels
Why are decibels confusing?
Because the reference level is sometimes implied rather than stated, people forget that a dB value is a comparison between two quantities.
Logarithms are not intuitive– they are often confusing to people who don’t work with them on a regular basis!
(so always state the reference level!)
“The decibel confers a number of advantages, ... . On the other hand, even some professionals find the decibel confusing and cumbersome.”
–– Wikipedia

## Slide 22
Measuring sound: decibels
The most important thing to remember about dB...
Whenever decibels are used, ask:
“dB relative to what?”

## Slide 23
What is a decibel, anyway?
presumably dB re 20 µPa,
probably A-weighted
dBFS (i.e., dB re the recorder’s clipping level)
dB re original signal
(at what distance?)
dB re arbitrary reference