## Slide 1
Band-Limited Energy Detector (BLED)
Bioacoustics Research Program
© 2007-17, Cornell Bioacoustics Research Program
Sound Analysis Workshop Ithaca, NY 3 – 7 April 2017

## Slide 2
Band-Limited Energy Detector (BLED)

## Slide 3
Band-Limited Energy Detector (BLED)

## Slide 4
Band-Limited Energy Detector (BLED)
Detects events where the energy in a specified frequency band exceeds a threshold for a specified range of durations.
Gaps where the energy drops below the threshold are ignored unless they exceed a minimum separation threshold.
The BLED is non-specific: it ignores shape and pattern of the sound.
What it does

## Slide 5
Band-Limited Energy Detector

## Slide 6
Stage 1. Identify candidate detections, based on signal-to-noise ratio (SNR) in a specified frequency band.
Stage 2. Eliminate candidates that are too short, too long, or too sparse.
Band-Limited Energy Detector
How it works
Notes: RESTRUCTURE:
STAGE 1: Identify candidate detections (by identifying gaps)
STAGE 2: Screen candidates by duration and occupancy.

## Slide 7
Stage 1. Identify candidate detections, based on signal-to-noise ratio (SNR) in a specified frequency band.
Band-Limited Energy Detector
How it works
a. Calculate the in-band power for each spectral slice (frame).
b. Estimate the in-band background noise based on the distribution of powers for all frames.
c. Find gaps where the power remains below the specified SNR for longer than a specified minimum separation time.
d. Consider segments between gaps as candidate detections.
Notes: *** in-band power or energy??? [ask Dean]
RESTRUCTURE:
STAGE 1: Identify candidate detections (by identifying gaps)
STAGE 2: Screen candidates by duration and occupancy.

## Slide 8
Time →
In-band power (dB)
Power order →
In-band power (dB)
1. Calculate in-band power for each spectral slice (or “frame”):
2. Estimate background noise:
a. sort the power values
b. choose a low percentile power value for the noise estimate
20%
Band-Limited Energy Detector
Stage 1: Identify candidate detections

## Slide 9
Time →
In-band power (dB)
3. Apply noise estimate + threshold to sequence of power measurements:
20% noise estimate
4. Identify gaps longer than Minimum Separation where power is < threshold:
Band-Limited Energy Detector
gap
Stage 1: Identify candidate detections
+10 dB SNR threshold

## Slide 10
Time →
In-band power (dB)
5. Consider segments between gaps to be candidate detections:
Band-Limited Energy Detector
gap
Stage 1: Identify candidate detections

## Slide 11
Time →
In-band power (dB)
Eliminate candidates that are too short, too long, or too “sparse”; declare remaining candidates to be detections:
Band-Limited Energy Detector
Stage 2: Eliminate candidate detections
5. Consider segments between gaps to be candidate detections:

## Slide 12
Band-Limited Energy Detector
What do we mean by too sparse?
Time →
In-band power (dB)
Occupancy: The percentage of individual power values in a candidate detection that are above the SNR threshold.
A candidate detection is too sparse if its occupancy is below the specified Minimum Occupancy.

## Slide 13
1.2. Estimate the background noise by using a low percentile of all of the in-band power values.
1.1. Compute in-band power for each frame (spectral slice).
1.4. Identify gaps longer than the minimum separation parameter where the power remains < SNR threshold.
1.5. Consider sequences of frames between gaps as candidate detections.
2.1. Eliminate candidate detections that are too short, too long, or too sparse.
2.2. Declare the remaining candidates as detections.
How it works (recap)
Band-Limited Energy Detector
1.3. Determine the SNR threshold (add specified dB value to noise estimate).
Stage 1: Identify candidate detections
Stage 2: Prune candidates

## Slide 14
What you need
1. Lower and upper frequency limits for target.
2. Min and max duration of target.
3. Minimum separation (“gap”) between targets.
Band-Limited Energy Detector
4. Approximate signal-to-noise ratio.
The minimum separation needed to recognize that there are two separate events (rather than one with a brief dropout); this is typically much shorter than the minimum separation between events that you observe in the recording.

## Slide 15
Band-Limited Energy Detector