## Slide 1: Key Design Requirements
Functional Requirements
Platform
Depth: depth of Robison dives
ROVs: must be functional for Robison mid-water dives on all platforms
Weight: must be able to mount laser to the front of ROVs
Size of system: laser must fit in front of ROV and remaining system must fit on vehicle
Electrical
Power: must provide adequate power for selected laser (Laserglow 1 W 671 nm DPSS laser), controller, and related components
Voltage: must use available voltages with sufficient wattage from each ROV
Communications: must be able to control the laser from the host ROV
Environmental
Temperature: stay within the range of the laser specifications
System Design Requirement
Platform
Depth: 4000m
ROVs: Ricketts, Ventana, MiniROV
Weight: laser housing <30 lbs
Size of system: TBD
Electrical
Power: +12V, 125 W peak, < 60 W nominal
Voltages:
Ricketts: 240 VDC, 110 VAC
Ventana: 375 VDC, 110 VAC
MiniROV: 400 VDC
Communications: RS232
Environmental
Temperature: 2 - 35° C

## Slide 2: Key Design Requirements
Functional Requirements
Cameras
Resolution: must be able to resolve a minimum of 1 Mpixel
Frame rate: sufficient rate to minimize particle streaking
Light sensitivity: sufficient to image light in the wavelength of the laser in low light environments
Laser
Wavelength: frequency of laser light shall minimize changes in organismal behavior and response
Optical power: should be sufficient to illuminate particles in sheet of 0.5 m2
Sheet thickness: Laser and optics shall generate a sheet thin enough to isolate flows
Sheet area: Laser and optics shall generate a sheet large enough to image the motion of a 10 cm animal
System Design Requirement
Cameras
Resolution: the current ROV cameras are sufficient, a camera upgrade may be proposed for 2016
Frame rate: minimum of 30 Hz with ability to change shutter speed
Light Sensitivity: dependent on camera properties
Laser
Wavelength: 671 nm
Optical power: 1 W
Sheet thickness: 1 mm
Sheet area: 0.5 m2