## Slide 1: DeepPIV Simple Block Diagram
Laser Housing
Controller Housing
Laser
Optics
Glass
Port
Laser Controller
Serial to
Analog
Converter
Vicor, 150W
HV:12Vdc
DC-DC
Converter
To
Vehicle
MINM-25
MINM-25
MINK-10L
MINK-10L
12Vdc
Analog Control
High Voltage DC
Serial Comms

## Slide 2: MiniROV Connection
DeepPIV
Laser
Housing
Controller
Housing
DeepPIV
Power
Can
MiniROV
375Vdc
Serial
375V Vicor
MINM-25
MINM-25
MINK-10L
MINK-8L

## Slide 3: Ventana/Ricketts Connection
DeepPIV
Laser
Housing
Controller
Housing
DeepPIV
Power
Can
Ventana
or
Ricketts
300Vdc
or
240Vdc
300V Vicor
MINM-25
MINM-25
MINK-10L
MINK-10L
Science
Can
Serial
MINK-10

## Slide 4: Ventana/Ricketts Interface Can Optional Connection
DeepPIV
Laser
Housing
Controller
Housing
DeepPIV
Power
Can
120Vac
Ethernet
375V Vicor
MINM-25
MINM-25
MINK-10L
MINK-10L
Interface
Can
MINK-10L
MINK-10L
Ventana
or
Ricketts
375Vdc
Serial

## Slide 5: Power Budget
Laser: 12Vdc @ 5A nominal
  10.5A Peak on startup
DGH Analog Output Mod: 12V (>1W)
Maximum usage: 126 Watts
Vicor Micro ~80% Efficiency
  ~160 Watts input from vehicles