## Slide 1: Timelines

## Slide 2
USBL transponder
acoustic release
anchor
float
iUSBL
tines
science payload
battery
control
LBL (x4)
a-modem
antenna
INS/DVL
hibernation controller
nose
mission-dependent trigger
a-modem (station M)
volcano eruption detector (arctic)
Notional System

## Slide 3: New subsystems/caps
Must have
  Docking system
  Hibernation controller
  Corrosion-free exterior
  Extended duration s/w
  Low-altitude flight behavior
  No-surfacing emergency system
    in case any of the critical subsystems fails: loss of nav, loss of dock power/signal, loss of control, loss of propulsion, loss of power.
Nice to have
    Volcano eruption trigger system
    Control planes for low-altitude/low-speed flight
      would also improve docking performance + buyancy compensation

## Slide 4: Science payload requirements
BENTHIC SURVEYS (STATION M)
Down-looking camera w/strobe
Depth: 4000m
1 km transects @ 2m altitude & 1m/s speed
Event-triggered transects:
  source: acoustic message sent by automated sediment trap
  up to TBD/year (e.g. 2/year)
Total of 6 transects/year.
MUD VOLCANO SURVEYS (ARCTIC)
Multibeam echosounder & side-scan sonar
Depth: between 290 and 760m depending on the volcano
2-hour surveys of a predefined area
Event-triggered surveys:
  source: TBD signal sent by TBD high-SPL detection
  up to TBD/year (e.g. 2/year)
Total of 6 surveys/year
CONSTRAINTS
Equipment needs to ship May 2019
Op area will be under ice most of the year

## Slide 5: High-risk elements
Software: Can the vehicle boot reliably after a long hibernation period?
Oil leakage: is there sufficient oil reserve to last 12 months?
Effect of long-term exposure to:
  wet and corrosive environment
  cold
  high-pressure

## Slide 6: Mid-risk elements
Docking
Undocking
Not enough energy to finish the mission
Loss of nav
Excessive change of buoyancy
Cannot resurface if a failure arises.
No way to know if the vehicle is lost
Shaft stiction after extended sleep
(Fouling by mud?)

## Slide 7: 2 VEHICLES OR 1?
2 is preferred:
  doubles the amount of testing hours
  allows the two missions to be run in parallel

## Slide 8: Park&Fly: Notional CONOPS
Arrive at site
Deploy the dock
Prep the AUV
Launch the AUV
Run first transect
Park
Parking verification
Depart site
AUV periodically parks and flies
Return to site
Recover AUV
Recover dock (minus anchor)