## Slide 1: Timelines

## Slide 2
USBL transponder
acoustic release
anchor
float
iUSBL
tines
science payload
battery
control
LBL (x4)
Avtrak
(track&comms)
antenna
INS/DVL
hibernation controller
nose
mission-dependent trigger
a-modem (station M)
volcano eruption detector (arctic)
Notional System
emergency scuttle

## Slide 3: New subsystems/caps
Must have
  Docking system
  Hibernation controller
  Corrosion-free exterior
  Extended duration s/w
  Low-altitude flight behavior
  Mission abort
    called on loss of any critical subsystem failure: nav, loss of dock power/signal, loss of control, loss of propulsion, loss of power.
    failure while docked: stay docked.
    failure while undocked: scuttle.
Nice to have
    Volcano eruption trigger system
    Control planes for low-altitude/low-speed flight
      only if science payload requires it
      fallback if docking is more difficult than anticipated
      would also improve docking performance + buyancy compensation

## Slide 4: Science payload requirements
BENTHIC SURVEYS (STATION M)
Down-looking camera w/strobe & multibeam echosounder
Depth: 4000m
1 km transects @
  camera: low altitude @ 2 knots
  multibeam: 50m @ 3 knots
Event-triggered transects:
  source: acoustic message sent by sediment event sensor
  up to TBD/year (e.g. 2/year)
Total of 4 transects/year.
MUD VOLCANO SURVEYS (ARCTIC)
Multibeam echosounder & side-scan sonar
Depth: between 290m and 760m depending on the volcano
2-hour surveys of a predefined area
Event-triggered surveys:
  source: TBD signal sent by TBD high-SPL detection
  up to TBD/year (e.g. 2/year)
Total of 6 surveys/year
CONSTRAINTS
Equipment needs to ship April 2019
Op area will be under ice most of the year

## Slide 5: Risk elements
HIGHER
Long-term exposure to environment.
Testing long mission in short time.
Guaranteeing data quality & integrity.
Software:
  Reliable vehicle boot after long hibernation.
  Mission execution error-handling.
Sufficient oil reserve for 12 months
LOWER
Docking.
Undocking (nb: fail-safe failure).
Sufficient energy to complete mission.
Loss of nav.
Excessive change of buoyancy.
Cannot resurface if a failure arises.
No way to monitor the vehicle in-mission
Emergency relocation of vehicle after 1 year

## Slide 6: 2 VEHICLES OR 1?
2 is preferred:
  doubles the amount of testing hours
  allows the two missions to be run in parallel

## Slide 7: Park&Fly: Notional CONOPS
Arrive at site
Deploy the dock and LBL
Prep the AUV
Launch the AUV
Run first transect
Park
Parking verification
Depart site
AUV periodically parks and flies
Return to site
Recover AUV
Recover dock and LBL (minus anchor)