## Slide 1: Science payload requirements
BENTHIC AUV (station M)
Down-looking camera w/strobe & multibeam echosounder
Depth: 4000m
1 km transects @
  camera: low altitude @ 2 knots
  multibeam: 50m @ 3 knots
Event-triggered transects:
  source: acoustic message sent by sediment event sensor
  up to TBD/year (e.g. 2/year)
Total of 4 transects/year.
ARCTIC AUV (mud volcanoes)
Multibeam echosounder & side-scan sonar
Depth: between 290m and 760m depending on the volcano
2-hour surveys of a predefined area
Event-triggered surveys:
  source: TBD signal sent by TBD high-SPL detection
  up to TBD/year (e.g. 2/year)
Total of 6 surveys/year
CONSTRAINTS
Equipment needs to ship April 2019
Op area will be under ice most of the year

## Slide 2
USBL transponder
acoustic release
anchor
float
iUSBL
tines
science payload
battery
control
LBL (x4)
Avtrak
(track&comms)
antenna
INS/DVL
hibernation controller
nose
mission-dependent trigger
a-modem (station M)
volcano eruption detector (arctic)
Notional System
emergency scuttle

## Slide 3: System Features
Must have
  Docking system
  Hibernation controller
  Corrosion-free exterior
  Extended duration s/w
  Low-altitude flight (benthic)
  "no-ship-above" mission aborts
    critical subsystem failure: nav, loss of dock power/signal, loss of control, loss of propulsion, loss of power.
    when docked: stay docked.
    when undocked: scuttle.
Nice to have
    Volcano eruption trigger system
    Control planes for low-altitude/low-speed flight
      only if science payload requires it
      fallback if docking is more difficult than anticipated
      would also improve docking performance + buyancy compensation

## Slide 4: Risk elements
NEW ELEMENTS
Long-term environmental exposure.
Robust docking/undocking.
Unsupervised boot reliability.
Guaranteeing data quality & integrity.
S/W error-handling.
OTHER
Running unsupervised.
  Cannot resurface if a failure arises.
  Cannot monitor progress while under-ice
Emergency relocation of vehicle after 1 year
Testing long mission in a short time.

## Slide 5: Timelines

## Slide 6: JUMP TO SPREADSHEET

## Slide 7: Backups

## Slide 8: 2 VEHICLES OR 1?
2 is preferred:
  doubles the amount of testing hours
  allows the two missions to be run in parallel

## Slide 9: Park&Fly: Notional CONOPS
Arrive at site
Deploy the dock and LBL
Prep the AUV
Launch the AUV
Run first transect
Park
Parking verification
Depart site
AUV periodically parks and flies
Return to site
Recover AUV
Recover dock and LBL (minus anchor)