## Slide 1: Park –n- Fly AUV
PI: Ken Smith
Scientists: Ken Smith and Charlie Paull
Project Manager: Brett Hobson
Systems Engineer: Mathieu Kemp
AUV Engineer: Hans Thomas
Controls Engineer: Rob McEwen
EE: Scott Jensen, Paul McGill
SE: Kent Headley, Rich Henthorn
ME: Jon Erickson, Brett Hobson
Project Team

## Slide 2: Park & Fly AUV – Abstract
Develop the capability for a persistent presence in the deep ocean
Conduct seasonal, seafloor imaging and bioacoustics surveys at Station-M. Without a ship.
Conduct seasonal, seafloor mapping with sidescan and multi-beam sonars to investigate the geologic evolution of mud volcanoes in the Arctic. Without a ship. For one year. Under the ice.

## Slide 3: Near-term opportunities
Benthic AUV (Ken)
4 deep transects in 12 months.
Sample w/down-looking camera one way, Bioacoustics on return.
Highly desirable: Event-triggered response.
Arctic AUV (mud volcanoes, Charlie)
6 under-ice surveys in 12 months
MBES & SSS
Highly desirable: Event-triggered response.
Ship date: April 2019
Notes
Camera: low-altitude / low-speed
Trigger: a-comms from sediment event sensor.
Notes
300m<D< 750m depending on volcano
Trigger: sound-pressure level from eruption.

## Slide 4: Approach
Stretch our routine AUV operation from a continuous run over 17 hours to ~four 3-hours missions spaced over one year
Park the AUV between missions and put it to sleep
An independent controller wakes the AUV up, runs the checklist, starts the mission and monitors for problems. If the AUV cannot get back to the dock, just sink to the seafloor and wait for help
Optionally enable event response by allowing a remote or local trigger the deployments remotely or locally for event response

## Slide 5
USBL transponder
acoustic release
anchor
float
iUSBL Homing Sensor
science payload
battery
control
Opt. LBL (x4)
Avtrak
(track&comms)
INS/DVL
hibernation controller
nose
trigger:
a-modem (benthic)
eruption detector (arctic)
Notional Vehicle
emergency scuttle
corrosion-free exterior
AUV Dock
Data & Opt.
Power
Transfer

## Slide 6
Hydroid Line Capture System
COTS (?)
Can we just buy the components, or even a complete nose section?
Can the existing system be used on a Dorado (~2x mass of Remus 600)?
Hydroid showed a path to full docking with power and data Tx
  Complicated
Bluecom or A-comms for data

## Slide 7
USBL transponder
acoustic release
anchor
float
iUSBL Homing Sensor
science payload
battery
control
Avtrak
(track&comms)
INS/DVL
hibernation controller
nose
trigger:
a-modem (benthic)
eruption detector (arctic)
Notional Vehicle
emergency scuttle
corrosion-free exterior
Data Transfer
Cable Latch
Whiskers
Data Transfer

## Slide 8
Test Dock for offshore MBARI
Line-capture docking
High bandwidth comms to MBARI
  <4 nmi
Homing beacon
Live camera feed to validate
Data transfer device

## Slide 9: What are the Risk elements?
Schedule (arctic AUV 2019 launch window)
Environmental exposure
Long-duration
Robust docking/undocking
Software reliability & error-handling
Testing long mission in a short time
Cannot monitor AUV status
Cost and # of operational assets

## Slide 10: Risk Reduction
Risk | Approach
Schedule | Address high risk ASAP Go/NoGo gates Postpone deployment
Long-term environmental exposure | all Ti/plastic/FRP larger oil reserve / testing
Long-duration | Independent hibernation controller battery chemistry: trade study
Robust docking | Lots of testing
S/W reliability and error-handling | Test and fix - early
Testing long-duration in short time | see Test Sequence
No AUV status | WG for St. M, fail-safe mission abort

## Slide 11: Why we think this is Do-able
Strong fleet of Dorado vehicles, spares and operational know-how
Dorado docking success in 2007, and efforts at Bluefin, WHOI/Hydroid and SPAWAR
Long-term deployment of the Benthic Rover
Industrial partnerships (motivated to ensure our success) with Sonardyne (homing), Bluefin, General Atomics (power/data transfer, batteries, homing)

## Slide 12: schedule
NOW:
  SYSTEM DESIGN, SYNTACTIC FOAM & BATTERY TESTING
SOON:
  COMPUTER S/W & H/W EVAL, BENTHIC PAYLOAD DEVELOPMENT, CONCEPT DESIGN REVIEW
NEXT YEAR:
  DETAILED DESIGN, TEST VEHICLE BUILD, DOCK BUILD, NEARSHORE DOCK TESTING
2018:
  PRODUCTION VEHICLE BUILD, MORE NEARSHORE TESTING FOLLOWED BY MARS TESTING AND 3-MONTH TEST DEPLOYMENT

## Slide 13: Estimated Resources
year | labor | expense | ship time
2016 | Brett: +3 weeks, Andy: 2 week Rob: +2 weeks Hans: + 2 weeks MK: 1 day/week | $1.1k | 
2017 | 3-4 FTEs: design/fab/testing | $100k | 10 days
2018 | 3-4 FTEs: fab/assembly/at-sea testing | $ 800k 2 AUVs | 10 days
2019 | 2 deployments |  | 5 days (contingency)
2020 | 2 recoveries |  | n/a

## Slide 14
Existing MBARI Dock

## Slide 15: ‘07 Docking Video - plays during question period

## Slide 16: End

## Slide 17: Backups

## Slide 18: Park&Fly: Notional CONOPS
Arrive at site
Deploy the dock and LBL
Prep the AUV
Launch the AUV
Run first transect
Park
Parking verification
Depart site
AUV periodically parks and flies
  - At Station-M, could control from shore via wave-glider comm relay
Return to site
Recover AUV
Recover dock and LBL (minus anchor)

## Slide 19: General Atomics - Notional

## Slide 20: WPDX Medium Power Data Sheet MBARI/Maughan
Power:
  150 Watt continuous, 240 Watt peak (1 hr), resonant transfer using PowerByProxi technology
  Voltage: 24v DC input and output
  Current: 6 Amp output
  Efficiency: ~75%
Data:
  100 Mbps ethernet
  Option RF: 2.4 GHz point to point Ubiquity Radio, 10mW nominal, adjustable to 600mW
  Option Optical: ‘work in progress’
0 to 5 mm separation (derated from 1cm to allow for potting thickness)

## Slide 21: Block Diagram of What we want to build for MARS Toast goes in the Toaster
Input:
375v @ 2 amps
or
24v @ 30 amps
Load Light
Resonant Power
Load Control / Mon
802.11 PtP Radio
Ethernet Switch / Status Mon
Inrush Lim / 375 to 24v
150W continuous
240W peak