## Slide 1: Park –n- Fly AUV
PI: Ken Smith
Scientists: Ken Smith and Charlie Paull
Project Manager: Brett Hobson
Systems Engineer: Mathieu Kemp
AUV Engineer: Hans Thomas
Controls Engineer: Rob McEwen
EE: Scott Jensen, Paul McGill
SE: Kent Headley, Rich Henthorn
and Brian Kieft
ME: Jon Erickson, Brett Hobson
Project Team

## Slide 2: Abstract Feedback
Rating: Some possibility of support
MT contact: Doug
The concept of having a system that could provide long-term presence, repeat survey, and
event response is well aligned with MBARI’s future research and development
objectives. This system could enable many new and unique scientific investigations.
For your phase 1 proposal, consider the following comments:
The team should step back from a schedule that is being driven by science-deployment
deadlines. Develop a project plan that is well thought out and engineering-based. The
project plan should focus on the high-risk elements first and include go/no-go gates as
these elements are investigated. Much can be gained by making MBARI’s existing
Dorado class AUVs’ hardware and software more robust as a first step. Sufficient testing
should be scoped into this plan and timeline as well. This should include a long-duration
test equivalent to the planned deployment duration. We feel it is premature to plan on
building two vehicles in 2017.
Finally, we note that the project team members are part of several large proposals for
2017 and beyond. The group should consider the timing and scope of each of these
efforts and provide a realistic high-level plan that includes priorities and timing of these
efforts to yield a more integrated and staged development prospectus.

## Slide 3: Feedback Conclusions
Drop the 2019 deployments as milestones
  Unless ready
Technology development drives the schedule
Focus on high-risk elements
Improve Dorado reliability
Lots of testing
  Including 1 year test before science deployment
Don’t pitch to build two vehicles in 2017 (no plans)
Coordinate with other projects
  Slow burn verses priority project: 5 year project

## Slide 4
Hydroid Line Capture System
COTS (?)
Can we just buy the components, or even a complete nose section?
Can the existing system be used on a Dorado (~2x mass of Remus 600)?
Hydroid showed a path to full docking with power and data Tx
  Complicated
Bluecom or A-comms for data

## Slide 5
USBL transponder
acoustic release
anchor
float
iUSBL Homing Sensor
science payload
battery
control
Avtrak
(track&comms)
INS/DVL
hibernation controller
nose
trigger:
a-modem (benthic)
eruption detector (arctic)
Notional Vehicle
emergency scuttle
corrosion-free exterior
Data Transfer
Cable Latch
Whiskers
Data Transfer

## Slide 6
Test Dock for offshore MBARI
Line-capture docking
High bandwidth comms to MBARI
  <4 nmi
Homing beacon
Live camera feed to validate
Data transfer device

## Slide 8: Park & Fly AUV – Abstract
Develop the capability for a persistent presence in the deep ocean
Conduct seasonal, seafloor imaging and bioacoustics surveys at Station-M. Without a ship.
Conduct seasonal, seafloor mapping with sidescan and multi-beam sonars to investigate the geologic evolution of mud volcanoes in the Arctic. Without a ship. For one year. Under the ice.

## Slide 9: Near-term opportunities
Benthic AUV (Ken)
4 deep transects in 12 months.
Sample w/down-looking camera one way, Bioacoustics on return.
Highly desirable: Event-triggered response.
Arctic AUV (mud volcanoes, Charlie)
6 under-ice surveys in 12 months
MBES & SSS
Highly desirable: Event-triggered response.
Ship date: April 2019
Notes
Camera: low-altitude / low-speed
Trigger: a-comms from sediment event sensor.
Notes
300m<D< 750m depending on volcano
Trigger: sound-pressure level from eruption.

## Slide 10: Approach
Stretch our routine AUV operation from a continuous run over 17 hours to ~four 3-hours missions spaced over one year
Park the AUV between missions and put it to sleep
An independent controller wakes the AUV up, runs the checklist, starts the mission and monitors for problems. If the AUV cannot get back to the dock, just sink to the seafloor and wait for help
Optionally enable event response by allowing a remote or local trigger the deployments remotely or locally for event response

## Slide 11: Abstract Feedback
Rating: Some possibility of support
MT contact: Doug
The concept of having a system that could provide long-term presence, repeat survey, and
event response is well aligned with MBARI’s future research and development
objectives. This system could enable many new and unique scientific investigations.
For your phase 1 proposal, consider the following comments:
The team should step back from a schedule that is being driven by science-deployment
deadlines. Develop a project plan that is well thought out and engineering-based. The
project plan should focus on the high-risk elements first and include go/no-go gates as
these elements are investigated. Much can be gained by making MBARI’s existing
Dorado class AUVs’ hardware and software more robust as a first step. Sufficient testing
should be scoped into this plan and timeline as well. This should include a long-duration
test equivalent to the planned deployment duration. We feel it is premature to plan on
building two vehicles in 2017.
Finally, we note that the project team members are part of several large proposals for
2017 and beyond. The group should consider the timing and scope of each of these
efforts and provide a realistic high-level plan that includes priorities and timing of these
efforts to yield a more integrated and staged development prospectus.

## Slide 12: Feedback Conclusions
Drop the 2019 deployments as milestones
  Unless ready
Technology development drives the schedule
Focus on high-risk elements
Improve Dorado reliability
Lots of testing
  Including 1 year test before science deployment
Don’t pitch to build two vehicles in 2017 (no plans)
Coordinate with other projects
  Slow burn verses priority project: 5 year project

## Slide 13
Hydroid Line Capture System
COTS (?)
Can we just buy the components, or even a complete nose section?
Can the existing system be used on a Dorado (~2x mass of Remus 600)?
Hydroid showed a path to full docking with power and data Tx
  Complicated
Bluecom or A-comms for data

## Slide 14
USBL transponder
acoustic release
anchor
float
iUSBL Homing Sensor
science payload
battery
control
Opt. LBL (x4)
Avtrak
(track&comms)
INS/DVL
hibernation controller
nose
trigger:
a-modem (benthic)
eruption detector (arctic)
Notional Vehicle
emergency scuttle
corrosion-free exterior
AUV Dock
Data & Opt.
Power
Transfer

## Slide 15
USBL transponder
acoustic release
anchor
float
iUSBL Homing Sensor
science payload
battery
control
Avtrak
(track&comms)
INS/DVL
hibernation controller
nose
trigger:
a-modem (benthic)
eruption detector (arctic)
Notional Vehicle
emergency scuttle
corrosion-free exterior
Data Transfer
Cable Latch
Whiskers
Data Transfer

## Slide 16
Test Dock for offshore MBARI
Line-capture docking
High bandwidth comms to MBARI
  <4 nmi
Homing beacon
Live camera feed to validate
Data transfer device

## Slide 17: What are the Risk elements?
Schedule (arctic AUV 2019 launch window)
Environmental exposure
Long-duration
Robust docking/undocking
Software reliability & error-handling
Testing long mission in a short time
Cannot monitor AUV status
Cost and # of operational assets

## Slide 18: Risk Reduction
Risk | Approach
Schedule | Address high risk ASAP Go/NoGo gates Postpone deployment
Long-term environmental exposure | all Ti/plastic/FRP larger oil reserve / testing
Long-duration | Independent hibernation controller battery chemistry: trade study
Robust docking | Lots of testing
S/W reliability and error-handling | Test and fix - early
Testing long-duration in short time | see Test Sequence
No AUV status | WG for St. M, fail-safe mission abort

## Slide 19: Why we think this is Do-able
Strong fleet of Dorado vehicles, spares and operational know-how
Dorado docking success in 2007, and efforts at Bluefin, WHOI/Hydroid and SPAWAR
Long-term deployment of the Benthic Rover
Industrial partnerships (motivated to ensure our success) with Sonardyne (homing), Bluefin, General Atomics (power/data transfer, batteries, homing)

## Slide 20: schedule
NOW:
  SYSTEM DESIGN, SYNTACTIC FOAM & BATTERY TESTING
SOON:
  COMPUTER S/W & H/W EVAL, BENTHIC PAYLOAD DEVELOPMENT, CONCEPT DESIGN REVIEW
NEXT YEAR:
  DETAILED DESIGN, TEST VEHICLE BUILD, DOCK BUILD, NEARSHORE DOCK TESTING
2018:
  PRODUCTION VEHICLE BUILD, MORE NEARSHORE TESTING FOLLOWED BY MARS TESTING AND 3-MONTH TEST DEPLOYMENT

## Slide 21: Estimated Resources
year | labor | expense | ship time
2016 | Brett: +3 weeks, Andy: 2 week Rob: +2 weeks Hans: + 2 weeks MK: 1 day/week | $1.1k | 
2017 | 3-4 FTEs: design/fab/testing | $100k | 10 days
2018 | 3-4 FTEs: fab/assembly/at-sea testing | $ 800k 2 AUVs | 10 days
2019 | 2 deployments |  | 5 days (contingency)
2020 | 2 recoveries |  | n/a

## Slide 22
Existing MBARI Dock

## Slide 23: ‘07 Docking Video - plays during question period

## Slide 24: End

## Slide 25: Backups

## Slide 26: Park&Fly: Notional CONOPS
Arrive at site
Deploy the dock and LBL
Prep the AUV
Launch the AUV
Run first transect
Park
Parking verification
Depart site
AUV periodically parks and flies
  - At Station-M, could control from shore via wave-glider comm relay
Return to site
Recover AUV
Recover dock and LBL (minus anchor)

## Slide 27: General Atomics - Notional

## Slide 28: WPDX Medium Power Data Sheet MBARI/Maughan
Power:
  150 Watt continuous, 240 Watt peak (1 hr), resonant transfer using PowerByProxi technology
  Voltage: 24v DC input and output
  Current: 6 Amp output
  Efficiency: ~75%
Data:
  100 Mbps ethernet
  Option RF: 2.4 GHz point to point Ubiquity Radio, 10mW nominal, adjustable to 600mW
  Option Optical: ‘work in progress’
0 to 5 mm separation (derated from 1cm to allow for potting thickness)

## Slide 29: Block Diagram of What we want to build for MARS Toast goes in the Toaster
Input:
375v @ 2 amps
or
24v @ 30 amps
Load Light
Resonant Power
Load Control / Mon
802.11 PtP Radio
Ethernet Switch / Status Mon
Inrush Lim / 375 to 24v
150W continuous
240W peak