## Slide 1: WPDX Medium Power Easy Swap Connector MARS Cabled Observatory
Thom Maughan
June 2016

## Slide 2: WPDX Medium Power Data Sheet
Power:
  150 Watt continuous, 240 Watt peak (1 hr), resonant transfer using PowerByProxi technology
  Voltage: 24v DC input and output
  Current: 6 Amp output
  Efficiency: ~75%
Data:
  100 Mbps ethernet
  Option RF: 2.4 GHz point to point Ubiquity Radio, 10mW nominal, adjustable to 600mW
  Option Optical: ‘work in progress’
0 to 5 mm separation (derated from 1cm to allow for potting thickness)

## Slide 3: Block Diagram of What we want to build for MARS Toast goes in the Toaster
Input:
375v @ 2 amps
or
24v @ 30 amps
Load Light
Resonant Power
Load Control / Mon
802.11 PtP Radio
Ethernet Switch / Status Mon
Inrush Lim / 375 to 24v
150W continuous
240W peak

## Slide 4: First, Demonstrate 150 Watt Power and 100Mbps data transfer “Single slot toaster with a piece of toast” on ROV at 1000 meters
Input:
120vac @ 2.5 amps
100Mbps ethernet
Toaster Top View
“Toaster” Side View
Slot Components
“Toast” Side View
Components
Load Light
Resonant Power
Load Control / Mon
802.11 PtP Radio
Ethernet Switch / Status Mon
120v AC to 24v DC
150W Lights
1080p EthernetCamera