## Slide 1
Benthic Observation System (BOS)

## Slide 2
BOS: 2-Camera Prototype Build/Testing in 2017
Records stereoscopic HD video
  Real-time HD video also streamed to ship
Narrow base allows BOS to land in and around rocky habitats
  Swappable bases depending on seafloor type
Downward approach camera assists with drop location
Attached fin allows BOS to be easily maneuvered underwater to multiple sites in one dive
Full system control from ship
System is easily transported and can be deployed from multiple ship classes
  Successfully operated on R/V John Martin in Monterey Bay in Sep. 2017 for initial testing

## Slide 3
BOS: NMFS Experiment in The Channel Islands
Participated in the National Marine Fisheries Untrawlable Habitat Experiment in October of 2017
  Evaluation of attraction and repulsion of fishes to underwater vehicles
Operated on the R/V Shearwater
  First operational deployment of BOS
  Joint operation between: MBARI, MLML, TNC, NOAA, and MARE
Recorded 5 days worth of stereo imagery
Able to reliably place BOS on the seafloor within a 5 meter radius of a specific coordinate
BOS was fully stable on steep rocky inclines/declines
All video and contextual data was available in real time

## Slide 4
BOS: Where do we go in 2018?
8-Camera version (4 camera pairs)
  Will give 360-degree coverage
  Less time required at each survey site
Fiber tether with strength member
  Will cut down on launch/recovery time and complexity
  Large bandwidth allows 8 channels of HD video streaming topside
Topside recording
  Eliminates need for slow post-recovery video transfer via USB
  Simpler subsea camera control
Coastal wide survey planned in Fall of 2018