## Slide 1: Benthic Observation System Concept Design Review (draft)
March 27, 2017

## Slide 2: Functional Requirements
The lander must provide the ability to identify, count, and size marine organisms by capturing video and/or still images.
The lander must have the ability to interface and log various contextual sensors, such as O2, pH, ADCP, acoustic, and other novel sensors such as 3G-ESP.
The lander must be a modular platform that can be reconfigured for various sensors and deployment scenarios.

## Slide 3: Operational Requirements (TNC)
Must operate tethered
Must operate in a benthic environment
Must capture stereo video
Must have 360 degrees of stereo video coverage
Must be rated to 300 meters
Must be able to land on or hover above rocky outcroppings
Must be able to collect data from up to 30 sites within a normal operational ship day
Must be able to be deployed from various vessels of opportunity
Must have real time video
Must have real time telemetry data (heading & depth)

## Slide 4: Operational Requirements (Barry)
Must operate autonomously
Must operate in a benthic environment
Must capture stereo still images
Must be rated to 1500 meters
Must be able to land on or near coral ridges
Must be able to operate from days to one year
Must be able to be deployed from MBARI ships
Must have O2, pH, ADCP, and CTD sensors

## Slide 5: Operational Requirements (Chavez)
Must operate autonomously
Must operate in a benthic environment
Must capture stereo video
Must be rated to 300 meters
Must be able to land on seafloor
Must be able to operate for 3-6 months
Must be able to be deployed from MBARI ships
Must have O2, and CTD sensors
Must be able to interface the 3G-ESP

## Slide 6: Operational Requirements (Benoit-Bird)
Must operate tethered
Must operate in a mid-water environment
Must capture stereo video
Must be rated to 300 meters
Must be able to be mounted to a mooring or be suspended from a ship
Must be able to operate 1-2 hours each at up to 5 sites per day from ships
Must be able to be deployed from MBARI ships or various smaller vessels
Must be able to interface the EK80 echosounder or similar
Must provide real time data when operating from a ship

## Slide 7: Operational Requirements Matrix
Requirement |  | TNC | Barry | Chavez | Benoit-Bird
Tethered |  | Yes | No | Yes | Yes
Autonomous |  | No | Yes | Yes | No
Depth 300 Meters |  | Yes | No | Yes | Yes
Depth 1500 Meters |  | No | Yes | No | No
Benthic |  | Yes | Yes | Yes | No
Mid-water |  | No | No | No | Yes
Stereo video |  | Yes | No | Yes | Yes
Stereo imaging |  | No | Yes | No | No
360 degrees coverage |  | Yes | No | No | No
O2 sensor |  | No | Yes | Yes | No (Nice)
pH probe |  | No | Yes | No (Nice) | No
CTD |  | No | Yes | Yes | No (Nice)
ADCP |  | No | Yes | No (Nice) | No
EK80 echosounder (or similar) |  | No | No | Yes | Yes
3G-ESP |  | No | No | Yes | No