## Slide 1: Benthic Observation System Concept Design Review (draft)
March 27, 2017

## Slide 2: Team & PIs
Principal Investigators
Jim Barry
Francisco Chavez
Kelly Benoit-Bird
Mary Gleason (TNC)
Rick Starr (MLML)
Design Team
Chad Kecy (PM)
Francois Cazenave
Kent Headley
Craig Okuda
Eric Martin
Mike Parker
Jared Figurski
Ryan Fields (MLML)
Tyler Maricich (Collaborator)

## Slide 3: CDR Agenda
Motivation behind the project
Science use cases
Functional requirements
Derived requirements
Summary

## Slide 4: Motivation for Benthic Observation System
Expressed desire for a modular platform which combines stereo imagery with contextual sensors
Modifiable system can reduce the number expensive one-off specific systems
Driven by an immediate need by The Nature Conservancy

## Slide 5: Science Use Case: TNC
Collaboration with NOAA-Fisheries to add visual component to the coast wide Fishery Resource Analysis and Monitoring (FRAM) trawl survey to assess “untrawlable” (rocky) habitats and inform fisheries stock assessments and management
Provide density estimates (#/m2) and size structure of 6-8 demersal species
  yelloweye, cowcod, lingcod, canary, bocaccio, greenspot

## Slide 6: Science Use Case: Barry
Long term collaboration with The Monterey Bay National Marine Sanctuary (MBNMS) to study the benthic biological environment at Sur Ridge
Characterize environmental conditions to help understand various processes
  Feeding in relation to water flow
  Predator-prey interactions
  Temporal variation in benthic conditions

## Slide 7: Science Use Case: Chavez

## Slide 8: Science Use Case: Benoit-Bird
The use of high resolution stereo video
  assists in the interpretation of the data acquired via acoustic instruments
  provides data on the behavior of the biota to the acoustic instruments themselves
    Biota sizes range from Humboldt squid to larger mammals

## Slide 9: Common Functional Requirements
The lander must provide the ability to identify, count, and size marine organisms by capturing video and/or still images.
The lander must have the ability to interface and log various contextual sensors, such as O2, pH, ADCP, acoustic, and other novel sensors such as 3G-ESP.
The lander must be a modular platform that can be reconfigured for various sensors and deployment scenarios.

## Slide 10: Derived Requirements (TNC)
Must operate tethered
Must be depth rated to 300 meters
Must operate in a benthic environment
Must be able to land on or hover above rocky outcroppings
Must capture stereo video
Must have near 360 degrees of stereo video coverage
Must be able to collect data from up to 30 sites within a normal operational ship day
Must be able to be deployed from various vessels of opportunity
Must provide real time telemetry data for positioning including video, depth, and heading

## Slide 11: Derived Requirements (Barry)
Must operate autonomously
Must be depth rated to 1500 meters
Must operate in a benthic environment
Must be able to sit on or near coral ridges
Must capture stereo still images
Must be able to operate from days to one year
Must be able to be deployed from MBARI ships
Must have O2, pH, ADCP, and CTD sensors

## Slide 12: Derived Requirements (Chavez)
Must operate autonomously
Must be depth rated to 300 meters
Must operate in a benthic environment
Must be able to sit on seafloor
Must capture stereo video
Must be able to operate for 3-6 months
Must be able to be deployed from MBARI ships
Must have O2 and CTD sensors
Must be able to interface the 3G-ESP
Must be able to interface the EK60 Echosounder

## Slide 13: Derived Requirements (Chavez)
Must operate tethered (to a cabled observatory)
Must be depth rated to 300 meters
Must operate in a benthic environment
Must be able to sit on seafloor
Must capture stereo video
Must be able to operate for one year between maintenance
Must be able to be deployed from MBARI ships
Must have O2 and CTD sensors
Must be able to interface the 3G-ESP
Must be able to interface the EK60 Echosounder
Must provide real time video/data

## Slide 14: Derived Requirements (Benoit-Bird)
Must operate tethered
Must be depth rated to 300 meters
Must operate in a mid-water environment
Must be able to be suspended from a ship
Must capture stereo video
Must be able to operate 1-2 hours each at up to 5 sites per day from ships
Must be able to be deployed from MBARI ships or various smaller vessels
Must be able to interface the EK80 echosounder or similar
Must provide real time video/data

## Slide 15: Derived Requirements (Benoit-Bird)
Must operate autonomous
Must be depth rated to 300 meters
Must operate in a mid-water environment
Must be able to be suspended from a mooring
Must capture stereo video
Must be able to collect 5 minutes of video/data every 30 minutes for 3 months
Must be able to be deployed from MBARI ships or various smaller vessels
Must be able to interface the EK80 echosounder or similar

## Slide 16: Operational Requirements Matrix
Requirement | TNC | Barry | Chavez | Benoit-Bird
Tethered | Yes | No | Yes | Yes
Autonomous | No | Yes | Yes | Yes
Depth 300 Meters | Yes | No | Yes | Yes
Depth 1500 Meters | No | Yes | No | No
Benthic | Yes | Yes | Yes | No
Mid-water | No | No | No | Yes
Stereo video | Yes | No | Yes | Yes
Stereo imaging | No | Yes | No | No
360 degrees coverage | Yes | No | No | No
Operate from MBARI ships | No | Yes | Yes | Yes
Operate from non-MBARI ships | Yes | No | No | Yes
O2 sensor | No | Yes | Yes | No (Nice)
pH probe | No | Yes | No (Nice) | No
CTD | No | Yes | Yes | No (Nice)
ADCP | No | Yes | No (Nice) | No
EK80 echosounder (or similar) | No | No | Yes | Yes
3G-ESP | No | No | Yes | No

## Slide 17: Summary
TNC: Preliminary design options studied – will be presented next
MBARI Use Cases
  Widely divergent sets of requirements
  Large design gap between autonomous & tethered
    Electrical energy required & software (data management)
  Can this task be performed with existing hardware?
  Can all requirements be met by one system?
Recommendations
  TNC: Proceed with PDR + build
  MBARI: Further study needed