## Slide 1: Benthic Observation System Preliminary Design Review for TNC Use Case (draft)
March 27, 2017

## Slide 2: Team & PIs
Principal Investigators
Mary Gleason (TNC)
Rick Starr (MLML)
Design Team
Chad Kecy (PM)
Francois Cazenave
Kent Headley
Craig Okuda
Eric Martin
Mike Parker
Jared Figurski
Ryan Fields (MLML)
Tyler Maricich (Collaborator)

## Slide 3: PDR Agenda
Science Background & Motivation
1st Generation Lander
Review of Functional & Derived Requirements
Proposed Concept
  Deck System
  Lander
  Camera Selection
  Topside System
  Software & Data Management
Proposed Design
Schedule
Next Steps

## Slide 4: Science Background
Collaboration with NOAA-Fisheries to add visual component to the coast wide Fishery Resource Analysis and Monitoring (FRAM) trawl survey (mostly in rocky habitats)
Provide density estimates (#/m2) and size structure of 6-8 demersal species
  Sizes range from 4” to 16”

## Slide 5: First Generation TNC Lander
Crab pot base
Stereo camera pair on
a rotatable mount
SeeStar (not part of
TNC Lander)
Separate handling line
and electrical tether

## Slide 6: Functional Requirements
The lander must provide the ability to identify, count, and size marine organisms by capturing video and/or still images.
The lander must have the ability to interface and log various contextual sensors, such as O2, pH, ADCP, acoustic, and other novel sensors such as 3G-ESP.
The lander must be a modular platform that can be reconfigured for various sensors and deployment scenarios.

## Slide 7: Derived Requirements (TNC)
Must operate tethered
Must be depth rated to 300 meters
Must operate in a benthic environment
Must be able to land on or hover above rocky outcroppings
Must capture stereo video
Must have near 360 degrees of stereo video coverage
Must be able to collect data from up to 30 sites within a normal operational ship day
Must be able to be deployed from various vessels of opportunity
Must provide real time telemetry data for positioning including video, depth, and heading

## Slide 8: Additional Requirements
Ability to transfer videos from lander during station transit periods
Topside control of system
  Cameras (start/stop REC)
  Lights (on/off)
Ability to stay on station for up to 6 minutes
Ability to count fish up to 4 meters away from lander
Ability to size fish up to 2 meters away from lander
Ability to synchronize all 8 cameras
Live video feed from 1 camera in each quadrant
  Total of 5 live video feeds
Load bearing tether (no second line)
Simplify launch and recovery processes
Ability to record the 8 HD video feeds topside in the future

## Slide 9: Proposed Concept Drawing for TNC

## Slide 10: System Deployment
In order to deploy unit on bottom, the cable must keep free from propellers, not drag on bottom, and must facilitate an acceptable watch circle for a non-DP vessel.
For MBARI vessels and other identified ships this leads to a number of regulated safety factors that will inform the specification of the tether, and therefore the powered winch.

## Slide 11: Considerations for Seagoing Installations
Max system weight: 500 lbs
Allowing for dynamic loading a tether must have an SWL of 1000 lbf, and via CFR189 the NBL of the tether must be 7000 lbf.
The tether must be the weakest link.
The winch must have a brake rated above 7000 lbf.
A 3 HP winch system will facilitate 30 m/min haul rates for this system, and will integrate with ships of opportunity.

## Slide 12
Operational Components
BOS
Winch
Tether
Handling
Sheaves
Overboard
Frames
Slip Ring
Terminations
Subsea
Tether Management
Floats
Depressor
Weights
Payout Counter

## Slide 13: Solution Pathways
A trade study was conducted with regards to two potential system architectures that satisfy TNC requirements.
Option 1: Custom tether/winch to suit current needs and allow for system scalability to other applications
Option 2: Use widely available CTD wire which meets telemetry requirements and will result in lower cost system with lower maintenance impacts.
The study was not conclusive that either scenario was superior.

## Slide 14: Soft Jacket Fiber Tether Solution
TETHER | Custom Design will meet requirements.
ELECTRICAL | No batteries, independent GFI conductors
MECHANICAL | Can size SWL & NBL
DATA IMPACT | Topside data collection would be possible in future developments.
OPERATIONAL | Will require custom winch, larger sheaves. More care need be taken.
MAINTENANCE | Needs fiber kits and training. More downtime for damaged terms & tethers
COST | Estimated Costs 80k$, for winch, slip ring, and tether

## Slide 15: Standard CTD Cable Solution
TETHER | UNOLS Standard 0.322"ø (Coax ¦ 4C)
ELECTRICAL IMPACT | Batteries required to get to power lamps
MECHANICAL | Already supported on many ships (WF, RC, JM, SR)
DATA IMPACT | Real-Time data collection at the surface lost. Network data only.
OPERATIONAL | May Avoid depressor weight, but floats remain. More Flexible sheave options.
MAINTENANCE | Field servicable, inexpensive terminations
COST | Lower cost (~$30,000), less gear on accommodating ships

## Slide 16: Camera Selection
[Francois’s slides]
Criteria
  Video/image quality (sensor size, sensitivity)
  FOV large enough for covered area (swappable lenses)
  Form factor / size
  Ability to have wired interface camera (remote trigger)
  Local storage (sd card)

## Slide 17: Lander: Mechanical Options
[Francois’s slides]
Horizontal vs vertical camera mounting
Preliminary testing & mock up
Multiple camera housings vs one housing
  Four quadrants with 2 cameras + 1 light each
Configurable (swappable) base

## Slide 18: Electrical Concept Functional Diagram

## Slide 19: Estimated Power Budget
Hotel Load: 100W
Lights (Switchable): 250W
Cameras (Switchable): 50W
Total: 400W

## Slide 20: Tether Selection
Fiber Optic
Single mode fibers
  BW: 10Gbps+
  Dist: >10km
Pair of OE converters
Optical path on slip ring
Future HD recording topside
14-16AWG for power
22AWG for ground fault det
Coax or Twisted Pairs
GigE Ethernet
  BW: 100Mbps
  Dist: 100m
Pair of ADSL Ethernet extenders
  BW: 168Mbps
  Dist: 1km
Cheaper, smaller slip ring
Limits HD recording to subsea
14-16AWG for power
22AWG for ground fault det

## Slide 21: Electrical Power Options
DC Volts
Must generate topside
Higher Vdc means lower i2r losses
Ground fault detection already designed & built
Conversion to low volts DC required subsea
AC Volts
Readily available on ships
Requires isolation transformer
Conversion to low volts DC required subsea
Less heat generated
Tethered only

## Slide 22: Controller (CPU) Selection
Features
Data storage
Relay control
Serial ports
GPIO
Analog inputs
Design considerations
COTS or custom
  Tech transfer
Form factor
Ease of programming
  Firmware development
  Instrument drivers
Ease of use for end users
Daughter boards required?
Power consumption

## Slide 23: Controller (CPU) Options
Oasis5
Arduino
Raspberry Pi
Programmable
Logic Controller
(PLC) Stack

## Slide 24: Topside Electronics Design
Functions
Electrical power generation
Ground fault detection
Method for system control
Real time telemetry & video display
Method for transferring HD videos post deployment
Design Considerations
Must be portable
Safety features
Prefer to not open housing to retrieve HD videos

## Slide 25: Proposed Design
Tether: Fiber
Power: DC
Housing: Single housing (with cameras)
Base: Detachable
Controller: PLC
Software: Aggsoft wedge

## Slide 26: Tentative TNC Schedule

## Slide 27: Next Steps
Identify high risk & long lead time items
Evaluate feedback from this review
Finalize TNC system design
Schedule critical design review (or alternate)

## Slide 29: Standard CTD Cable Solution
CATEGORY | KEY SPECs | IMPACT
TETHER | UNOLS Standard 0.322"ø (Coax ¦ 4C) | 
ELECTRICAL IMPACT | 19AWG Conductors 1000V rated | Batteries required to get to 600W
MECHANICAL | 10 klbf NBL, 5 klbf SWL | Already support on many ships (WF, RC, JM, SR)
DATA IMPACT | 45 Mbps limits via VDSL | Real-Time data collection at the surface lost. Network data only.
OPERATIONAL | 6” Min Bend Radius | May Avoid depressor weight, but floats remain
MAINTENANCE | Can use standard terms and splice whips | Field Servicable, inexpensive terminations
COST | ~ $30,000 (Tether/Winch/SlipRing/Xverters | Lower cost, less gear on accommodating ships

## Slide 30: Soft Jacket Fiber Tether Solution
CATEGORY | KEY SPECs | IMPACT
TETHER | Custom Cable w SMF, GFI and 600W 400V Conductors | Custom Design will meet all requirements.
ELECTRICAL IMPACT | 19AWG Conductors 1000V rated | No batteries, will add GFI safety
MECHANICAL | 7 klbf NBL, 1 klbf SWL | Lower NBL will accommodate smaller ships than steel.
DATA IMPACT | Fiber facilitates 10 Gbps and CWDM for expansion | Topside data collection would be possible.
OPERATIONAL | 10” Min Bend Radius | Will require custom winch, larger sheaves. More care need be take.
MAINTENANCE |  | Needs fiber kits and training. More downtime for damaged terms & tethers
COST | ~$80,000 for winch, slip ring, and tether | Much higher cost and upkeep