## Slide 1
Notes: …
I have just ~10 slides on software
should be pretty quick
Will start by looking at where software may be needed in BOS system…

## Slide 2
Notes: Here: another version of BOS block diagram, this one showing required software components in dark blue.
Everything below the blue line is underwater, everything above on the surface…prob a boat
Starting at the bottom - of course: cameras, lights, with some control system for switching power, start/stop recording,etc
Contextual sensors: TD, along w/ heading sensor and steering cam to facilitate positioning
There is a control interface at the surface that reflects those control operations on the platform.
Steering video needs to be available during operations, and sensor data along w. control events need to be archived.
There is a need to be able to look at data and video telemetry in real time, as well as review it, in a post processing context.

## Slide 3
Notes: Those blue boxes make up four core requirements for software
For which I’ve fashioned the CART acronym (as if need another one)
I’d point out here that data timestamping is an important archiving requirement
We need to be able to know when control events occur (lights, camera start/stop)
And align that other contextual sensors and video data
Otherwise I think we’ve covered these, but I’ll refer to the CART requirements as we go along.

## Slide 4
Notes: In addition to the functional requirements, there are some nice to have options
That we should keep in mind – at least not design out
Computation
Configuration (…also maybe network)

## Slide 5
Notes: There are a few guiding principles to keep in mind as we narrow down concepts for software and system
Given that schedule and resources are tight, trying not to take on too much SW development would reduce some schedule and technical risk
As software tasks can be hard to estimate
For any software development we might choose to take on,
We should make it as easy as possible to use and extend software, with an eye toward the day-to-day operators of the system like TNC and transfer partners like MARE,
We can help by reducing custom code, choosing well supported languages and tools, and keeping parts to a minimum.
We also want to be sure to leave room future expansion, and do what we can to overlap with requirements of potential MBARI users

## Slide 6
Notes: In chad’s earlier slides, we looked at some of the hardware being considered for BOS [PLC, OASIS, COTS embedded]
I’ll cast those here as as key parts of a platform:
by which I mean a combination of hw and sw that together satisfy our functional (ie. CART) requirements
Of course HW and SW are somewhat symbiotic
Here I just want to draw attention to some of the ways that hardware selection can affect
Software development, and thereby the project as a whole
I won’t cover the whole list, but which hardware we choose has a big impact
Locks down choices that determine
how much software we develop, how long it will take, and how much that will cost
And especially as something we intend to transfer, it‘s critical to keep an eye on what
Expertise requirements will be shouldered by operators and developers down the road.

## Slide 7
Notes: Lots of ways to satisfy functional requirements
Can build system with no software development – may not be best performance across the board, but could be done
The decisions focus on what requirements to address with hw and which with sw
Also, what to build (usually for performance reasons) or buy (to help with schedule, performance and risk)
What platform – combo of hw, sw – is best…and what does best mean?
On the left: some of the many technologies we could use to cover CART
Short list highlighted in orange
On the right: some criteria for judging what’s best – no surprises there
The takeaway is that here are some things we considered, and how we downselected
I think most of these are familiar – OK w PLC? LabView?
COTS relays: industrial control boards functionally like PLC w/ different specs and different software interfaces
Before moving on, I’ll briefly describe OASIS and Flux
  OASIS: custom mbari hw/sw,
  instrument controller/data logger, isolated applications like moorings and respirometry
  Covers much of control and archiving functions
  Robust, low power
  25+ yr history, 5th generation
  Flux: a similar body of software that runs on commodity HW (desktop or embedded)
  Very much like OASIS in its ability to archive data, but has some additional telemetry and review features, and is architected for connectivity
The other technology that you may not recognize is what I’m calling a software wedge…

## Slide 9
Notes: What I’ve done here is to use the short list to make 5 platforms that at least cover CART requirements
In each platform box: HW on top, SW underneath
Here, a comparison of relative advantage (bigger in cost/time means better in that category…not higher cost, e.g.)
For me, the top pick is to combine a PC with PLCs for control,
and use Wedge software to do archiving, review, telem
PLCs are simple to configure and use, widely available and low cost
They address the control requirements with almost no software development (more configuration than coding)
A PLC touchscreen simplifies control interface, implementing distributed control interfaces w/ some configuration, but little/no code
The wedge is very inexpensive, and fills the Archive and Telemetry requirements out of the box – once again, zero coding required
There is no custom HW or SW development, and there are a number of vendors offering PLCs and wedge software, so it is somewhat modular
As you can see, that platform doesn’t rate well in the roadmap category:
mostly, this is due to power, knowing that the MBARI Pis are interested in long duration, stand-alone operations.
The take-home is that the PC/PLC/Wedge platform is best for TNC
And that OASIS and Flux (and possibly others from our list) should be looked at as options that could make sense we develop a roadmap for future MBARI applications.

## Slide 10
Notes: So, to summarize, here is a reprise of the first block diagram, with the specific software concept I’d propose using for TNC implementation of BOS
Again, the blue boxes are software
PLC and touch screen covering Control
PC and Wedge cover archiving, telemetry and (to some extent) review
Video uploads are to be done manually and stored on this or another PC
Video telemetry and review would be done using third-party applications that run on the PC
While it’s not super exciting as a software project, it’s a cost-effective solution that will reduce near term risk, meet requirements and transfer well