## Slide 1: Predictive Fault-Detection: Concept Review
04 April 2018

## Slide 2: Team Composition / Roles
CORE TEAM
Matt systems, algorithms
Eric firmware/software
Mark hardware
Lab Engineer* software, integration, testing
ADDITIONAL PEOPLE
Tom O’Reilly software assist
Jon, Mike Parker, Brian Kieft point help
* interviewing

## Slide 3: Foundation

## Slide 4
Vehicle | Endurance | MTBF | Source
Autosub (1996-2000) | 45h | 10h | Griffiths 2003
Autosub LR | 4,400h | 20h | Brito 2015
Webb Gliders (2010-12) | 6 months | 1 month | Brito 2014
LRAUV (2012-16) | 21 days | 35h | MBARI
Commercial aircraft | 10 h | 10,000h | Patton 1991
HOW DID THEY GET TO 10,000h?

## Slide 5
TOOLS
Predictive maintenance
Fault tolerance
  triple/quad sensor redundancy, incl. dynamic redundancy
  redundant actuators
  redundant computers
Predictive health monitoring (awareness)
  FDI/P,R framework
  time-to-failure prediction
IS IT POSSIBLE TO ACHIEVE RELIABILITY IN A SMALL MARKET WITH LIMITED FUNDING?
  FDI/P,R
  Fault = non-nominal operation
  Detect a fault “something’s weird”
  Isolate the fault “it’s a mass-shifter overload fault”
  Predict the time-to-failure “it will overload in 8 seconds”
  Recovery “pull the actuator back and disable it”

## Slide 6
Lessons from aerospace/automotive:
  reliable systems have redundancies
    adding sensors and actuators actually decreases operating costs
    weight penalty is ~ 10%
  majority of hardware failures are due to sensors
  majority of in-mission failures are algorithmic
  prediction + analytic redundancy are ways of reducing cost
    prediction allows mitigation prior to failure
    analytic redundancy allows redundancy without additional h/w
  realistic failure testing is essential
  presence of health management comes from upstairs
    the engineers themselves never want it – e.g. Cadillac SRX
    needs to be integrated into the design process from the get go
POSSIBLY!

## Slide 7: 2017: Fault characterization of a critical actuator*
#1. overload
#3. bad sensor
#2. loose lead-screw
nominal operation
*mass-shifter

## Slide 8: Fault Detection and Fault Isolation?
NOMINAL
OVERLOAD
SENSOR
LEAD SCREW
nominal performance
YES: NOMINAL AND FAULTS ARE WELL-SEPARATED
nominal +faults
Notes: All the data. Nice separation, except for the tails.

## Slide 9: Time-to-Failure Prediction?
contact
overload
shutdown
YES: WE HAVE A 10S HORIZON
current vs time
speed vs time
Notes: Current grows, velocity decreases
10s to catch the fault before it overloads.

## Slide 10
2018 GOALS
Situational awareness
  achieve online FDI/P of a critical actuator
  achieve online FDI of a sensor
  design-in the fault-injection system
Fault-tolerance
  implement sensor redundancy
  implement analytical redundancy

## Slide 11
THRUSTER
MASS-SHIFTER
SEABED COLLISION
SHIP COLLISION
SURFACING
CANDIDATE SYSTEMS FOR FDI/P
RUDDER/ELEVATOR
BATTERY
DVL INTEGRITY
ATTITUDE CONTROLLERS
GUIDANCE INTEGRITY
NAVIGATION INTEGRITY
COMMUNICATION INTEGRITY
SONAR INTEGRITY
PROCESSOR INTEGRITY
starting point
GROUND FAULT
ESP PLUNGER?

## Slide 12: Requirements

## Slide 13: Capabilities
Prototype
  not a production system: the goal is to make our mistakes quickly and cheaply, not deployment on a production vehicle.
Focus on one actuator only
  mass-shifter: well-characterized, well-separated faults, long prediction horizon
Limit the faults
  limit-tab overload, loose screw, bad absolute position sensor
Design for algorithm development (not the other way around)
  implemented in Python
  deployed on a powerful computer that runs an actual OS
Stand-alone hardware with minimal dependencies on the host
FDI/P framework
  Fault = non-nominal operation
  Detect a fault “something’s weird”
  Isolate the fault “it’s a mass-shifter overload fault”
  Predict the time-to-failure “it will overload in 8 seconds”
Make fault-injection a part of the design
  i.e. capability to put the system in and out of fault, under operating conditions, on purpose
  reversibly, repeatably, controllably

## Slide 14: Requirements
System
SYS01. The system will consist of 1) a predictive fault-detection subsystem, 2) a fault-injection subsystem, and 3) a fault-injection mission scripting tool, and 4) a post-mission analysis tool.
SYS02. The system will meet the data requirements described in the appendix “Data Requirements”.
SYS03. The system will be implemented on stand-alone hardware, with minimal dependencies on the host.
SYS04. The software will be implemented in Python.
SYS05. The system will be capable of native compilation.
SYS06. The fault-detection and fault-injection processor will be selected to support 1) computationally-intensive floating-point algorithms, 2) at least a 5X scaling-up of the computational load.
SYS07. The system will support at least 1MBps file transfer, without having to open the host.
SYS08. The system will be capable of logging time-stamped data from its data sources and from its algorithms.
SYS09. The system will fit inside the host’s housing, and will run off power provided by the host.
SYS10. The system will be testable on the bench, in the tank, and at sea.

## Slide 15: Requirements – cont’d
Fault Detection
FD01. The fault-detection subsystem will detect the following mass-shifter faults:
  Limit-tab current overload
  Loose lead-screw
  Position sensor failure
FD02. The fault-detection subsystem will estimate the remaining time to failure.
FD03. Optionally, the fault-detection subsystem will also detect the following thruster faults:
  Current overload
  Magnetic coupler failure
  Propeller loss
and estimate the remaining time to failure.

## Slide 16: Requirements – cont’d
Fault Injection
FI01. The fault-injection subsystem will be capable of injecting the mass-shifter faults enumerated in FD01:
FI02. The fault-injection subsystem will be capable of injecting faults during a mission.
FI03. The fault-injection subsystem will be capable of injecting faults reversibly, repeatably, and controllably.
  reversibly: can return to nominal.
  repeatably: can do it multiple times during a mission.
  controllably: has hooks to control the fault parameters: rate of fault application, fault magnitude, etc.
FI04. The fault-injection subsystem will be capable of coordinating fault injection and actuator motion.
  i.e. if we inject a mass-shifter failure, we ought to make sure the mass-shifter is commanded to move.
FI05. Optionally, the fault-injection subsystem will be capable of injecting the thruster faults enumerated in FD03
  Current overload
  Magnetic coupler failure
  Propeller loss
and do so in accordance with FI02, FI03, and FI04.

## Slide 17: Appendix: Data Requirements
data | range | repeatibility | sampling rate
motor current | typical = +/- 50mA full range = +/- 500mA | 1 mA | 10Hz
absolute tray position | +/- 50mm | 0.1mm | 10Hz
tray speed | +/- 1mm/s | 0.05 mm/s | 10Hz
tray pitch | +/- 30 degrees | 0.5 degrees | 10Hz
motor voltage | +/- 24V | 0.1V | 10Hz
SENSOR RANGE, REPEATIBILITY, AND SAMPLING RATE
CONTEXT DATA
data
goto X command
homing command
current position

## Slide 18: Hardware Design

## Slide 19: Mass Shifter Drive Voltage and Current

## Slide 20: Mass Shifter Position from Linear Sensor

## Slide 21: Mass Shifter Speed from Linear Sensor vs. Encoder Pulses
Similar to lab measurement RMS noise floor

## Slide 22: Thruster Motor Drive Voltage and Current

## Slide 23: Phase 1: Current and Planned Lab Test Bed Design

## Slide 24: Phase2: Prototype Proposed Hardware Design in Lab

## Slide 25
Phase 3: Proposed Final System Hardware Design

## Slide 26: Hardware Design Notes
Measuring Mass Shifter speed to 0.05 mm/sec. @ 10 Hz requires very high resolution position measurement - use encoder pulses!
Analog inputs need at least 11 effective number of bits (ENOB)*.
Embedded processor must support software toolchain, application processing load and hardware I/O requirements.
Full capability lab test system allows software development to proceed in parallel with hardware development.
* Converted signal resolution when all noise sources and quantization errors are taken into account.

## Slide 27: Software Design

## Slide 28: S/W architecture: Phase 1 & 2

## Slide 29: Software Architecture: Phase 3
Adopt / Create a more formal framework.
Create a support layer of device drivers for move away from NI-cDAQ (C/C++).
Assess performance penalties of the Python implementation, create optimizations where necessary.
Implement bi-directional communication with the LRAUV application.

## Slide 30: Data Acquisition
Sensor Data: Linux drivers
  C drivers with Python interface
Context Data: packet sniffing
  packet sniffing in and out of the servo controller
  LCB  servo: commanded position, homing command
  servo  LCB: motor position
Debug data: LCM
  e.g.: vehicle time, depth, heading, LCB voltage/current, encoder position
  LCM broadcast has been tested elsewhere – Tom/Brian K.
  Individual writers will have inherent time bases - 2.5Hz for many

## Slide 31: Fault Injection
Goal: controlled injection from within the application.
  e.g. overload = manually editing the configuration file & commanding motion into the limit tab
  e.g. loose screw = DO control of the clutch (ez-servo).
  Measurements:
    false-alarm rate
    missed detection probability
    misclassification errors

## Slide 32: Algorithm Design

## Slide 33: V1: baseline implementation of the FDI/P chain
Idea
  represent each of 4 states as 2D gaussians
    states = nominal, overload fault, screw fault, bad sensor
    get gaussian parameters from the 2017 data
  pick the nearest one
    technically, the one with the smallest Mahalanobis distance
  discard transients
Feature extraction
  current: mean over 100ms
  pitch detrending: linear in pitch
  position: mean over 100ms
  speed: finite differencing of mean position
  voltage: mean over 100ms
Transient rejection
  state machine = idle, accelerating, steady-state, decelerating
  only run detection during steady state
  idle  accelerating: on new command
  accelerating  steady-state: wait 1mm
  steady-state  decelerating: 1mm before target
  decelerating  idle:
Detection: nominal if distance < threshold
  pick the threshold that maximize a score giving equal weight to detection and false alarms
Isolation:
  compute the distance to each fault
  pick the nearest one
  overload: mean = best quadratic fit vs distance; sigma = cst
Time-to-Failure Prediction
  overload: extrapolate the current linearly to the overload value (3500mA)
  screw and bad sensor faults: set TTF = 0 because they’re already failed.
score =

## Slide 34: Algorithmic roadmap
V2: Physics-based overload degradation model - end of April
V3: Bayesian D-matrix fault isolation - tbd
  migrate to motor current/ relative speed model
  analytic redundancy
V4: model-based w/state residual - tbd
  false-alarms
  robustness to operating condition
V5: model-based w/parameter residual - tbd
  better/worse than state residual?
V6: deployed system - tbd

## Slide 35: Fault-Injection

## Slide 36: Limit-tab current overload
Concept | Pros | Cons
1. Adjustable limit tab | control | most complex load passed onto motor
2. Retractable limit tab | simple load passed to tab | attachment location?
3. Retractable, secured to tab | simple load passed to tab | 
4. change the max position in the config file. | no hardware | sw override or not?
5. Move the tab manually | no hardware | no reversible while underway
Fault description: wheel pushes into the mechanical stop until the electronics shuts-down due to a current overload.
Issue: software override.

## Slide 37: Loose lead-screw
Concept | Pros | Cons
1. Clutch replaces torque coupler | easy to mount easy to re-attach battery is not loose | lose the torque coupler battery is not loose
2. Clutch replaces flange | easy to mount, correct location easy to re-attach battery is not loose | battery is not loose
3. Solenoid-mounted pin | actual failure, lab or at-sea | the battery will be loose hard to re-attach.
4. Manual & easier to align/insert | easy, actual failure | only in lab hard to re-attach
Fault description: loss of coupling between the lead-screw and the mass.
Issues: reversibility, repeatability, controllability.

## Slide 38: Position sensor bias
Concept | Pros | Cons
1. Continuous extender | control | complex
2. Binary extender | simple | limited bias values
3. Manual / slots | simplest | only in lab
4. Voltage injection | simple lab and at-sea | 
Fault description: string-pot attachment point moves.
Issues: reversibility, repeatability, controllability.

## Slide 39: Risk Management

## Slide 40: Risk Elements
risk element | point person | approach
collect the signals with the required accuracy and rate | Mark | analyze high-sampling rate data for required noise rejection derive reqs for speed sensing from position
reversible/repeatable/controllable fault-injection | MK | - hold a brainstorming session - rank candidate solutions
overload fault recovery | Eric | meet with LRAUV s/w people to assess the exact sequence of events after an overload identify options for shortening the recovery time
getting context data (pitch, commanded position, encoder position) | Eric | identify possible sources, e.g. LCM, separate sensor, data sniffing, and their properties , e.g. rate, packet format. identify pros/cons of each.
GSAP appropriatness: compatibility with Python, and implementation overhead. | MK | bring testbed back acquire NI DAQ data with python build proof-of-concept fault detection/isolation/prognostication in python

## Slide 41: Denoising Requirement
energy below f
spectrum vs frequency
50,000 samples/s
1,600 samples/s
90% of the energy is noise
at least 20dB of anti-aliasing filtering is needed to get the SNR above 10dB

## Slide 42: Speed Measurement
sensor type | example | measurement principle | source of noise | rms speed error | typical sensor error | typical speed error at 10 S/s
analog | string potentiometer | V = (X2-X1)/DT | uncorrelated gaussian noise |  | 3 micron (when averaged over 160 samples) | 0.05mm/s
digital | optical encoder | V=(X2-X1)/DT | x-quantization |  | 5 micron | 0.015mm/s
counter | A-phase from encoder | V=C*nb pulses/(n*T_tb) | timebase + pulse jitter | *V | 10ns | 0.000 000 03 mm/s 0.00037 mm/s
sensor type | example | measurement principle | source of noise | rms speed error | typical sensor error | typical speed error at 10 S/s
analog | string potentiometer | V = (X2-X1)/DT | uncorrelated gaussian noise |  | 3 micron (when averaged over 160 samples) | 0.05mm/s
digital | optical encoder | V=(X2-X1)/DT | x-quantization |  | 5 micron | 0.015mm/s
counter | A-phase from encoder | V=C*nb pulses/(n*T_tb) | timebase + pulse jitter |  | 10ns | 0.000 000 03 mm/s 0.00037 mm/s
Requirement: 0.05mm/s at 10 S/s
we will use a counter

## Slide 43: GSAP/Python
Generic Software Architecture for Prognostication
GSAP is a no-go for now
  designed for prognostication  our focus is detection/ isolation
  has no Python bindings
  is model-based  we’re data-driven
  is too onerous for a prototype  keep option open for long-term

## Slide 44: Risk-reduction s/w prototype
Goal: Prove that we can stream NI DAQ data to a Python script + run fault detection/isolation on the spot:
  using DAQmx  Python interface
  input: current, voltage, position, speed
  FDI algorithm # 1
Status
  I,V,X acquisition done and validated
  in process of adding FDI algorithm
  in process of adding speed (NI 9361 counter)

## Slide 45: Overload Fault Recovery
When externally creating faults, the LRAUV Application must:
  Respond predictably to this fault
  Not disable the unit
  Recover without user intervention
  Report status appropriately
Current LRAUV fault handling:
  Overcurrent faults are resolved by unpowering the ez-servo from the LCB.
  The ez-servo goes through its startup, and is re-homed (5-20 seconds)
  This is allowed <X> times before the servo is considered in failure, which triggers the “default” mission.
  That <X> can be changed in configuration.
We can script missions that directly command the mass shifter to move. Both in water and the lab.†
Configurations will be modified to allow for many faults.
No core code changes will be required.
†unsure if that instruction allows for command past stops

## Slide 46: Next steps

## Slide 47: Next step: prototype design
2 parallel tracks
  track 1: algorithm development using NI-DAQ
  track 2: hardware development
  merger
Fault-Injection prototype
Review

## Slide 48: Backups

## Slide 49: 2017 FAULT DETECTION
THRUSTER VOLTAGE AND CURRENT
MASS SHIFTER POSITION, VOLTAGE AND CURRENT
HOST PROCESSOR RUNNING FAULT DETECTION AND ISOLATION MATRIX ALGORITHIMS

## Slide 50: Sampling of linear position sensors