## Slide 1: Proposed Hardware/Software Development Plan

## Slide 2
LRAUV System
National Instruments NI9229 Interface
Easiest software development and test platform
Step 1
LRAUV System
COTS CPU Candidates and interface hardware
Step 2
COTS CPU Candidates and interface hardware
Software development and testing can start immediately independent of hardware development.
Hardware requirements for sampling rates etc. can be determined.
Software is run on candidate CPU’s to validate hardware processing requirements, etc.
Multiple approaches can be prototyped and tested.

## Slide 3
LRAUV System
Optimized embedded hardware
Step 3

## Slide 4: Data Acquisition Approach
Motor Voltage and current captured with analog data acquisition subsystem.
  Anti-aliasing filter.
  Signal conditioning amplifier.
  Sigma Delta or Dual Slope A/D converter.
Position of Mass Shifter measured with absolute position encoder.
  Optical tape – high accuracy low noise.
  String pot, have to look at resolution and noise issues.

## Slide 5: System Development Approach 1
Collect motor data from test bed (or analyze existing data) using National Instruments NI9229.
Use to determine:
  Effective number of bits (ENOB) required.
  Level of input filtering required.
  Channel to channel isolation required?

## Slide 6: System Development Approach 2
Use data acquisition reference design COTS hardware to verify system design.
  SPI bus interface?
  Interface to target embedded computer?