## Slide 1: Dorado Bioacoustics Concept
901807 Next Gen Bioacoustics on Dorado MBARI 2018

## Slide 2: Statement of Problem
Integrate acoustics and imaging
  Provide acoustic backscatter measurements from known targets
  Observe animal responses to the platform (avoidance and attraction) up to 100 m away
  Observe spatial relationships of animals at multiple scales
  New measurements from the integrated system
    Animal size
    Independent measures of density over different volumes

## Slide 3: 2018 Goals
Integrate echosounder system into i2Map
Field trials
  Stable flight
  No interference with imaging
  Data quality suitable for acoustic sensing to at least 100 m using a -75 dB threshold
  Test effects of DVL in order to maximize ping rate

## Slide 4: Simrad EK80 Mini-WBT
Compact version of the EK80 Wide Band Transceiver (WBT)
12-16 VDC input, Max 6W
Notes: Autonomous mode will NEVER be used. We could simplify this considerably

## Slide 5: Transducers
ES200-7CDK Split
  Nominal Frequency: 200-kHz
  Frequency Range: 185 to 255 kHz
  Beamwidth: 7˚
  Split Beam
ES333-7CDK Single
  Nominal Frequency: 333-kHz
  Frequency Range: 270 to 445 kHz
  Beamwidth: 7˚
  Single Beam
Notes: Broadband capable for spectral response of targets, effective range ~100 m or more allows observation of behavioral responses of animals to vehicle, small and available. Electronics support changing these transducers at a later date.

## Slide 6: Previous Integration
Communications schematic

## Slide 7: Previous Integration
Electrical schematic

## Slide 8: Functional Requirements
All components must be contained within the I2Map Payload area.
The system must facilitate deck configuration and remote start/stop operation.
Time, depth, and position data from the vehicle must be incorporated in the recorded data.
The system must survive the depth rating of the overall payload.
Transducers cannot impact the video data.
The forward-oriented transducers’ field of view must overlap with the field of view of the camera from within the focal range of the camera.
I2Map must remain deployable without the acoustic payload and during development
Collect data often enough to track moving targets.
Cannot impact existing surveys in duration or depth capability.
Conduct continuous data collection.
Cannot impact other acoustic systems, and vice-versa.
Data must be available post-dive.
Data download must occur in time less than a recharge of the vehicle’s batteries.
System needs to deployed without the AUV for tank testing purposes
There must be a dedicated Windows-based processor to operate the software.

## Slide 9: Derived Requirements
System:
Depth rated to 1500-m
No obstruction for transducers to 7 degrees
No video obstruction
Transducers mounting must easily be installed/removed.
Neutrally buoyant
Vehicle shall remain in stable flight at existing I2MAP normal through-water speeds (2 knots).
Ping each pair of transducers at ±1 Hz (total 2 Hz) to allow tracking of moving targets
Data quality suitable for acoustic sensing to at least 100 m using a -75 dB threshold
Interface:
Self-powered (12-17VDC) and auv-host connection (18-36VDC), existing electronics require a clean 12-17VDC input.
Isolated Trigger Input
GPS/Depth/MRU serial data to sonar software
Configuration interface (ethernet/remote desktop)
CPU must accommodate simrad and echoview software
Accommodate data storage at rate 25-GB/hr.
Disciplined time input (ntp or 1-PPS)
Download interface must facilitate a maximum 5-hour download time.
Minimum 6 hour run time.
Must respect normal AUV health monitoring standards.

## Slide 10: System Concept

## Slide 11: Forward Mounting Transducers
Transducers are embedded in the
delrin camera shield:
Low drag
Somewhat out of harm’s way
Close to camera
No cables outside of fairing
No interference with light beams.

## Slide 12
The transducers are mounted on a 3/16” aluminum plate.
The plate is screwed to the plastic ring from the front using two ¼-20 screws.
The cables are easily routed to the back of the AUV.
View without the transducers.

## Slide 13: Placement of Downward Transducers in AUV

## Slide 14: Downward facing transducer bracket
Gauge 14 stainless steel bracket
Gets screwed to bottom fairing
Transducers can we accessed without removing the camera

## Slide 15: Buoyancy
Sphere:
33lb positive
Transducers and hardware:
6lb Negative
Lead:
27lb Negative

## Slide 16: Comparison of camera field of view and transducer beams

## Slide 17: Electronics Packaging: The Sphere Solution
Concept
Since electrical noise has affected data quality in previous integrations, let’s choose a solution that provides initial flexibility and reduces design time and risk.
Replace a 5-kWhr sphere with a similar 17” sphere with Simrad and support electronics in its place.
Capable because of short i2Map mission duration limitation (recording 5 hours)
Enough room for key components, and space for a dedicated battery pack to run the acoustics and processor
Extra room allows for better EMI rejection
Removes need for new section
Current wet-connector count dictates a large housing regardless.
This solution will likely reduce need for much flotation.

## Slide 18: Notional Wiring Concept

## Slide 19
From Below, Connector View

## Slide 20: Custom Electronics: Battery Controller
Current Battery: PH2054HD34
Features:
Incorporate the LPC1769 using Micromint SOM and firmware from dorado for SMBus Driver
Leverage existing circuits from 41-Cell pcb
Leverage existing filter circuit from the glider
Trigger/Signal isolation
Fusing
Health Monitoring (humidity, pressure, leak)
Potential Voltage regulation for SBC, MiniWBT

## Slide 21: Preliminary Power Budget

## Slide 22: Software Architecture (Windows SBC)
Time
NTP to MVC
Presence
MVC AHRS (VIRTUAL COM)
MVC GPS
(VIRTUAL COM)
Trigger
MVC ISO (TTL)
MVC DEPTH (VIRTUAL COM)
REAL-TIME PROCESSING W/ ECHOVIEW
Acquisition
EK80 SOFTWARE
REMOTE DESKTOP
FUTURE DEV
TARGETED VIDEO SAMPLING
FEATURE TRACKING

## Slide 23: Preliminary Cost Estimates
Padding in budget from likely unnecessary foam and fairing line items.
Missing estimates for some mounting parts and sphere parts.

## Slide 24: Risk Elements
The Simrad MiniWBT has notorious noise susceptibility from a broad array of electrical and mechanical sources as seen in previous integrations (glider and Ventana)
  Approach:
    Leverage sphere space for EM enclosures, grounding, & other solutions
    Dedicated battery pack
    Leverage previously designed filters
    Isolated connections
    Design room for mechanical isolation of transducers
Acoustic interference from AUV subsystems, DVL & CTD Pump
  Approach: Characterize potential problem as early as possible.
The transducers are mechanically sensitive devices and must have unimpeded exposure to the environment.
  Approach: Transducers have been brought as close into vehicle as possible, there is room for more protection if necessary.

## Slide 25: Performance Stack-Up
Category | Requirement | Design Concept
Functionality | Preserve current functionality and capabilities. | No obstructions Small change in drag profile Transducers easily removed
Depth Rating | 1500 | 7000
Mission Duration | 6 | 7.5 (for AUV w/ 1 battery and package on its own)
Data Storage | 6*25GB/hr = 150-GB | TBD - Commonly Available
Data Offloading | 5 hour | 20 min at Gig-E
Mounting | 2FWD/2DWN Focal range 50-cm | 2FWD/2DWN 13-cm (Blanking Dist 50-cm)

## Slide 26: Test Plan
April Tank testing:
  Identifying noise sources as soon as possible by running against i2Map section
  Waiting on transducers & software fixes
April/May:
  Purchase COTS components and test against the hardware in May
  Assess final processor requirement.
May/June: PCB Design CDR
July/August: Package assembly and testing
At Sea Testing: 10/26, 10/29, 12/6

## Slide 27: Team
Kelly Benoit-Bird: PI, Simrad POC
Eric Martin: PM, Wiring, Board Design
Bruce Robison: Investigator, I2MAP POC
Kim Reisenbechler: I2MAP POC, collaborator
François Cazenave: Brackets, EMI Enclosures, Chassis Design
Hans Thomas: Sphere Housing, Wiring, Board Design
Paul McGill: Noise Isolation
Chad Waluk: Sonar software, SBC configuration

## Slide 28: Questions

## Slide 29: Additional Slides

## Slide 30: Preliminary Cost Estimates (Detail)
Padding in budget from likely unnecessary foam and fairing line items.

## Slide 31: SBC Requirements
Celeron or better x86/x64
10-16.8V Input range desired
2x Gig-Ethernet & 2 100BT-Ethernet
Serial port or dig IO for trigger
Runs Windows 7 or better (Windows 10 preferred)
HDD SIZE BASED ON REQ