## Slide 1: Deep Sea Coral Observatory Design Review

## Slide 2: Project Goal
Design a time-lapse camera system that can observe changes in a coral community on a time scale of months

## Slide 3: DiSCO Functional Requirements
The DiSCO shall image a fixed area of a chosen coral community. The area should be large enough to be relevant to abundance studies.
The DiSCO shall be capture images of substantial resolution to identify 10 cm organisms.
The DiSCO shall be engineered to operate without maintenance for up to one year.
The DiSCO shall be deployable at sites as deep as Sur Ridge. 4k preferable.

## Slide 4: DiSCO Functional Requirements
The DiSCO shall capture images at the frequency necessary to study changes in community structure. Every hour sufficient.
The DiSCO shall be deployable as a free vehicle.
The DiSCO shall leverage to the extent possible from previously developed technology and COTS solutions.
The DiSCO shall be operated and maintained by non-engineering personnel.
The DisCO shall be deployable from the Western Flyer. Nice to have Rachel Carson.

## Slide 5: Smith Time-Lapse Camera Tripod
1 picture/hour
Images 20m2 of seafloor
Duration: 1 year
Successful in field for many years

## Slide 6: Smith Dual Tripod FOV

## Slide 7
Seafloor area viewed

## Slide 9: DiSCO Challenges
More topography
More visually dynamic targets
More active area- high currents
Must be positioned to area of interest

## Slide 10: DiSCO Development
Reuse as much of the Smith system as possible
Enable real-time image feedback to optimize camera settings
Build frame that is ROV-moveable and optimized for imaging deepsea coral

## Slide 11: DiSCO Block Diagram

## Slide 12: New Components

## Slide 13: Real-time Comms with ROV
Talk Ethernet <-> USB to controller and camera
  Capture and view images
  Adjust camera settings at start of mission
Use tilt motor to adjust camera angle. Tilt motor powered from ROV, only on when ODI plugged in

## Slide 14: ROV Connection
On ROV
On DiSCO
Existing Pair
ODI on Disco will be on long enough leash to reach the front porch and be stowed in a dummy receptacle.

## Slide 15: DiSCO Block Diagram

## Slide 16: New Camera
EOS 5D Mark III now obsolete
EOS 5D Mark IV is same form factor
Bench testing has not yet revealed any significant issues interfacing with our existing electronics.
 | Mark III | Mark IV
Sensor | 22.3 Mpixel Full frame | 30.4 Mpixel Full frame
FOV |  | 

## Slide 17: Energy budget
Energy Use Each Image | 
 | Energy per image (WHr)
Canon EOS 5D MarkIIII | 0.02
Strobes (2) | 0.446
SUM= | 0.466
Hotel power | 
 | Energy per year (WHr)
Snappy Controller | 17
Total Energy per year (WHr) | 
Canon + strobes | 4082.16
Snappy | 17
Sum= | 4099.16
Li pack derated | 4.2 kWHr

## Slide 18: Mechanical Requirements:
Deploy & recover off the Flyer & Carson
2000 meter depth rating (4000 meter would be nice)
ROV able to move and manipulate position
Hold position on seafloor in up to 1 knot of current
Camera approximately 1.5 meters above seafloor
Acoustic release plus backup manual release by ROV
Capability to fine tune position of camera

## Slide 19: Tripod Frame
Make design flexible to adapt to future changes/requirements
Galvanize steel members to reduce cost
Bolt together frame
Frame dimensions a’ x b’ x c’

## Slide 20
Strobe w/swivel mounts
Acoustic
Release
Recovery line float w/x? meters
of lift line attached to lift bail
Tag line bails (X3)
Release weight (300 lbs)
Manual pull
pin release
Battery housing
Floor grating
Deployment/Rec. bail
Chain
Camera
Camera
Tilt unit
Syntactic float
ROV lift strap
ODI receptacle (not shown)

## Slide 21: Air/water weights w/2000 meter foam
In air weight = 1402
Drop weight = 300
In water weight w/drop weight = 111
In water weight wo/drop weight = -149
Note: 4000 meter foam loses 79 lbs of buoyancy and adds 77 lbs to in air weight

## Slide 22: Supplemental Materials

## Slide 24: Glenair Ti Connectors
Pros: cheaper than Seacon Ti connectors
Cons: long lead times

## Slide 25: Tilt Motor

## Slide 26: Snappy

## Slide 28: Strobe