## Slide 1: OPTIM MxD Camera System Camera Chassis Shim Spacing and Optical Centering Alignment
Note: See “notes” view for additional discussion and information on the slides

## Slide 2: Before Beginning Shim Setting Procedure
Have the optical block and front of Canon lens adjustment screws set for mechanically centering the two parts.
Perform the back focus adjustment on the Canon lens! See camera user manual for procedure. Don’t forget this step!

## Slide 3: Optical Alignment Requirements (from 89L REV 3 CORRECTOR TOLERANCES - FINAL - AUG 5, 2020)
Corrector cell to dome
Canon lens to corrector cell

## Slide 4: Camera Alignment Components - Cartoon
Optical Block and Lens Assembly
Camera Chassis
Titanium housing
dome support ring
Optical Adapter Lens Assembly
Dome Port
Rear support clamp fastener and springs to force chassis to forward axial stop
Camera Chassis radial alignment cone
Axial stop

## Slide 5: Canon Lens and Optical Block Reference Points
Optical center
Lens face of front element
Lens flange
Optical block
Note: Canon lens mechanical center of front element is NOT necessarily co-axial with optical center of lens  (..Canon communication)
Also assume lens and optical block are aligned by B4 lens mount – we have no control over this.
Chassis and lens mechanical center
Lens X-Y Adjustment
Optical block X-Y adjustment

## Slide 6: Adapter Optical Cell Reference Points
Optical and mechanical center are aligned
mechanical optical center & tilt reference
mechanical axial distance reference
Calibration plan requires that the optical center of the adapter cell is aligned with the mechanical reference points on the adapter assembly. Adapter cell assembly uses laser interferometry alignment to verify that individual lens centering and tilt specifications are met. (see PDR slide #32)
first glass element
fourth glass element

## Slide 7: Camera Chassis Reference Points - Cartoon
Mechanical center
mechanical center radial reference surface
Lens flange (optical block mount)
Axial spacing of Canon lens to adapter cell shim adjustment
Shims for adapter cell front lens to dome port spacing adjustment
Rear chassis plate to housing ID adjustment tabs
Housing bulkhead bolt circle
Rear camera chassis center support fastener
Adapter cell radial and Z alignment surfaces.
Axial spacing reference surface
chassis alignment cone
Face
Bore

## Slide 8: Chassis Spacing Alignment Components
Optical Adapter Lens Assembly
Canon lens X-Y adjustment screws (3x)
Adapter lens retaining screws (3x)
Optical block X-Y adjustment screws (x3 screws radially spaced)
Springs apply 57 lbs. of force against housing
Chassis alignment cone
Chassis radial alignment tab (x3)
Canon lens to adapter cell spacing shims
Adapter cell to dome port spacing shims
Chassis to housing radial alignment PEEK rings
Not shown, chassis length adjustment spacer

## Slide 9: Housing Reference Points
Optical and mechanical center
mechanical center reference
mechanical axial distance reference
Housing bulkhead bolt circle
Q1: Dome axial position change at pressure? Apparently -0.007 inches [0.18mm]
Note: Dome must be carefully aligned with the support ring reference bore. Split tolerance with adapter alignment?
Housing ID clamps during initial assembly

## Slide 10: Shim Adjustment Jigs & Tools
Chassis cradle doubles as chassis vertical support
100221414-92-A_CameraLensGage
100221414-93-A_AdapterLensGage
100221414-94-A_AdapterGageBlock (inside)

## Slide 11: Step 1: Set Canon lens to optical adapter spacing by adjusting shims between the chassis adapter cone and the chassis.
Step 1A:
Measure distance to vertex of optical adapter cell using alignment cone as a jig. Use lens paper on lens surface.
Adapter cell
Granite Block
Chassis alignment cone (prior to installing on camera chassis)
Large plunge micrometer (borrow from shop)
Granite Block
Step 1B:
Measure distance from alignment cone to granite block. as a jig. Also use same thickness lens paper on granite block.
A
B
Step 1C:
Difference (B-A) is adapter spacing (11.83mm nominal). Enter MEASURED distance in the EXCEL worksheet in ChassisShimsCalibrationProcedure.xlsx

## Slide 12: Illustration of Method of Verifying Adapter Cell Dimension Using Plunge Micrometer and Chassis Alignment Cone
B
A

## Slide 13: Step 2: Set Axial Distance of Canon Lens with Gage and Shims
Install the chassis alignment cone using the nominal shim stack plus any offsets measured on the optical adapter.
  Installation (and re-installation after shim adjustment) is easiest when camera is set vertically with the front facing down.
Note that insulating Kapton shim must be installed on chassis side of shim stack to maintain electrical isolation of chassis from the alignment cone.
The shim stack compresses with clamp force and it takes several laborious iterations of clamping and measuring to get the final shim stack height correctly set.
The is a tool in ChassisShimsCalibrationProcedure.xlsx for estimating the shim mix to make a target stack height.
This step is the hard part and the rest is much easier – at least until the optical alignment!

## Slide 14: Adapter Lens cell to Canon Front Lens Tolerance
CANON LENS FRONT ELEMENT
ADAPTER CELL LENS 4th ELEMENT
0.05MM FLARE GUARD CLEARANCE WITH 0.3MM AIR GAP
Specification: 0.3MM – 0.1 + 0.3mm AIR GAP

## Slide 15: Step 2A: Set Axial Distance of Canon Lens with Gage and Shims
Step 2D: Adjust axial spacing shims in 0.05 mm increments for 0.3mm Canon lens setback
Step 2B:
Zero gage jig mounted dial indicator on granite block (with lens paper)
Exact spacing specification
Canon lens to adapter cell calibration fixture
Granite Block
Step 2C: Dial gage will read offset from nominal spacing distance. Use lens paper for lens protection!
Step 2E: Note final value in worksheet ChassisShimsCalibrationProcedure.xlsx and make a copy for records.

## Slide 16: Step 3: Install optical adapter cell on chassis alignment cone
chassis alignment cone
optical adapter cell
reference surface
Adapter Cell retaining screws (x3)
Canon lens centering screws (x3)

## Slide 17: Optical System Alignment – Laser method
This alignment procedure assumes that the optical elements within adapter cell have been separately verified to be assembled within optical alignment tolerances that define a system optical axis which is concentric with outside diameter of its aluminum shell. It is further assumed that the shell outside diameter, chassis alignment cone internal and PEEK alignment ring diameters, dome mounting internal diameters and dome centration are all within design tolerance.
Alignment Laser and target setup.
  Pointing laser beamed through a 1mm aperture in a diffuse target set 233.4 mm from vertex of front Canon lens element.
  Attenuation filter* that can be placed between the laser and the target.
  A Jig or clamp to securely hold the camera chassis assembly in position.
Step 1: Centering of laser beam on Adapter Cell optical axis.
  Make sure that the Canon lens aperture is COMPLETELY CLOSED or imager damage may occur!
  Point laser and diffuse target at the adapter cell and observe the reflected image from the elements of the adapter cell on the diffuse target.
  Adjust the position of the laser & target until these reflections are exactly centered on the laser 1mm aperture. Tip: this maybe easier if you temporarily place a mask behind the optical adapter cell to block reflections from the Canon lens.
  The laser beam is now aligned on the optical axis of the Adapter Cell.
Step 2: Align the Canon lens/Optical block assembly to the Adapter Cell optical axis.
  Place the attenuator in front of the laser beam and open the Canon lens aperture so that a visible laser spot appears on the video image.
  Set the Canon lens zoom to full wide at f 8 and adjust focus to obtain a clear image of the Laser spot aperture.
  Adjust front of Canon lens laterally (X-Y) with front adjustment screws to center the laser spot in the video image.
  Change Cannon lens setting to full zoom and note image shift of the laser spot from the center of the field.
  Adjust the tilt of the Canon lens/Optical block assembly with the rear screws to re-center the laser spot in the image field.
  Repeat steps 3-5 until the laser dot remains stationary and located at center of image while lens is adjusted from full wide and full zoom settings.
Step 3: Verify Dome Alignment on optical axis.
  After final chassis and housing assembly repeat step 1 above to center on reflections from dome and adapter cell optics. All reflections should line up with the laser beam aperture within 1.mm. (how far can they be off?)
  Repeat step 2 above and verify that when changing the Canon lens setting from full wide to full zoom the laser spot remains near the center of the image field within ± 19 microns.
* Attenuator filter must allow a safe power level be projected toward the imager when the Canon lens aperture is open.
Note on adjusting radial alignment screws. While adjusting the front and back of the optical system, keep the screws barely firm to allow the system to tilt as the opposite end is adjusted. It takes a fine feel to have the screws engaged in the adjustment but not so tight as to cause binding or warping. After all adjustments are complete, apply Loctite to screws one by one and tighten firmly and evenly. Re-check optical alignment when done.
Notes: At full zoom, dome decenter of 0.30 mm yields object deviation from center = 19 microns.
At full zoom, dome tilt of 0.15 degrees yields object deviation from center of image = 18 microns.
At full wide, dome decenter of 0.30 mm or dome tilt of 0.15 degrees produces ~ 1 micron of object deviation from center of image.

## Slide 18: Laser Alignment Setup
Mirror
Mirror
Target
Attenuator

## Slide 19: Step 4: Center alignment laser on Optical Adapter cell by centering reflections from glass surfaces on target.*
Attenuator
~232 mm
1mm aperture in white target
Front lens element vertex of Canon lens
1mW Laser
(633nm HeNe)
* With Canon lens aperture closed!
Centering made easier by temporarily adding a mask behind the optical adapter cell to eliminate reflections from the Canon lens

## Slide 20: Step 5: Center alignment laser on video image using front lens X-Y adjustment.*
* With attenuator in place!
1mW Laser
(633nm HeNe)
Attenuator
1mm aperture in white target
3 fine pitch radial adjustment screws
With Canon lens in full wide position, adjust lens to exactly center laser spot on image (set center cross target on monitor menu)

## Slide 21: Step 6: Tilt alignment laser on video image using rear lens X-Y adjustment.*
* With attenuator in place!
1mW Laser
(633nm HeNe)
Attenuator
1mm aperture in white target
3 fine pitch radial adjustment screws
With Canon lens changing from full wide to full zoom position, adjust rear of lens to minimize lateral movement of the laser spot on image
Continue to adjust lens X-Y position and tilt settings until image is centered in lens wide position and center target remains exactly in position during lens zooming.

## Slide 22: Step 7: Confirm Housing Reference Surface to Dome Distance
DeepSea will measure and provide dimension from chassis reference surface to apex of dome concave surface in final housing checkout documentation.
Enter provided value in the ChassisShimsCalibrationProcedure.xlsx
Nominal dimension: 148.44mm

## Slide 23: Step 8: Measure Exact Adapter Cell to Dome Port Spacing
Measuring offset of adapter cell to dome port spacing from nominal (see ChassisShimsCalibrationProcedure.xlsx)
Note use of glass disk on 1st optical adapter element. This disk is also used on top of adapter gage block when zeroing dial indicator
100221414-94-A_AdapterGageBlock

## Slide 24: Step 9: Install shims to set adapter cell to dome port spacing
Adjust axial dome to adapter spacing shims in 0.05 mm increments for nominal specification + specified bias (see slide # 59 and ChassisShimsCalibrationProcedure.xlsx for bias)
Dome to adapter cell calibration plug
40 lbs. force

## Slide 25: Step 10: Set Rear Clamp Spacing Washer Thickness Based on Total Shim Stack Height.
0.150” Spring Compression limit*
0.050” Spring Extension limit
Heatsink/bulkhead fixed to housing end cap
Shoulder screw/guide determines maximum spring extension (shown in nominal or room temperature assembly position)
Compression springs
Chassis fore/aft active compliance
MRC Dec. 1, 2020
*set by maximum recommended spring compression
Select appropriate spacing washer depending on final adapter to Canon spacing and adapter to dome port shim stack up. 0.130 to 0.250” spacers allows static adjustment for adjusting for different shim configurations.
See ChassisShimsCalibrationProcedure.xlsx

## Slide 26: Step 10: Set Rear Clamp Spacing Washer Thickness Based on Total Shim Stack Height.
Compression springs
MRC Dec. 1, 2020
Select appropriate spacing washer depending on final adapter to Canon spacing and adapter to dome port shim stack up. 0.130 to 0.250” spacers allows static adjustment for adjusting for different shim configurations.
See ChassisShimsCalibrationProcedure.xlsx

## Slide 27: Step 11: Install and Mechanically Center Camera Chassis in Housing and Tighten Radial Alignment Tabs..
Adjust and tighten radial alignment tabs
Radial alignment tabs hold the camera chassis in centering alignment during the initial closure of the housing endcap.

## Slide 28: Step 12: Install Camera Housing Endcap and Tighten Center Support Fastener.
Access to allow tightening the chassis center support fastener is through the endcap center vent port
After chassis center support fastener is tightened, chassis alignment is firmly locked and chassis and housing bulkhead can be removed and re-installed without requiring re-alignment, but mark and keep the same radial alignment of the chassis to the housing.

## Slide 29: Step 13: Optical Verification Testing of Complete Assembly.
Attenuator
1mm aperture in white target
1mW Laser
(633nm HeNe)
Re-locate the optical axis by repeating step #3 with the fully assembled housing. Retro-reflections from dome and adapter optics centered within < 1mm at aperture.

## Slide 30: Step 14: Verify Complete Assembly Decenter and Tilt Alignment
Laser spot should be in the center of the video image
1mW Laser
(633nm HeNe)
Attenuator
1mm aperture in white target
Maximum spot movement through zoom range should be ≤ ± 19 microns
Notes: At full zoom, dome decenter of 0.30 mm yields object deviation from center = 19 microns.
At full zoom, dome tilt of 0.15 degrees yields object deviation from center of image = 18 microns.
At full wide, dome decenter of 0.30 mm or dome tilt of 0.15 degrees produces ~ 1 micron of object deviation from center of image.

## Slide 31: Step 15: In-Water Optical Verification Test of Complete Assembly.
Qualitatively compare in-water test target with in-air reference image for consistent resolution and lateral color, especially at image edges.