## Slide 1: 4K Camera PCB Layout
Ver. 1/4/2021

## Slide 2: 010421_1100_TopSolderMask.pdf

## Slide 3: 010421_1100_TopPlacement.pdf
Modify cutouts! Make closer to stand-off &U28.

## Slide 4: 010421_1100_TopCopper.pdf
Emi com
Vin
Vin
Vin
Vin
Emi com
Make 300mA traces!
Guard ring around R1&C3 should be at output potential (pin2&tab,10V) – not gnd!
U16. Add more stitching for VDD and Gnd (300mA). I added 1uF Cap between VDD & Gnd so new netlist.

## Slide 5: 010421_1100_In4Copper.pdf
Emi com
Emi com
Vicr com
Vicr com
More fill for 5V!
1st stg 5V
1st stg 5V

## Slide 6: 010421_1100_In3Copper.pdf
Emi com
Gnd
3.3Vpwr
Vin
Emi com
12Vpwr
5Vpwr
12Vpwr

## Slide 7: 010421_1100_In2Copper.pdf
Gnd
Emi com
PwrCom
PwrCom
PwrCom
AnaCom
AnaCom
Vin
Emi com
No earth gnd over here. Not necessary. Chassis ties together.
Adjust these traces and make wider PwrCom path.
Very narrow.
camera
Focal&fan
232 port
232 port
H2O alrm
Lens cntrl
Turn JP2 sideways

## Slide 8: 010421_1100_In1Copper.pdf
12Vpwr
12Vpwr
12Vpwr
10Vpwr
10Vpwr
AnaCom
Vicr Pwr
Vicr Pwr

## Slide 9: 010421_1100_BottomSolderMask.pdf

## Slide 10: 010421_1100_BottomPlacement.pdf

## Slide 11: 010421_1100_BottomCopper.pdf
Cam12V
Cam12V
12Vpwr
12Vpwr
Vin
Emi com
Vin
Vin
Make this long trace a little thicker