## Slide 1: MBARI Video Camera Work
MBARI’s first ROV camera project – a DXC3000 in 1987!
First full HDTV ROV camera system.
First high quality large format AUV camera system.

## Slide 2: 4000 Meter ROV Camera Sony HDC-750 camera and Fujinon HA10X5.2 wide angle zoom lens. MBARI camera and lens servo controls. Optical design by Milt Laikin, housing by Insite.

## Slide 3: MBARI i2MAP 4K Autonomous Vehicle Camera Sony PMW-F5 and AJA Ki Pri Quad recorder super 35 Bayer array and Sony SCL-P11X15 wide angle lens. Camera assembly and housing by MBARI. Optical design by Paul Remijan.

## Slide 4: MBARI i2MAP 4K Autonomous Vehicle Camera ~1 meter
Corner resolution
Center resolution

## Slide 5: MBARI i2MAP 4K Autonomous Vehicle Camera (in filtered sea water)

## Slide 6: Tests of Commercially Available ROV 4K Cameras (corner resolution)
Sony FDR-AX100
Sony FCB-ER8550
All commercial cameras tested had very poor lens controls…….
DSP&L
Sulis
Insite
SubC
MBARI i2MAP 4K
Building Blocks

## Slide 7: Major High Level 4K Camera Requirements
Image quality
  Resolution
  Contrast ratio
  Color reproduction
Camera controls
  Zoom, focus and iris
  Black and white balance, shutter speed , etc.
Camera size and weight
Camera cost
Camera ease of maintenance
Full Requirements Doc: \\Atlas\ProjectLibrary\901900_MBARI_Advanced_Imaging_Infrastructure\EngineeringDesignDocuments\4KCameraRequirements

## Slide 8: MBARI requirements for our main ROV cameras
MBARI requires professional quality zoom and focus controls!
Focus Position Slider
Pan & Tilt Control
Zoom Rate Control Rocker Switch
Ikegami RCP
https://www.youtube.com/watch?v=X8oWnbcLI40
(2,794,882 views)
Focus example

## Slide 9: Best Candidate Camera Module
Sony HDC P50
  2/3” 3-Chip CMOS imager
  4096x2160 progressive scanning @ 60 frames/sec.
4K Resolution Lenses – very important!
  Fujinon UA13x4.5 BERA 4K UHD Wide lens with 13x Zoom
  Canon CJ12ex4.3B 4K UHD wide-angle lens with 12x Zoom