## Slide 1: Agenda: 4K ROV Camera Architecture Brainstorming
July 2, 2019

## Slide 2: Invited Attendees?
Dave French
Andy Hamilton
Paul McGill
Brent Roman
Mike Risi
Rich Henthorn

## Slide 3: Goals of the Session
Background on lens controllers
  Performance requirements.
  Architectural constraints.
Brainstorm on lens controller architectures
  Four different architectural possibilities.
    #1 - Build from scratch.
    #2 - Use Fujinon controller for Iris.
    #3 - Use analog inputs to Fujinon Controller.
    #4 - Use digital inputs to Fujinon Controller.
  What option is the easiest to implement?
  How much software development required?

## Slide 4: Requirements
Camera controls
  Zoom : RATE control with smooth start and stop into low speed movement , but fast ramp to high speed. Feedback is either tachometer or encoder, depending on drive motor selection.
  Focus : POSITION control with smooth ramps to commanded position. Feedback is either position pot or encoder depending on drive motor selection.
  Iris: POSITION control with smooth ramps to commanded position. Feedback is either position pot or encoder depending on drive motor selection. Command signal comes though camera/lens interface.
    Option: Use Fujinon lens drive for Iris.
  Black and white balance, shutter speed , etc. Handled through camera system remote control panel (RCP).

## Slide 5: Issues to resolve in system design
Can Ethernet be real-time enough for control response without lag or intermittent sluggishness?
  Option would be to switch to EIA232/422, but would then have to write communications application?
Which embedded processor/development environment would be the best choice for the motor drive application?
Fujinon remote digital interface does not appear to have a rate control mode for zoom – position only. Would this be any good?
Not clear of Fujinon analog zoom input is rate or position – looks like position. Better option to spoof the hand control rocker input? It is definitely a rate control.

## Slide 6: MBARI requirements for our main ROV cameras
MBARI requires professional quality zoom and focus controls!
Focus Position Slider
Pan & Tilt Control
Zoom Rate Control Rocker Switch
Ikegami RCP
https://www.youtube.com/watch?v=X8oWnbcLI40
(2,794,882 views)
Focus example
https://vimeo.com/43330022
Commercial follow focus example

## Slide 7: Top to Bottom Architecture 1

## Slide 8: Top to Bottom Architecture 2

## Slide 15: Current Lapbox Design

## Slide 16: Fujinon Lens Control Interfaces

## Slide 17: Fujinon Lens to Camera Interface

## Slide 18: Older HD lens

## Slide 19
Micro coax cables

## Slide 20: Possible technology
Ethernet to fiber converters
  https://fibertronics.com/2-port-switch-101001000-rj45-to-2-sfp-ports
  https://fibertronics.com/101001000base-t-to-sfp-ethernet-media
  https://www.blackbox.com/en-us/store/Detail.aspx/Pure-Networking-Copper-to-Fiber-Media-Converter---10-100BASE-TX-to-100BASE-FX-SFP/LHC210A
  https://www.perle.com/products/10-100-poe-media-converters.shtml#applicationdiagrams
Sony RCP serial to Ethernet converters

## Slide 21: Lens Drive Motors & Encoders
Drive motors
  Maxon
  www.faulhaber.com
Torque limit clutches
  https://dynatect.com/product/clutches/mechanical-slip-clutches/series-16/
  https://shop.sdp-si.com/catalog/?brand=sdp&cid=p680
Encoders
  https://ecatalog.dynapar.com/ecatalog/incremental-encoders/en/E9?_ga=2.158800634.171294003.1560294496-1192861477.1560294496

## Slide 23: Sony HDC-P50 Camera
Geometric center
Optical center
15.5mm offset