## Slide 1: 4K ROV Camera Development Abstract Presentation
May 22, 2019 – Mark Chaffey

## Slide 2: The Importance of ROV Video to MBARI’s Research Mission
Notes: This is an example of one of the vent chimneys first discovered in the AUV mapping along the Alarcon rise.

## Slide 3: How We Got Here – the History of Video Formats at MBARI
Betacam SP
Analog
Panasonic D5 1920x1080 60i
2018 Prores HQ Files 1920x1080 60i
Prores HQ Files 4096x2160 60p
4K Video!
4K?
1999
1988
1998
Digital Betacam 720x480 60i
1995
2010
2020 +
2020?
20 years + !!
Museum of Obsolete Media
Notes: Museum of obsolete media!

## Slide 4: Advantages of 4K Video
Four times the pixel resolution of current HD.
  Better resolution increases scientific insight.
  Provides high quality images for public outreach and education.
  Allows cropping of images for publication without too much visual degradation.
Images are scanned progressively.
  Eliminates interlace artifacts.
High quality camera modules are now available.
  2/3” 3-chip for excellent depth of field and sensitivity.
  Compact modules suitable for deep housings.
Imaged in 2K
Imaged in 4K
i2MAP Test Tank Recordings Horizontal Resolution in Hundreds of Line Pairs/Picture Width

## Slide 5: 4k Technical challenge of long term data storage
4K video at 60 frames per second (4096 x 2160 60p) is a very large jump in the amount of data.
  Master level Apple ProRes Codec 422 HQ is about 848 Gigabytes per hour.
  Mezzanine level H.264 or H.265 Codec is around 10:1 or 85 Gigabytes/hr.
The MBARI Titan network share system has the capacity to support 4K video acquisition on MBARI’s main vehicles for at least 10 years.
Over a period of time the video data would grow to be by far the largest data share at MBARI.
Are there responsible ways to reduce the 4K total video data volume while preserving the value of video data thereby lowering the resource and capital cost? Yes!

## Slide 6: Handling the Data – Annotation Selects 4K Video at Master Level, All Else Mezzanine (H.265?) Only
4K Camera
Master and Mezzanine Level File Capture & write LTO tape (MBARI M3 System)
Shipboard
On-shore
Some Master Else Mezzanine Level 4K Video Files
Onsite Titan Disk and Tape store
All Master and Mezzanine Level 4K Video Files
Offsite Backup Tape Archive
Temp File Store
848 GB + /hour
X 2 ROV’s !
Video Clip Quality:
Master
Mezzanine

## Slide 7: Looking Ahead - Video Storage Cost Comparison Stay with HD vs 20% 4K Selects
Chart: Annual Video Only Data Storage Costs with 4K Cameras on ROV's Model D Select 4K
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
2 Main ROV Cameras Annual Video Fixed Cost + Tape HD switch to 4K | 7069.5529 | 8077.4386 | 17034.3302 | 8406.1832 | 8406.1832 | 8406.1832 | 8406.1832 | 8406.1832 | 8406.1832 | 8406.1832 | 8406.1832 | 8406.1832 | 8406.1832
Model D 2 Main ROV Cameras Annual Video Fixed Cost + Tape 4K HQ Selects + Mezz only | 0 | 0 | 29065.9482 | 34616.4325 | 40166.9167 | 45717.4009 | 51267.8852 | 52417.2326 | 53566.58 | 54715.9275 | 55865.2749 | 57014.6223 | 58163.9698
All other Video Data Projected Annual Fixed Cost + Tape HD | 785.5059 | 1034.9567 | 1289.6895 | 1544.4224 | 1799.1552 | 2053.888 | 2308.6208 | 2334.9928 | 2361.3647 | 2387.7367 | 2414.1086 | 2440.4806 | 2466.8525
Video Archive Conversion to File Data annual storage | 0 | 0 | 31833.8081 | 42261.5162 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163
Chart: Annual Video Only Data Storage Costs with HD Cameras on ROV's
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
2 Main ROV Cameras Annual Video Fixed Cost + Tape HD switch stay with HD | 7069.5529 | 15146.9915 | 19350.0831 | 23553.1747 | 27756.2663 | 31959.3579 | 36162.4495 | 40365.5411 | 44568.6326 | 48771.7242 | 52974.8158 | 57177.9074 | 61380.999
All other Video Data Projected Annual Fixed Cost + Tape HD | 785.5059 | 1034.9567 | 1289.6895 | 1544.4224 | 1799.1552 | 2053.888 | 2308.6208 | 2334.9928 | 2361.3647 | 2387.7367 | 2414.1086 | 2440.4806 | 2466.8525
Video Archive Conversion to File Data annual storage | 0 | 0 | 31833.8081 | 42261.5162 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163 | 20855.4163
Pre-2018 D5 Tape Annual Cost
Pre-2018 D5 Tape Annual Cost
1080 60p video
4028 60p video

## Slide 8: Looking Ahead - 2030 Storage Costs with 20% 4K selects
Chart: 2030 Annual Cost Breakdown: Model D - Select 4K Total Annual $90,356
| New Video Storage Tape Cost (includes backup tape) | Annual on-line fixed costs for video library | Annual backup cold storage costs for video library | Annual on-line fixed costs for converted video archive | Annual backup cold storage costs for converted video archive | Annual all other Video Data Projected Fixed Cost + Tape HD
Model D Total Annual Cost of ALL Video Storage with 4K Selects + Mezzanine | 23515.464 | 32946.591 | 10108.098 | 19834.1483 | 1021.2679 | 2466.8525
Chart: 2030 Annual Cost Breakdown: Model D - Select 4K Total Annual $103,279

## Slide 9: Major High Level Camera Requirements
Image quality
  Resolution
  Contrast ratio
  Color reproduction
Camera controls
  Zoom, focus and iris
  Black and white balance, shutter speed , etc.
Camera size and weight
Camera cost
Camera ease of maintenance
Full Requirements Doc: \\Atlas\ProjectLibrary\901900_MBARI_Advanced_Imaging_Infrastructure\EngineeringDesignDocuments\4KCameraRequirements

## Slide 10: MBARI requirements for our main ROV cameras
MBARI requires professional quality zoom and focus controls!
Focus Position Slider
Pan & Tilt Control
Zoom Rate Control Rocker Switch
Ikegami RCP
https://www.youtube.com/watch?v=X8oWnbcLI40
(2,794,882 views)
Focus example

## Slide 11
Corner resolution
Center resolution
Line pairs/PW
Chromatic aberration
Geometric distortion

## Slide 12: Tests of Commercially Available 4K Cameras
Sony FDR-AX100
Sony FCB-ER8550
All commercial cameras tested had very poor lens controls…….
DSP&L
Sulis
Insite
SubC
i2MAP 4K
Building Blocks

## Slide 13: Best Candidate Camera Module
Sony HDC P50
  2/3” 3-Chip CMOS imager
  4096x2160 progressive scanning @ 60 frames/sec.
4K Resolution Lenses – very important!
  Fujinon UA13x4.5 BERA 4K UHD Wide lens with 13x Zoom
  Canon CJ12ex4.3B 4K UHD wide-angle lens with 12x Zoom

## Slide 14: Camera Acquisition - Three potential paths forward
Co-develop with commercial vendor and license our contribution
  Reward
    Maintain high quality
    Shared technical risk
    Easy maintenance and replacement support
  Risks
    Some technical risk
Purchase commercial system
  Reward
    Controlled cost
    Easy maintenance and replacement support
    Low MBARI technical risk
  Risks
    Lower quality
    High capital cost
Develop and build in house
  Reward
    Maintain high quality
    Lower capital cost
  Risks
    Technical risk
    Higher engineering time commitment
    Maintenance and replacement support can be more difficult
    Unable to provide systems to outside partners

## Slide 15: Camera Progress to Date
Requirements developed and shared with vendors.
Trying to qualify vendors who we are confident can do a good job.
  Sulis camera and Subsea have expressed interest.
  Need to contact additional potential vendors.
The next step is to establish a final vendor list and issue an RFQ and evaluate the response.
Simultaneously continue discussions on co-development.

## Slide 16: Conclusions
MBARI invests a tremendous amount of capital and resources on video acquisition, processing and maintaining the video library.
Striving for the highest quality feasible for acquisition increases the value of all subsequent investments.
MBARI is well positioned to once again take a big step forward and be a leader in deep sea video imaging.
Notes: The higher the quality of the video the more valuable it is for MBARI’s research interests.
In addition the Aquarium is working extensively with video for public education with exhibits, including video walls and a very active YouTube channel. YouTube now depreciates content not in 4K. The aquarium provides MBARI a very active outlet for high quality content. Our access to the deep sea is unparalleled – our imaging should be also.
The truth is in the seeing and we ran an i2MAP transect in 4K resolution in order to not interrupt these presentations we can show it over the lunch break. Thanks to Todd
Finally….

## Slide 17: Previous Work ……

## Slide 18: Questions?