## Slide 1: The Environmental Sample Processor (ESP)

## Slide 2
Image courtesy of the Center for Environmental Visualization, University of Washington
What is an Ecogenomic Sensor?
Notes: Ginger Armburst and John Delany at UW had this illustration made in 2005. Where they envisioned
Retrieve information from the field directly, under natural conditions, and eliminate the traditional requirement for shore-side analyses of retrieved samples
Based on outcomes of a DOE workshop with a microbiology focus

## Slide 3
What is an Ecogenomic Sensor?
command
control
data
target
acquisition
sample
handling
analyte
detection
clients
native water sample
intake
A molecular analytical device capable of autonomous operation and 2-way comms –
a “lab in a can”
Scholin et al. 2017 Oceanography 30:100-113
sample and reagent volume handling spans ~6 orders of magnitude:
native water intake (L’s) to reagent (µL’s)
Notes: Ginger Armburst and John Delany at UW had this illustration made a little over a decade ago. Where they envisioned
Retrieve information from the field directly, under natural conditions, and eliminate the traditional requirement for shore-side analyses of retrieved samples
Based on outcomes of a DOE workshop with a microbiology focus

## Slide 4: The Environmental Sample Processor
2nd
Generation ESP
3rd
Generation
ESP
ESP FIDO
Co-design with USGS for freshwater applications
Crewed ship operation demonstrated
Purpose built for sample collection/preservation only
Simplified, easy-to-use interface
Enables mobile sampling
Deployment platform manages power, contextual sensors, communications
Modular system
  Sample preservation or homogenization
  Add-on Analytics
Stationary sampling
2G ESP manages contextual sensors and communications
Fully integrated sampling and sample processing
Add-on sampling and analytics
All internet-accessible and remotely controllable

## Slide 5: Environmental DNA
A cheaper, less invasive and larger scale approach to monitor species diversity – two approaches: next generation sequencing (NGS) or species specific primers, latter is easier
12S rDNA
COI
18S rDNA
16S rDNA
Vertebrates
Invertebrates, some vertebrates, & phytoplankton
Microbes
(Bacteria & Archaea)
?
Phytoplankton & invertebrates,
some vertebrates
Each marker targets a different group of organisms.
After Djurhuus et al. 2017 Frontiers in Marine Science

## Slide 6: 3rd Generation ESP
Sample preservation
  - filter & preserve
In situ sample homogenization
  cartridge lysate storage
  enable real-time analysis
  surface plasmon resonance
Autonomous Vehicle Integration
Notes: Point out the 2G ESP. All the hanging bags and puck. 3G, smaller, only carry reagents needed one cartridge. More functionality than the 3G.
Each cartridge holds sample collection material and all reagents needed to preserve it or process to provide real time data.
Developed protocols for preservation, lysis and to modifiy so it could be analzyed imeddiately by the AM
One cartridge = everything to process one sample
  Filter (25 mm)
  Preservative reagent (RNAlater)

## Slide 7: Modularity and Standardized Interfaces = Flexibility
mechanical actuation
electrical bus
Allow for different types of cartridges, same form factor
sample in, filtrate out
To analytical device

## Slide 8: ESP Sample Preservation
Sample collection
Preservative (RNAlater) pushed in and displaces the sample water to waste.
Preservative reaches >95% concentration.
Water Sample in
Sample
Filtration
Valve Sample Position
Preservative (1.6ml)
1
2
Valve Reagent Position
Preservative (1.6ml)
waste
waste
Sample
Preserved
Preservative displaces residual sample water to waste on cartridge.

## Slide 9
Increasing eDNA spatial and temporal sampling
Solution #1
  increase the fleet size

## Slide 10
Blade diameter = 93m
Tower height = 68m
Offshore Windfarm eDNA Survey
91 Turbines; 209MW capacity. 30km offshore. 35 km2.
LRAUV/ESP operations--June 6-18, 2024

## Slide 11
June 2024 – Denmark – Biodiversity Monitoring
104 eDNA Samples
New Challenges:
Navigation within the windfarm & cathodic protection
Shallow (< 15m), large tides and current
Offshore Windfarm eDNA Survey
Notes: Denmark has 13 operational wind farms. We focused on Horn’s Reef II.

## Slide 12
Increasing spatial and temporal coverage
Solution #1
  increase the fleet size
Solution #2
use complementary sensing/sampling modalities
inter-vehicle coms/ranging to target sampling
AUV Docking

## Slide 13
Increasing spatial and temporal scales
Solution #1
  increase the fleet size
Solution #2
complementary payloads
multi-vehicle ops
adaptive response
docking
Solution #3
multiple deployment platforms
Crewed ships
Saildrone Surveyor
- Seatrac
- Tidewise Tupan (in progress)

## Slide 14: Saildrone Surveyor CA to HI
Preston, C., et al., Environmental DNA, 6, e468. https://doi.org/10.1002/edn3.468
2021 – CA to HI – 29 days, 4200 km, 52 eDNA samples
Combined with seafloor mapping
Notes: When we begin to start deploying these types of instruments on autonomous surface vehichles, such as Saildrone surveyor here we can increase the spatial coverage of biodiversity observation through eDNA. Here I am showing a deployment of the ESP onboard the Saildrone Survey on a deployment from Califronia to Hawaii, where we collected 52 eDNA samples over 4200 km and the result relative abundance of taxa returned through metabarcoding of CO1 and we can drill down into the metabarcoding data to investigate changes in the cnidarian population of the transect.
Coupling these autonomous eDNA samplers with autonomous surface vehichle like saildrone surveyor is providing the ability to collect biodiversity data with eDNA over large spatial areas.
Rodney saildrone testing technology for Aleutians.

## Slide 15
Saildrone Surveyor CA to AK
August 2022 – February 2023 (110 days)
45,000 km2 seafloor mapped
163 eDNA samples over 17,000 km traveled
Notes: Notes from Neah’s Mission Posts: 2/22/23
At least 50% of the area was previously unmapped
1.5 X size of Massachusetts
20 X size Luxemburg
August 2022 – February 2023
45,000 km2 seafloor mapped over 96 mapping days
163 eDNA samples collected over 17,000 km traveled
All performed autonomously, overseen by pilots all throughout the US.

## Slide 16: Aleutian Islands: eDNA sampling & mapping leg
Alaska
97 eDNA samples collected along the Aleutian Islands
August 12 to October 3, 2022
Amlia Basin
50 nm
10 nm
Notes: The expedition focused on a 300nm region of the Aleutian Islands west of Dutch Harbor. Filtration of eDNA samples occurred while SD-1200 was underway and mapping the seafloor in priority areas identified by X. An example of the mapping path of Amlia Basin and the location of eDNA samples collected.
US Department of Interior: Bureau of Ocean Energy Management
300nm from Dutch Harbor to Western point Amlia Basin
August 12 to October 3. Sampling within Aleutian Chain
Winds up to 40+ kn and gusts to 50+ kn (58 mph)
Seas up to 8+ m (26 ft)
Still sampling during as transit back to Alameda.