## Slide 1
Underwater Vehicle Docking
Northrop Grumman Collaboration
Brett Hobson
François Cazenave
Rob McEwen
Brian Kieft
Ben Ranaan
Scott Jensen
Andrew Hamilton

## Slide 2: Why should MBARI be developing AUV Docking, now?
LRAUVs are ready:
  Reliable: over 25,000 hours
  Payloads: ESP, BioAcoustic, Biolum, Water Sampler, Imaging (soon)
  On-Board Processing: Plankton Proxies, eDNA (soon)
  Expanding Operator Pool for Routine Operations (Time-Series):
    25 Now
    New User Interface to Allow Novice Operators: 100? (soon)
Time-Series operations are great, but Event Response is the “Killer App” for Long-Endurance, Mobile Robots Like our LRAUV
Existing 24/7/360 observatories:
Slide from last year. Andy to update or remove.

## Slide 3
Notes: Video has been trimmed to 30 s.

## Slide 4: Brett: no slide necessary

## Slide 5: Niobicon technology
Patented and developed by Northrop-Grumman
Uses pure Niobium, a chemical element with atomic number 41
Thin oxide layer isolate niobium in water
Submersible connector does not require waterproofing
Allows axial and rotary motion
Limited to 60 V

## Slide 6: Power Transfer device: AUV side

## Slide 7: Power Transfer device: charging rod
6’ long, ¾” diameter niobium tube bonded to fiberglass core
Contacts are potted in resin

## Slide 9
Notes: Replace with more recent video

## Slide 12: New docking mooring in 2022
  Build a more robust mooring in collaboration with WHOI.
  Implement charging and data transfer
  Support science missions

## Slide 13: Dock on MARS in 2023 and 2024
  MARS is an ideal site for an AUV dock
  Power and comms are available
  No wave action or biofouling
  Will require deep LRAUV

## Slide 14: Northrop Grumman License Agreement
Royalty free license. Signed May 15th
New technology developed is Jointly owned IP
Existing MBARI IP remains owned by MBARI (and vice versa)
Patent procurement is Northrop Grummans responsibility
Future commercial license revenue is split
MBARI has a right to use all Joint IP for our own use
Slide from last year. Andy to update.

## Slide 15: Show provisional patent cover sheet