## Slide 1
Underwater Vehicle Docking
Northrop Grumman Collaboration
Brett Hobson
François Cazenave
Rob McEwen
Brian Kieft
Ben Ranaan
Scott Jensen
Andrew Hamilton

## Slide 2
Notes: Video has been trimmed to 30 s.

## Slide 3: Why should MBARI be developing AUV Docking, now?
LRAUVs are ready:
  Reliable: over 25,000 hours
  Payloads: ESP, BioAcoustic, Biolum, Water Sampler, Imaging (soon)
  On-Board Processing: Plankton Proxies, eDNA (soon)
  Expanding Operator Pool for Routine Operations (Time-Series):
    25 Now
    New User Interface to Allow Novice Operators: 100? (soon)
Time-Series operations are great, but Event Response is the “Killer App” for Long-Endurance, Mobile Robots Like our LRAUV
Existing 24/7/360 observatories:
Slide from last year. Andy to update

## Slide 4: Niobicon technology
Patented and developed by Northrop-Grumman
Uses pure Niobium
Thin oxide layer isolates niobium in water
Submersible connector does not require waterproofing
Can allow axial and rotary motion
Limited to 60 V and moderate power

## Slide 5: Power Transfer device demonstration
Niobium “brushes”
Spring loaded niobium brushes inside clamp
Charge rod

## Slide 6
Actuator
Arm
Clamp with niobium brushes
Optical sensor

## Slide 7
Notes: Replace with more recent video

## Slide 9: Mooring design

## Slide 10: New mooring to be built in 2022
  Build a more robust mooring in collaboration with WHOI.
  Implement charging and data transfer
  Support science missions

## Slide 11: Deploy a dock on MARS in 2023 and 2024
  MARS is an ideal site for an AUV dock
  Power and comms are available
  No wave action or biofouling
  Will require deep LRAUV

## Slide 12: Wave-powered AUV dock
Solar buoy generates 25 W on average:
    Can support 1 LRAUV
MBARI’s wave energy buoy generates 200 W on average:
    Could support several LRAUVs, or a DORADO AUV.
Some challenges remain.

## Slide 13: Northrop Grumman License Agreement
Royalty free license. Signed May 15th, 2021
New technology developed is jointly owned IP
Existing MBARI IP remains owned by MBARI (and vice versa)
Patent procurement is Northrop Grumman's responsibility
Future commercial license revenue is split
MBARI has a right to use all Joint IP for our own use

## Slide 16
Organization | Name | Title
Naval Research Warfare Center (NUWC Newport) | CDR Jason Patton | CDR
VTG Defense | Jim Shannon (RADM USN, Retired) | Executive Vice President Gov't Relations
Leidos | Steve Boraz | Business Development Director - Maritime
Teledyne Energy Systems | Gard Clark | Senior Vice President Energy and Environment
Teledyne Technologies | Thomas Altshuler | Senior Vice President, Global Maritime Defense Strategy and Business Development
Landing Craft Support Museum | Christopher Lehman | Chairman
RCT Systems | Stephen M. Cobb | President
Massa Products Corporation | Dawn Massa Stancavish | President/CEO & Chief Innovation Officer
Artimus Robotics | Timothy G Morrissey | Chief Executive Officer
SAAB Autonomous & Undersea Systems | Daniel Lawrence | Director, Marine Operations and Training
General Dynamics Electric Boat | Chris Tate | 
General Dynamics Electric Boat | Keith Sacco | Principal Engineer
Proteq | Robert Grieve | President & CEO (former WHOI rep)
Advanced Technology International | Chance Xavier Roman | Sr Project Manager
L3 Harris | Michael Rose | Principal Mission Solution Architect
L3 Harris | Noland Smith | Principal Business Development Manager
L3 Harris | Matt Gusto | Business Development Director - Maritime

## Slide 17: Conclusion. Slide TBD