## Slide 1
Underwater Vehicle Docking
Northrop Grumman Collaboration
Brett Hobson
François Cazenave
Rob McEwen
Brian Kieft
Ben Ranaan
Scott Jensen
Andrew Hamilton

## Slide 2
Notes: Video has been trimmed to 30 s.

## Slide 3: AUV Docking
Docking has been a long term goal, bedeviled by complexity (at MBARI and elsewhere), especially for cruising vehicles.
  Cone dock efforts, crash landing.
Latch-on-wire techniques came into view a few years back. But no way to transfer power. Niobiocon technology has changed that.
Great progress has been made in 18 months, nearly operational system is at sea.
Applications include:
  Docking for recharge and support of vehicles in remote locations.
  Buoy supported (solar and wave-energy)
  MARS supported
  Axial Seamount and other lie-in-wait applications.

## Slide 4: Niobicon technology
Patented and developed by Northrop-Grumman
Uses pure niobium
Thin film isolates niobium in water
Submersible connector does not require waterproofing
Can allow axial and rotary motion
Limited to 60 V and moderate power

## Slide 5: Power Transfer device demonstration
Niobium “brushes”
Spring loaded niobium brushes inside clamp
Charge rod

## Slide 6
Actuator
Arm
Clamp with niobium brushes
Optical sensor

## Slide 7
Notes: Replace with more recent video

## Slide 8: Mooring design

## Slide 9: Brett to talk about how the AUV docks, acoustics, software. Talk about live video, then video of AUV docking.

## Slide 11: Brett to talk about what happens when the AUV is on the dock and show screen shot of AUV on the dock.

## Slide 13: New mooring to be built in 2022
  Build a more robust mooring in collaboration with WHOI.
  Implement charging and data transfer
  Support science missions

## Slide 14: Deploy a dock on MARS in 2023 and 2024
  MARS is an ideal site for an AUV dock
  Power and comms are available
  No wave action or biofouling
  Will require deep LRAUV

## Slide 15: Wave-powered AUV dock
Solar buoy generates 25 W on average:
    Can support 1 LRAUV
MBARI’s wave energy buoy generates 200 W on average:
    Could support several LRAUVs, or a DORADO AUV.
Some challenges remain.

## Slide 16: Northrop Grumman License Agreement
Royalty free license. Signed May 15th, 2021
New technology developed is jointly owned IP
Existing MBARI IP remains owned by MBARI (and vice versa)
Patent procurement is Northrop Grumman's responsibility
Future commercial license revenue is split
MBARI has a right to use all Joint IP for our own use

## Slide 19
Organization | Name | Title
Naval Research Warfare Center (NUWC Newport) | CDR Jason Patton | CDR
VTG Defense | Jim Shannon (RADM USN, Retired) | Executive Vice President Gov't Relations
Leidos | Steve Boraz | Business Development Director - Maritime
Teledyne Energy Systems | Gard Clark | Senior Vice President Energy and Environment
Teledyne Technologies | Thomas Altshuler | Senior Vice President, Global Maritime Defense Strategy and Business Development
Landing Craft Support Museum | Christopher Lehman | Chairman
RCT Systems | Stephen M. Cobb | President
Massa Products Corporation | Dawn Massa Stancavish | President/CEO & Chief Innovation Officer
Artimus Robotics | Timothy G Morrissey | Chief Executive Officer
SAAB Autonomous & Undersea Systems | Daniel Lawrence | Director, Marine Operations and Training
General Dynamics Electric Boat | Chris Tate | 
General Dynamics Electric Boat | Keith Sacco | Principal Engineer
Proteq | Robert Grieve | President & CEO (former WHOI rep)
Advanced Technology International | Chance Xavier Roman | Sr Project Manager
L3 Harris | Michael Rose | Principal Mission Solution Architect
L3 Harris | Noland Smith | Principal Business Development Manager
L3 Harris | Matt Gusto | Business Development Director - Maritime

## Slide 20: Conclusion. Slide TBD