## Slide 1: Slide Show Prelude
LRAUV_highlights_reel_with_music.mp4
maybe no music
Maybe play outside of PP for full ProRes

## Slide 2: Project Update MBARI LONG RANGE AUV - LRAUV

## Slide 3: Project Update MBARI LONG RANGE AUV - LRAUV
SECTION OUTLINE:
Review of the LRAUV – Why it’s so cool
Current Payloads and Capabilities
Future Payloads, Capabilities and Export
Killer Apps
Call for new missions

## Slide 4: MBARI’s LRAUV Development Project Update 9/30/25
Brett Hobson, hobson@mbari.org
Outline – not a slide
Who is and has been involved
Review:
  Describe the LRAUV: specs, shipless/sub-v-sub, why its unique and useful
  Payloads, including why they’re useful and a use-case plus pubs
  Other capabilities, including adaptive sampling, under-ice, docking
Export
Future capabilities
  Hovering, deep-er, arctic
Discussion of the uber mission, only at MBARI, with a fleet of LRAUVs
Call for new missions. Give hats as prizes/incentive
Notes: In my presentation about the development of robots for open ocean ecology I’m going to start with an introduction to the open ocean environment to hopefully show why an improved understanding of this massive environment is vitally important to us all. From there, I’m going to review some of the tools ocean scientists use and then get to the topic I’m most familiar with: The development of platfoms to carry these tools. I’ll then present a case study experiment we recently performed and end with our development plans for the future.
The open ocean is a massive 3D ecosystem responsible for absorbing much ~90%) of excess heat we produce and about 25% CO2 emissions produced by humans. A portion of the ocean’s carbon pump sequesters atmospheric carbon into the sediments of the deep sea. Quantifying the amount of this carbon exported to the deep and identifying the variables driving that export is vital to understanding how we might better mitigate the deleterious effects of climate change. The Monterey Bay Aquarium Institutes MBARI has developed high endurance mobile robots to investigate ocean carbon transport. One of its vehicles, the Benthic Rover has been working continuously on the seafloor at 4000m for 6 years-- measuring the spatial and temporal variability of carbon export from the surface. This long-term dataset has revealed that carbon enters the deep sea in large pulses of sinking detritus. MBARI is now focused on connecting these carbon pulses to processes in the upper layers of the ocean. Exploring, mapping and sampling the upper water column to uncover ocean productivity hotspots (HS) is a central/key initiative/goal requiring the collaboration of MBARI’s Long Range Autonomous Underwater Vehicles (LRAUVs) as well as other complementary vehicles that are able to measure the full ecology of the hotspots from the microbes to the whales.

## Slide 5: LRAUV - People
Development team:
Brett Hobson, Brian Kieft and Quinn Shemet
Yanwu Zhang, Erik Trauschke, Carlos Rueda, Jon Erickson
Michael Anderson, Denis Klimov, Brent Jones,, Tom O’Reilly, Francois Cazenave, Andy Hamilton
Alumni: James Bellingham (Johns Hopkins), Mike Godin, Ed Mellinger, Mark Chaffey, Chad Kecy
Operations:
Chris Wahl, Varsha Senthil, Cole Grasse, Evan Mattiasen
Payload Specialists:
Chris Preston, Paul Roberts, Thom Maughan, Jared Figurski, Chad Waluk
Support:
Jose Rosal and his ET team, Paul Coenen and his MT team, Aaron Schnittger, Frank Flores, Machine Shop
Science Early Adopters:
Francisco Chavez, Chris Scholin, Steve Haddock, Kelly Benoit-Bird, Monique Messie, John Ryan, Kakani Katija, Colleen Durkin, Steve Rock, Giancarlo Troni

## Slide 6: LRAUV - Key Characteristics
Length: 6.6 – 10.4 ft (2-3 M)
Diameter: 1 ft (0.3 M)
Weight: 243-350 lbs (110-160 kg)
Speed: 0 – 3 knots
Range: Up to 1000 km in long range transit mode
Battery: 5.7 kW-hr Rechargeable or 14 kW-hr Primary
Neutrally Buoyant at Depth – Efficient Cruise and Lagrangian Drift
Low-Speed/Long range + Optional High Power Payloads
Shipless Operations - Submarine verses a Submersible
Mature: Over 60,000 Hours of Offshore Operations

## Slide 7: Core Vehicle Features
Core Science Payload
Direct-Drive Thruster
Open
Payload Bay
Move-able Mass Battery Pack
24 Channel Configurable Load Control
Antenna Mast
Variable Buoyancy System Plus Emergency Drop Weight
Paired Elevators and Rudders
Backseat Computer
Main Vehicle Computer
Open Payload Bay
Move-able Battery Pack
24 Channel Load/Comms Control
High Efficiency Direct Drive Thruster
1L Variable Buoyancy
Antenna Mast Sat/Cell/WiFi/Argos/VHF
1/3 Watt Main Computer
Backseat Computer

## Slide 8
We’ve created a new class of ocean science robot:
  Persistence
    Variable-speed: low Speed/power = long range or high speed/power
      low drag hull, high efficiency drive train, variable buoyancy
  Ship-less
    Submarine vs Submersible: A submarine is a self-sufficient vessel capable of leaving port, operating independently for extended periods, and returning on its own power, while a submersible is dependent on a mothership for launch, recovery, and support, and has limited power reserves for short-duration dives
  Smart:
    Adaptive sampling
    Open Backseat Computer
      Easy to safely run third party software
    Configurable
      Parallel hull can be extended for various payload configurations
  Collaborative
    Inter-vehicle communication and positioning
      Multi-vehicle collaboration with complimentary payloads, formation flying, sampling hand-off
    Open-source software and simulator
Big Idea

## Slide 9: Operational LRAUV Payloads

## Slide 10: Core Sensors On All Vehicles
Chlorophyll + OBS
Wetlabs Triplet Puck
Acoustic Modem + iUSBL Benthos DAT
Dissolved Oxygen
Seabird SBE-43
CTD
Seabird GPCTD

## Slide 11: Payloads – Imaging 2 In-Situ Plankton Imaging Microscope - Planktivore
Size range:
  20 µm to 2 cm
Illumination modes:
  Shadowgraph. Monochrome, large DOF (depth of field), accurate size
  Darkfield. Color, smaller DOF, excellent contrast
  Holographic. Monochrome, large DOF, accurate size
Embedded compute module providing image processing
Real-time data reduction (~1000:1) by image processing and storing ROI
Real-time particle size spectra
Plankton identification leveraging machine learning

## Slide 12
Ship-less operations –
CHALLENGE: During EcoHAB,
LRAUVs could find Chlorophyl hot spots, but needed boats and people to ID HAB Species
Payload Use Case:
Pseudo-Nitzschia ID

## Slide 14: Payloads – Imaging 2 3-D Plankton Imaging – Triton
2 L Imaged Volume
@ 50 um Resolution
300k Lumen Strobe
24 MP 3 Camera Array
Quantitative macroscopic imaging of 3D particle distributions, plankton/nekton, and marine snow
Detection of objects: 2 mm to 20 cm
Detection of particles: 0.4 mm to 20 cm
Realtime ROI extraction
Realtime particle size analysis
Animals, Marine Snow, Oil droplets, and Dispersant
Mining Sediment in the Water Column
5 mm
10 mm
20 mm

## Slide 15
CHALLENGE: It’s difficult to connect deep sea carbon pulses to surface processes
Payload Use Case: Marine Snow Carbon Export
Annotated
Raw
Particle Size
Marine Carbon Dioxide Removal (mCDR)
Ship-less EXPORTS experiment
Find, Follow and Sample biological hotspots
  USVs like MBARI’s Wave Glider can follow hot spots to provide an acoustic reference for submerged mobile detritus imaging systems
  LRAUVs can track submerged hot spots without a surface expression
  Map the 3D particle distribution of sinking material under these hotspots with Triton
Credit: Kristen Krumhardt

## Slide 16: Payloads – Acoustic Kongsberg EK-80 Mini Echosounder
Unique Features
Collect in situ water column data above and below the vehicle
Optimum beam geometry for near bottom or near surface
Loitering capability
Specs
200 kHz and 333 kHz
Simultaneous upward and downward
Gimbaled mount to maintain vertical transducers

## Slide 17
Ship-less operations – Beach launch and recovery
Low-speed transit between survey lines and loiter during he day, followed by “high speed” night time survey: 421km mission included 163 km of survey lines
Survey from the midwater: looking up and down
- Full view of Surface Acoustic Dead Zone
Coupled with eDNA samples as a proxy for trawl net surveys: in, above and below thermocline + Benthic
CHALLENGE: Existing ship-based surveys are expensive and have an acoustic dead zone near the surface
Payload Use Case: USGS Fisheries Surveys
Surface Acoustic Dead Zone
Blair et al. In review at ICES: Quantifying fish abundance in the surface acoustic dead zone using a long range autonomous underwater vehicle

## Slide 18: Payloads – Environmental Sampler MBARI 3G ESP Microbial Sampler
Unique Features:
Preserved filtrate: microbes & eDNA
Near-real-time in situ detection of HAB toxins and other substances with add-on analytical module SPR today, PCR and Full Sequencing soon
Specs:
60 self-contained sample cartridges
60 day preservation stability
Proven eDNA collection/extraction
Analytical Module interface for in situ target substance detection
3G ESP Module, +60 cm

## Slide 19
CHALLENGE:
Payload Use Case: eDNA

## Slide 20: Payloads – Piscivore How can we find rare, diffuse, highly mobile and evasive species? How can we find rare, diffuse, highly mobile and evasive species?
Unique Features
  Add-on to LRAUV
  Lure to attract predators
  Environmental sensors
Characterizing the Habitat
Due to the extreme challenge of locating and studying them in the wild because
  Fast and Evasive
  Highly Mobile
  Rare
  Patchy
  Difficult to see beneath the ocean’s surface
Specs

## Slide 21
CHALLENGE: How do predator communities in the Monterey Bay ecosystem change seasonally and what prey field and physical habitat features do they associate with?
Payload Use Case: Picivore

## Slide 22: Missions Under-Ice Oil and Hazard Mapping
Rapid deployment to incident site using a Helicopter
Autonomous oil-in-water patch mapping and peak localization
Under-ice (cannot surface) operating mode, single beacon navigation
Homing and docking to thru-ice acoustic/RF Gateway for recovery
Development funded by US Coast Guard/DHS
Helicopter Deployable
Autonomous Oil patch Mapping
CHALLENGE: Quickly respond to oil spills under ice in the Arctic
Thru-ice Launch/Recovery
Under-ice operations
Oil patch mapping off Santa Barbara

## Slide 23: AUV Docking Persistent Operations
Omni-directional, compliant vertical line dock
Niobicon sliding contact power transfer: 500 Watts (48v @ 11 amps)
Collaboration with Northrop Grumman
1+ Mbps data transfer, plus acoustic modem backup
Web-based dock control interface with live video
Input power: Solar, wave or wind energy at the surface or
direct connect to a seafloor cable, battery or fuel cell
Surface buoy with Solar Energy Harvesting
Homing to Dock
AUV Parked on Dock

## Slide 24: Ocean Food Webs
Notes: Ecology slide
Inertial and viscus forces – do you sink or get stuck in the honey?
Reabsorption – biology is consuming (eating) everything, so only the fast sinkers make it out of the top ~200m
Life (biomass) is evenly distributed across all taxa, e.g.
  The larger the animal or plant, the less concentrated they are in ocean water, but
  Or at least was, until we eat most of the big fish and killed most of the sharks
However, the ocean’s predators cannot make a living on the average distribution of prey – it must be concentrated. A filter feeding whale would starve on a diet of the average distribution of krill
  Fortunately for the whales, and every other predator, life clusters along the boundaries. E.g. at fronts, transitions and layers – hot spots
Some of these hot spots are very effective at transporting carbon to the deep sea
  Krill and Salp Fecal pellets and mucus bombs of phyto detritus

## Slide 25: Tools to look at Open Ocean Life
From: F. Lombard et al., “Globally Consistent Quantitative Observations of Planktonic Ecosystems,” Front. Mar. Sci., vol. 6, p. 196, Apr. 2019
From: K. J. Benoit-Bird and G. L. Lawson, “Ecological Insights from Pelagic Habitats Acquired Using Active Acoustic Techniques,” Annu. Rev. Mar. Sci., vol. 8, no. 1, pp. 463–490, Jan. 2016
Triton
Optics
Acoustics
LRAUV Bioacoustics
LRAUV Micro Imaging
Notes: Many organisms aggregate in regions of abrupt bathymetry
Dense aggregations of zooplankton occupying vertical scales on the order of 1mand horizontal scales of kilometers, typically referred to as thin layers, constitute another form of aggregation
Acoustic estimates of the biomass of zooplankton and fish can be used to estimate the production of fecal pellets and contributions to downward carbon export

## Slide 26: Emerging Technology eDNA
Drawing by Kevan Yamahara, MBARI
Notes: Ecology slide
Inertial and viscus forces – do you sink or get stuck in the honey?
Reabsorption – biology is consuming (eating) everything, so only the fast sinkers make it out of the top ~200m
Life (biomass) is evenly distributed across all taxa, e.g.
  The larger the animal or plant, the less concentrated they are in ocean water, but
  Or at least was, until we eat most of the big fish and killed most of the sharks
However, the ocean’s predators cannot make a living on the average distribution of prey – it must be concentrated. A filter feeding whale would starve on a diet of the average distribution of krill
  Fortunately for the whales, and every other predator, life clusters along the boundaries. E.g. at fronts, transitions and layers – hot spots
Some of these hot spots are very effective at transporting carbon to the deep sea
  Fecal pellets and mucus bombs of phyto detritus

## Slide 27: AUV Docking Science Deployment

## Slide 28: Summary MBARI’s LRAUV is:
Medium Sized, Multi-Mission AUV
Long-Range Transit Mode
Suite of Payloads, including
eDNA Sampling, Fisheries Echo-sounder, Imaging and Mapping
Solar-Powered Docking Station for persistent operations

## Slide 29: Killer App1: Chasing Eddies
Surveyed eddy field north of Hawaii
Deployed
  LRAUV Opah at N edge, head S
  LRAUV Aku at E edge, head W
  Eddy transect is really a glider task
Deep Chlorophyll Max (DCM)
Started multi-day observation and sampling missions

## Slide 30: Typical Mission
LRAUV Aku dives to 250m looking for the DCM
  Notes temp at DCM
  Drives back up and takes up station on DCM isotherm 21°C in this example
  Samples ~ 1 liter every three hours – repeat
  Occasionally sample above and below the DCM

## Slide 31: Typical Mission 2
Did Aku stay in the DCM the entire time?
  Was the DCM still at 21°C?
  Did the patch move horizontally?
Nice to know Aku’s drift track
Nice to know if everything is OK & be able to abort
  Remember, this is supposed to work over the horizon, w/o ship

## Slide 32: Multi-Vehicle Collaboration
Wave Glider SV-3 with MBARI Hotspot payload
  USBL tracking, autonomous following
  Acoustic/RF Gateway
2nd LRAUV (Opah) to collect contextual data around sampler
  USBL tracking, autonomous following: circle + YoYo

## Slide 33: Combined Dataset
Yes, Aku stayed in DCM, collected 24 samples and moved ~100 km!
Low-res data available on shore for review

## Slide 34: Experiment Conclusions
Demonstrated An Autonomous Vehicle Based Open Ocean Lagrangian Observatory
  Long transit to work site – could have been ship-less
  Autonomous targeted sampling
  Collected 82 samples at, above and below the DCM over 9 diel cycles (4, 3 and 2 days continuous)
  3 vehicles working collaboratively
Subsurface tracking and acoustic/RF gateway
Produced a 4-D 'motion picture' of the genetic, taxonomic, transcriptional, metabolic, physical and chemical fields that drive the ecological dynamics of microbes in the DCM of a cycloidal eddy

## Slide 35: Killer App – Bio Hotspot Following
Upwelling-relaxation
Bloom
Advect out of Bay
Zooplankton
Carbon Export
MESSIÉ AND CHAVEZ 2017

## Slide 36: Killer App – Biological Hotspot Following
Dock-supported LRAUVs monitor evolution of hotspot – 1 month
Payloads: Chl/Biolum + Planktivore

## Slide 37: Killer App – Biological Hotspot Following
Dock-supported LRAUVs monitor evolution of hotspot – 1 month
Patch-Tracking to follow hotspot offshore - 1 week
Payloads: Chl/Biolum + Planktivore
Payloads: ESP Lagrangian at centroid – timeseries of eDNA
Mobil Chl for Patch centroid and contextual

## Slide 38: Killer App – Biological Hotspot Following
Dock-supported LRAUVs monitor evolution of hotspot – 1 month
Patch-Tracking to follow hotspot offshore - 1 week
LRAUVs with Primary Batts replace originals – 2/3 weeks
Payloads: Chl/Biolum + Planktivore
Payloads: ESP Lagrangian at centroid – timeseries of eDNA
Mobil Chl for Patch centroid and contextual
Payloads: ESP Lagrangian at centroid – timeseries of eDNA
Mobil Chl for Patch centroid and contextual
Triton below for carbon export mapping

## Slide 39: Killer App – Biological Hotspot Following
Dock-supported LRAUVs monitor evolution of hotspot – 1 month
Patch-Tracking to follow hotspot offshore - 1 week
LRAUVs with Primary Batts replace originals – 2/3 weeks
Packard heads out for intensive survey and LRAUV recovery – 1-2 weeks
Payloads: Chl/Biolum + Planktivore
Payloads: ESP Lagrangian at centroid – timeseries of eDNA
Mobil Chl for Patch centroid and contextual
Payloads: ESP Lagrangian at centroid – timeseries of eDNA
Mobil Chl for Patch centroid and contextual
Triton below for carbon export mapping
Payloads: ESP Lagrangian at centroid – timeseries of eDNA
Mobil Chl for Patch centroid and contextual
Triton below for carbon export mapping
Plus Planktivore

## Slide 40: NOWRDC National Offshore Wind Research and Development Consortium
Pelagic Observatory
perform a wide range of coordinated and complimentary ecosystem monitoring tasks over long periods of time without a continued presence of crewed ships.

## Slide 41: Floating Offshore Wind Power
California “might” get some offshore wind farms
Deep water – so the turbines must be floating
Regulators are planning rules to monitor the sites before and during installation
There are precedents for seafloor monitoring. Nothing exists for the water column

## Slide 42: Pelagic Observatory
Microbes-phytoplankton-zooplankton-forage fish-predatory fish and whales

## Slide 43: Future Plans (not funded)
Six+ month continuous operations
Seafloor mapping payload + precision navigation
Over the horizon LRAUV recovery using an Un-crewed Surface Vessel (USV)
Passive Acoustic Monitoring (PAM) with real-time ID of cetaceans and source vectoring
Resident operations at an active volcano (Axial Seamount)
Ship-less seafloor Imaging and mapping (Sur Ridge)

## Slide 44: LRAUV Export - Technology
Why do we want to license the LRAUV?
Packard Foundation wants us to share the technology
Facilitate new ocean science discoveries
Somebody to build vehicles for other users
Stock and sell spare parts and answer the phone for support
Somebody who will invest to improve the vehicle and expand the market for LRAUV
Somebody who won’t turn their back on ocean science
  OK to focus on defense/energy, but must support science
Help us develop a self sustaining, critical mass of external users that requires minimal support from us
License fee, from commercial buyers, e.g. people making money with our tech

## Slide 45: LRAUV Export - Technology
Requested licensing offers from:
  Cellula Robotics, Ocean Power Technologies, SeaTrec and Saab
  Teledyne, Kongsberg, Hydroid, ISE
You can now buy an LRAUV from Saab, for only $1.3M
News release from October 10, 2025:
Exciting news from Saab, Inc.! We have recently been selected to deliver a Long Range Autonomous Undersea Vehicle (LRAUV) to @NOAA’s Northeast Fisheries Science Center. This vehicle will become the next generation platform for offshore scallop bed surveys, boosting efficiency, helping advance sustainable fisheries and driving marine science forward. #SaabintheSea

## Slide 46: LRAUV Export - Collaborations
WHOI, Amy Kukulya and Mike Jakuba
  Licensed to build and operate three LRAUVs – Two are operational: Polaris and Stella
  Collaborated on a 5 year DHS funded effort to adapt LRAUV to track oil spills under ice - Pubs
  WHOI routinely performs seafloor scallop surveys for NOAA NMFS
  WHOI Salinity-Intrusion Front tracking – Pub
University of Hawaii, Dave Karl and Ed DeLong,
  Develop and open ocean microbial observatory
  NSF funding to manufactured three LRAUVs: Ahi, Aku and Opah – all Hawaiian names of local fish
  Eddies Experiment on the Falkor – Pub
  Lost staff due to funding cuts and eventually the vehicles were returned to MBARI
    Ahi and Aku were refurbished with funding from USGS for Great Lakes science
    Opah was rebuilt as the 1500 meter depth rated Mesopelagic LRAUV
USGS, Great Lakes Science Center, Peter Esselman, Hannah Blair (Cornell) and Murulee Byappanahalli,
  Improved fisheries bioacoustics surveys and an investigation into the microbiome of the Great Lakes
  Two pubs in review
JPL, Andrew Branch and Steve Chien
  Developed Front tracking/local maxima search algorithms; testing in Monterey Bay, Two pubs
University of Porto –João Sousa and Bernardo Gabriel,
  Various technology sharing projects
  Hosted a Fullbright student (Gabriel) at MBARI to develop a universal communications Module, Pub
NTNU (Norwegian University of Science and Technology), Martin Ludvigsen
  Future Fullbright, Grad student project or Post Doc collaboration
Johns Hopkins University, Jim Bellingham and Tanya Tebcherani
  Grad student projects on LRAUV and seeking joint funding for Arctic work

## Slide 47: Acknowledgements
The Packard Foundation
James Bellingham, Johns Hopkins University, Institute for Assured Autonomy
LRAUV team: Brian Kieft, Yanwu Zhang, Ben Raanan, Jon Erikson, Denis Klimov, Ed Mellinger, Mark Chaffey, Carlos Rueda, Tom O’Reilly, Rob McEwen, Brent Jones, Erik Trauschke, Chris Wahl, Paul Roberts, Thom Maughan and Quinn Shemet
Rover Team: Alana Sherman, Paul McGill, Rich Henthorn, Johnny Ferreria
MBARI Scientists: Chris Scholin, Francisco Chavez, Kelly Benoit-Bird, John Ryan, Steve Haddock, Monique Messie, Kakani Katija, Henry Ruhl, Ken Smith
External Collaborators: Amy Kukulya and Dana Yoerger (WHOI), Steve Rock (Stanford), Andrew Branch (JPL), Dave Karl and Edward DeLong (UH), Steve Ruberg (NOAA), Pete Esselman (USGS)

## Slide 48
2025 - 2029
Find, follow and sample hot spots, anywhere, for months on end
Enable true autonomy aboard individual and groups of vehicles to answer our questions and solve any new problems along the way
Map and image in complex terrain down to 1500m
Watch a legion of new users around the world extend MBARI’s success with their own LRAUV applications and discoveries
Where Do We Think We’re Heading?

## Slide 49: LRAUV Science Publications 1/3
[1]
[2]
D. H. Bennion, D. M. Warner, P. C. Esselman, B. Hobson, and B. Kieft, “A comparison of chlorophyll a values obtained from an autonomous underwater vehicle to satellite-based measures for Lake Michigan,” Journal of Great Lakes Research, May 2019, doi: 10.1016/j.jglr.2019.04.003.
[3]
J. Birch et al., “Autonomous Targeted Sampling of the Deep Chlorophyll Maximum Layer in a Subtropical North Pacific Eddy,” in OCEANS 2018 MTS/IEEE Charleston, Charleston, SC: IEEE, Oct. 2018, pp. 1–5. doi: 10.1109/OCEANS.2018.8604898.
[4]
A. Branch et al., “Front delineation and tracking with multiple underwater vehicles,” Journal of Field Robotics, Dec. 2018, doi: 10.1002/rob.21853.
[5]
A. Branch et al., “Demonstration of Autonomous Nested Search for Local Maxima Using an Unmanned Underwater Vehicle,” in 2020 IEEE International Conference on Robotics and Automation (ICRA), Paris, France: IEEE, May 2020, pp. 1888–1895. doi: 10.1109/ICRA40945.2020.9196625.
[6]
F. Cazenave, Y. Zhang, E. McPhee-Shaw, J. G. Bellingham, and T. P. Stanton, “High-resolution surveys of internal tidal waves in Monterey Bay, California, using an autonomous underwater vehicle: AUV surveys of internal tidal waves,” Limnology and Oceanography: Methods, vol. 9, no. 12, pp. 571–581, Dec. 2011, doi: 10.4319/lom.2011.9.571.
[7]
O. M. Cheriton, E. E. McPhee-Shaw, W. J. Shaw, T. P. Stanton, J. G. Bellingham, and C. D. Storlazzi, “Suspended particulate layers and internal waves over the southern Monterey Bay continental shelf: An important control on shelf mud belts?: Suspended Particulate Layers,” Journal of Geophysical Research: Oceans, vol. 119, no. 1, pp. 428–444, Jan. 2014, doi: 10.1002/2013JC009360.
[8]
S. Kemna, D. A. Caron, and G. S. Sukhatme, “Adaptive informative sampling with autonomous underwater vehicles: Acoustic versus surface communications,” in OCEANS 2016 MTS/IEEE Monterey, Monterey, CA, USA: IEEE, Sep. 2016, pp. 1–8. doi: 10.1109/OCEANS.2016.7761128.
[9]
MBARI et al., “Climate Variability and Change: Response of a Coastal Ocean Ecosystem,” Oceanography, vol. 30, no. 4, pp. 128–145, Dec. 2017, doi: 10.5670/oceanog.2017.429.
[10]
MBARI et al., “Climate Variability and Change: Response of a Coastal Ocean Ecosystem,” Oceanog, vol. 30, no. 4, pp. 128–145, Dec. 2017, doi: 10.5670/oceanog.2017.429.
[11]
D. Pastrana, “THE EFFECTS OF SHOALING INTERNAL TIDES ON BENTHIC EXCHANGE EVENTS AND NEAR-BOUNDARY MIXING ALONG THE CONTINENTAL SHELF.” Jun. 2013. [Online]. Available: https://apps.dtic.mil/sti/pdfs/ADA584685.pdf
[12]
M. J. Stanway et al., “White shark strike on a long-range AUV in Monterey Bay,” IEEE, May 2015, pp. 1–7. doi: 10.1109/OCEANS-Genova.2015.7271726.
[13]
N. K. Truelove et al., “Expanding the temporal and spatial scales of environmental DNA research with autonomous sampling,” Environmental DNA, vol. 4, no. 4, pp. 972–984, Jul. 2022, doi: 10.1002/edn3.299.
[14]

## Slide 50: LRAUV Science Publications 2/3
W. Ussler et al., “Underway measurement of cyanobacterial microcystins using a surface plasmon resonance sensor on an autonomous underwater vehicle,” Limnology & Ocean Methods, vol. 22, no. 9, pp. 681–699, Sep. 2024, doi: 10.1002/lom3.10627.
[15]
K. M. Yamahara et al., “In situ Autonomous Acquisition and Preservation of Marine Environmental DNA Using an Autonomous Underwater Vehicle,” Frontiers in Marine Science, vol. 6, Jul. 2019, doi: 10.3389/fmars.2019.00373.
[16]
Yanwu Zhang, J. G. Bellingham, M. A. Godin, and J. P. Ryan, “Using an Autonomous Underwater Vehicle to Track the Thermocline Based on Peak-Gradient Detection,” IEEE Journal of Oceanic Engineering, vol. 37, no. 3, pp. 544–553, Jul. 2012, doi: 10.1109/JOE.2012.2192340.
[17]
D. R. Yoerger et al., “Mesobot: An Autonomous Underwater Vehicle for Tracking and Sampling Midwater Targets,” in 2018 IEEE/OES Autonomous Underwater Vehicle Workshop (AUV), Porto, Portugal: IEEE, Nov. 2018, pp. 1–7. doi: 10.1109/AUV.2018.8729822.
[18]
Y. Zhang et al., “Thermocline tracking based on peak-gradient detection by an autonomous underwater vehicle,” in OCEANS 2010 MTS/IEEE SEATTLE, Seattle, WA, USA, Sep. 2010, pp. 1–4. doi: 10.1109/OCEANS.2010.5664545.
[19]
Y. Zhang, J. G. Bellingham, J. P. Ryan, and M. A. Godin, “Evolution of a physical and biological front from upwelling to relaxation,” Continental Shelf Research, vol. 108, pp. 55–64, Oct. 2015, doi: 10.1016/j.csr.2015.08.005.
[20]
Y. Zhang, J. G. Bellingham, J. P. Ryan, B. Kieft, and M. J. Stanway, “Autonomous Four-Dimensional Mapping and Tracking of a Coastal Upwelling Front by an Autonomous Underwater Vehicle: AUV 4D Mapping and Tracking of Upwelling Front,” Journal of Field Robotics, vol. 33, no. 1, pp. 67–81, Jan. 2016, doi: 10.1002/rob.21617.
[21]
Y. Zhang, M. A. Godin, J. G. Bellingham, and J. P. Ryan, “Using an Autonomous Underwater Vehicle to Track a Coastal Upwelling Front,” IEEE Journal of Oceanic Engineering, vol. 37, no. 3, pp. 338–347, Jul. 2012, doi: 10.1109/JOE.2012.2197272.
[22]
Y. Zhang, M. A. Godin, B. Kieft, B.-Y. Raanan, J. P. Ryan, and B. W. Hobson, “Finding and Tracking a Phytoplankton Patch by a Long-Range Autonomous Underwater Vehicle,” IEEE J. Oceanic Eng., vol. 47, no. 2, pp. 322–330, Apr. 2022, doi: 10.1109/JOE.2021.3122195.
[23]
Y. Zhang, B. W. Hobson, B. Kieft, M. A. Godin, T. Ravens, and M. Ulmgren, “Adaptive Zigzag Mapping of a Patchy Field by a Long-Range Autonomous Underwater Vehicle,” IEEE J. Oceanic Eng., vol. 49, no. 2, pp. 403–415, Apr. 2024, doi: 10.1109/JOE.2023.3338694.
[24]

## Slide 51: LRAUV Science Publications 3/3
Y. Zhang et al., “Persistent Sampling of Vertically Migrating Biological Layers by an Autonomous Underwater Vehicle Within the Beam of a Seabed-Mounted Echosounder,” IEEE Journal of Oceanic Engineering, pp. 1–12, 2020, doi: 10.1109/JOE.2020.2982811.
[25]
Y. Zhang et al., “Using a long‐range autonomous underwater vehicle to find and sample harmful algal blooms in Lake Erie,” Limnology & Ocean Methods, vol. 22, no. 7, pp. 473–483, Jul. 2024, doi: 10.1002/lom3.10621.
[26]
Y. Zhang et al., “Coordinated and Collaborative Sampling by Two Long-Range Autonomous Underwater Vehicles,” IEEE J. Oceanic Eng., vol. 49, no. 4, pp. 1371–1382, Oct. 2024, doi: 10.1109/JOE.2024.3408889.
[27]
Y. Zhang et al., “Tracking and sampling of a phytoplankton patch by an autonomous underwater vehicle in drifting mode,” in OCEANS’15 MTS/IEEE Washington, Oct. 2015, pp. 1–5.
[28]
Y. Zhang et al., “Isotherm Tracking by an Autonomous Underwater Vehicle in Drift Mode,” IEEE Journal of Oceanic Engineering, pp. 1–10, 2016, doi: 10.1109/JOE.2016.2625058.
[29]
Y. Zhang, R. S. McEwen, J. P. Ryan, and J. G. Bellingham, “Design and Tests of an Adaptive Triggering Method for Capturing Peak Samples in a Thin Phytoplankton Layer by an Autonomous Underwater Vehicle,” IEEE Journal of Oceanic Engineering, vol. 35, no. 4, pp. 785–796, Oct. 2010, doi: 10.1109/JOE.2010.2081031.
[30]
Y. Zhang et al., “Autonomous Tracking and Sampling of the Deep Chlorophyll Maximum Layer in an Open-Ocean Eddy by a Long-Range Autonomous Underwater Vehicle,” IEEE Journal of Oceanic Engineering, pp. 1–14, 2020, doi: 10.1109/JOE.2019.2920217.
[31]
Y. Zhang, J. P. Ryan, J. G. Bellingham, J. B. J. Harvey, and R. S. McEwen, “Autonomous detection and sampling of water types and fronts in a coastal upwelling system by an autonomous underwater vehicle: AUV sampling across an upwelling front,” Limnology and Oceanography: Methods, vol. 10, no. 11, pp. 934–951, Nov. 2012, doi: 10.4319/lom.2012.10.934.
[32]
Y. Zhang et al., “A system of coordinated autonomous robots for Lagrangian studies of microbes in the oceanic deep chlorophyll maximum,” Sci. Robot., vol. 6, no. 50, p. eabb9138, Jan. 2021, doi: 10.1126/scirobotics.abb9138.
[33]
Y. Zhang et al., “Targeted Sampling by Autonomous Underwater Vehicles,” Frontiers in Marine Science, vol. 6, Aug. 2019, doi: 10.3389/fmars.2019.00415.
[34]
Y. Zhang et al., “Autonomous Tracking of Salinity-Intrusion Fronts by a Long-Range Autonomous Underwater Vehicle,” IEEE J. Oceanic Eng., vol. 47, no. 4, pp. 950–958, Oct. 2022, doi: 10.1109/JOE.2022.3146584.

## Slide 52: LRAUV Engineering Publications 1/2
[1]
J. G. Bellingham et al., “Efficient propulsion for the Tethys long-range autonomous underwater vehicle,” in 2010 IEEE/OES Autonomous Underwater Vehicles, Monterey, CA, USA, Sep. 2010, pp. 1–7. doi: 10.1109/AUV.2010.5779645.
[2]
A. Branch et al., “Demonstration of Autonomous Nested Search for Local Maxima Using an Unmanned Underwater Vehicle,” in 2020 IEEE International Conference on Robotics and Automation (ICRA), Paris, France: IEEE, May 2020, pp. 1888–1895. doi: 10.1109/ICRA40945.2020.9196625.
[3]
D. M. Pargett, J. M. Birch, C. M. Preston, J. P. Ryan, Y. Zhang, and C. A. Scholin, “Development of a mobile ecogenomic sensor,” in OCEANS 2015 - MTS/IEEE Washington, Oct. 2015, pp. 1–6.
[4]
M. A. Godin, J. G. Bellingham, B. Kieft, and R. McEwen, “Scripting language for state configured layered control of the Tethys long range autonomous underwater vehicle,” in OCEANS 2010 MTS/IEEE SEATTLE, Seattle, WA: IEEE, Sep. 2010, pp. 1–7. doi: 10.1109/OCEANS.2010.5664515.
[5]
B. W. Hobson, J. G. Bellingham, B. Kieft, R. McEwen, M. Godin, and Y. Zhang, “Tethys-class long range AUVs - extending the endurance of propeller-driven cruising AUVs from days to weeks,” IEEE, Sep. 2012, pp. 1–8. doi: 10.1109/AUV.2012.6380735.
[6]
B. W. Hobson et al., “An Autonomous Vehicle Based Open Ocean Lagrangian Observatory,” in 2018 IEEE/OES Autonomous Underwater Vehicle Workshop (AUV), Porto, Portugal: IEEE, Nov. 2018, pp. 1–5. doi: 10.1109/AUV.2018.8729719.
[7]
B. Kieft et al., “Fault Detection and Failure Prevention on the Tethys Long-Range Autonomous Underwater Vehicle,” Unmanned Untethered Submersible Technology Conference, Aug. 2011.
[8]
A. L. Kukulya, J. G. Bellingham, J. W. Kaeli, C. M. Reddy, M. A. Godin, and R. N. Conmy, “Development of a propeller driven long range autonomous underwater vehicle (LRAUV) for under-ice mapping of oil spills and environmental hazards: An Arctic Domain Center of Awareness project (ADAC),” in 2016 IEEE/OES Autonomous Underwater Vehicles (AUV), Tokyo, Japan: IEEE, Nov. 2016, pp. 95–100. doi: 10.1109/AUV.2016.7778655.
[9]
D. M. Pargett, J. M. Birch, C. M. Preston, J. P. Ryan, Y. Zhang, and C. A. Scholin, “Development of a mobile ecogenomic sensor,” in OCEANS 2015 - MTS/IEEE Washington, Washington, DC: IEEE, Oct. 2015, pp. 1–6. doi: 10.23919/OCEANS.2015.7404361.
[10]
MBARI et al., “The Quest to Develop Ecogenomic Sensors: A 25-Year History of the Environmental Sample Processor (ESP) as a Case Study,” Oceanography, vol. 30, no. 4, pp. 100–113, Dec. 2017, doi: 10.5670/oceanog.2017.427.
[11]

## Slide 53: LRAUV Engineering Publications 2/2
T. R. Player et al., “From Concept to Field Tests: Accelerated Development of Multi-AUV Missions Using a High-Fidelity Faster-than-Real-Time Simulator,” in 2023 IEEE International Conference on Robotics and Automation (ICRA), London, United Kingdom: IEEE, May 2023, pp. 3102–3108. doi: 10.1109/ICRA48891.2023.10160447.
[12]
B. Y. Raanan et al., “A real-time vertical plane flight anomaly detection system for a long range autonomous underwater vehicle,” in OCEANS 2015 - MTS/IEEE Washington, Washington, DC: IEEE, Oct. 2015, pp. 1–6. doi: 10.23919/OCEANS.2015.7404462.
[13]
B.-Y. Raanan et al., “Automatic fault diagnosis for autonomous underwater vehicles using online topic models,” in OCEANS 2016 MTS/IEEE Monterey, Monterey, CA, USA: IEEE, Sep. 2016, pp. 1–6. doi: 10.1109/OCEANS.2016.7761139.
[14]
B.-Y. Raanan et al., “Detection of unanticipated faults for autonomous underwater vehicles using online topic models,” Journal of Field Robotics, vol. 35, no. 5, pp. 705–716, Aug. 2018, doi: 10.1002/rob.21771.
[15]
Q. Shemet, M. Anderson, Y. Zhang, B. Kieft, and B. Hobson, “Binary Range Control for Multi-Vehicle AUV Operations: Field Validation of a Minimalist Approach,” in OCEANS 2025 Brest, BREST, France: IEEE, Jun. 2025, pp. 1–8. doi: 10.1109/OCEANS58557.2025.11104340.
[16]
M. J. Stanway, B. Kieft, T. Hoover, B. Hobson, A. Hamilton, and J. Bellingham, “Acoustic tracking and homing with a long-range AUV,” IEEE, Sep. 2014, pp. 1–7. doi: 10.1109/OCEANS.2014.7003277.
[17]
T. C. O’Reilly, B. Kieft, and M. Chaffey, “Communications relay and autonomous tracking applications for Wave Glider,” in OCEANS 2015 - Genova, May 2015, pp. 1–6. doi: 10.1109/OCEANS-Genova.2015.7271243.

## Slide 54: User Interface Web-based Command and Control GUI
Mission programming: Preloaded on AUV; Select and send parameters over the horizon; GUI visualizations; Safety envelops protect the vehicle
LRAUV state visualization
Point and click waypoints
Real-time data access
Portal to logs, checklists and configs
Seamless communications switching: Cellular, Satellite, Acoustic
Pilot-in-Charge schedule and log

## Slide 55: TethysDash System LRAUV Command and Control Interface
TethysDash
Server/Backend
Dash UI
Dash V4
Dash V5
TrackDB
Situational Awareness
Other assets
Notes: Continuous Stream of Improvements:
  Enhanced Command & Mission Control
  Full support for TethysL mission scripts
  Improved "Send via" options with configurable timeouts
  Command queue management with cancellation ability

## Slide 56
User Interface
  Migrating to Dash 5
Data
  Quick look within the Dash
  Quick plots with Data Vis
  Monique’s Automated Quick-look
  Stoqs
Software tools to continue to ease end user burden of vehicle deployment preparation

## Slide 57: Vehicle Simulator Desktop Development
Open Robotics Gazebo Simulator
Modular plug-in based
~100x faster than real-time
High fidelity vehicle dynamics
Simultaneous multi-vehicle sims
Sensor Plug-ins: CTD, Chl, DVL, Acoustic Modem
World Plug-ins: 1m Resolution Seafloor DEMs; 3-D Water Column parameters;
4-D ROMs Models

## Slide 58: Open Architecture Easy 3rd Party Integration
Backseat Computer (BSC) Architecture: High performance computers; 3rd party applications; High-rate sensors; Machine learning
Front-seat API – Open source LCM Protocol
Access to all control inputs and sensor outputs
All vehicle safety envelopes remain
NVIDIA Nano BSC
Multi-vehicle Coordination
Backseat Computer
Backseat Application
Network Interface
TETHYS LCM* API
Main LRAUV Application
Simulation
Host
LRAUV
Main Computer
Hardware
Software
COMMANDS
DATA

## Slide 59: Missions Remote, Ship-less Operations
1 Month Continuous Operations – primary batteries
Ship-less operations – Pier launch/recovery – No on-site support
Two LRAUVs + ESP + SPR (real-time toxin detection)
Autonomous patch tracking to find 3D location of sub-surface peak chlorophyll signal
Archived 85 samples of filtrate from ~ one liter seawater samples
Post sample, near real-time analysis to measure concentration of HAB toxin, Domoic Acid
850 km on one 450 km on the second
Goleta Pier Launch/Recovery
HAB peaks at 20m depth
CHALLENGE: Locate Harmful Algal Blooms, locate peak signals and monitor for toxins

## Slide 60: Missions Remote Mapping
AUV Mapping Data
Low-power Transit - 400 km
Round Trip
10 watts @ 2km/hr, ~2kW-hr, 4 days each way
High-power Mapping
100 km of Mapping for 24 hours @ 100 watts @ 4km/hr, ~2.5 kW-hr
Power up and align IxBlue C3 INS on-site
Power up and log Norbit WBMS high res multibeam sonar
CHALLENGE: Seafloor mapping of remote shelf break

## Slide 61
From: Camilli, R., & Duguid, Z. (2020). Improving resource management for unattended observation of the marginal ice zone using autonomous underwater gliders. Frontiers in Robotics and AI, 7, 184.