## Slide 1: AUV Docking Persistent Operations
Proven design with thousands of offshore docks
All acoustic homing for operation in low visibility ocean water
Omni-Directional design works with ocean currents – AUV swims into current
Niobicon sliding contact power transfer: 500 Watts
Collaboration and patented with Northrop Grumman
1+ Mbps data transfer, plus acoustic modem backup
Web-based dock control interface with live video, lights, DAQ,
Optional surface expression for solar/wave energy harvesting and RF comms
Or use stand-alone seafloor battery/fuel cell, or seafloor cable
Surface buoy with Solar Energy Harvesting
AUV Parked on Dock
Video – Homing to dock

## Slide 2: AUV Docking Components
Capture Arm (open)
Payload Protector
Deflector
Linear Actuator
Power Transfer Brushes (3)
Dock Detector Sensor
(Not shown)
Power Transfer/comms Electronics Can

## Slide 3: AUV Docking Dock - Subsea Interface
Power Transfer
Voltage and Current
Dock Relay Control
Acoustic Modem
Console
Live Video, with Light

## Slide 4: AUV Docking Dock – Topside by Victron
Dock Ground Fault Monitor
Power Harvesting and Consumption History
Dashboard
Dock Energy Storage History