## Slide 1: State of Homing

## Slide 2: Where Are We Now?
Nov 2023: Dock/miss ratio was 1 in 6.
Objective: Do better.
Jan 2024: Hit miss ratio was 1 in 3.
Progress due to several incremental fixes.

## Slide 3: Fixes So Far:
Fixed rangeClosing()
PP was latching the last dock location 2 m out, needed 10.
Corrected median filter initialization to eliminate delay.
Integrator windup now correctly handled.
Bandwidth/gains increased (not finished).
Vehicle consistently approaching up-current (not tested at sea yet)

## Slide 4: Remaining Problems and Questions:
Dock “walks” as vehicle approaches (why)?
Why does the vehicle hook and the end?
What is the size of the point spread?
  Masked by the median filter

## Slide 5: 1. Dock Walk: Data
12 Jan run:
  Dock usually walks in the direction of the turn.
  20240112T171341. 7-10% DT
  20240112T042707. 3-9% DT
Show data:

## Slide 6: Tethys Log: Down/Cross Current

## Slide 7: Tethys Log: Up current

## Slide 8: Tethys Log: Down/Cross Current with Dock

## Slide 9: 2. Hook at the End:
d =1 m
R=100 m, = .01 = .57 deg.
R=10 m, = .1 = 5.7 deg.
r

## Slide 10: What is Causing Dock Walk?
Simulate Sensor and Navigation Error:
DAT: range & misalignment.
DAT: delay.
Nav: yaw delay.
Nav: Dvl velocity scale factor.

## Slide 11: Dock Walk: Simulation Results
50% lateral Dvl:
  Dvl possibly has nonlinearity around zero.
  Northerly Start: 20240312T213652.
  Southerly Start: 20240312T182612.
Show data:

## Slide 12: Docking Simulation - Cross Current

## Slide 13: Docking Simulation – Up Current

## Slide 14: 1. Proposed Solutions:
Feed DAT bearing directly into PN/PP:
  Eliminates Nav error source.
  Expect better performance in one-way mode.
  May need filtering.
  How to latch bearing 10 meters out?
Use Buoy Location to Reset Nav:
  May need additional filter/estimator.
  Suited to simulation.

## Slide 15: 3. Point Spread: Two Ways
Use Radii
Use Lateral Distance

## Slide 16: Tethys Log: Down/Cross Current with Dock

## Slide 17: Tethys Log: Down/Cross Current with Dock

## Slide 18: To Do:
Implement bearing-only control with switch.
  Latch filtered bearing at 10 meters out.
Implement dock-referenced nav updates with switch.
Simulate docks with higher bandwidth control.
  Larger fins.
Fix gain scheduling to resume original gains after rollout.
Note: All of the above well suited to simulation!

## Slide 19: End

## Slide 20: Navigation Error
Consider last 10 meters:
  Assume nav error = 2% DT.
  10 * .02 = 20 cm.
  Aperture center is offset to the arm side ~15 cm.
  Vehicle aperture = (+ 39, -9 ) cm, 48 cm edge-to-edge.
  9/20 = 45% or about 1 in 2 on the left side.

## Slide 21: Causes: Homing Error Sources in H Plane
Sensor error – DAT
  How is SOS set?
  Roll angle
Navigation error
Latency in homing loop
PN algorithm
Bugs in code
  Median reset bug
  One-way bug(?)
Dock motion – watch circle
  How fast can it move?
More?

## Slide 22: Nav and Sensor Error
Simple kinematic simulation.
All error sources removed except nav and sensor.
Pure pursuit control assumed perfect.

## Slide 23: Supplementary Information
Reynolds:
  1 m/s => Re = 1.42e6
  .35 m/s => Re = 4.98e5