## Slide 1: The Problem:
Homing: Hit miss ratio is 1 in 6.

## Slide 2: Causes: Homing Error Sources in H Plane
Sensor error – DAT
  How is SOS set?
  Roll angle
Navigation error
Latency in homing loop
PN algorithm
Bugs in code
  Median reset bug
  One-way bug(?)
Dock motion – watch circle
  How fast can it move?
More?

## Slide 3: Navigation Error
Consider last 10 meters:
  Assume nav error = 2% DT.
  10 * .02 = 20 cm.
  Aperture center is offset to the arm side ~15 cm.
  Vehicle aperture = (+ 39, -9 ) cm, 48 cm edge-to-edge.
  9/20 = 45% or about 1 in 2 on the left side.

## Slide 4: Nav and Sensor Error
Simple kinematic simulation.
All error sources removed except nav and sensor.
Pure pursuit control assumed perfect.

## Slide 5: Conclusion
Task: Debug Pure Pursuit. (Rob + ?)

## Slide 6: End

## Slide 7: Supplementary Information
Reynolds:
  1 m/s => Re = 1.42e6
  .35 m/s => Re = 4.98e5