## Slide 1: R/V Paragon Status Report
Jared Figurski
9/06/16

## Slide 2: Overview
CTD Hydraulic Winch
Hydraulic System Upgrade
  Specifications
  Status
  Plan
Towing Setup
  Engine Guard
  T-Bar
Underway CTD
Paragon Plans

## Slide 3: Hydraulic CTD overview
The CTD and Carousel will be stored on the deck, behind the boat driver seat
They will be deployed using the Paragon’s boom (500 lb load rating).
After being lowered in the water, the load will be transferred to the CTD boom and released with a quick release shackle

## Slide 4: The winch
780 lb, including cable
Aluminum frame
Level winder
1000m long, 3/8” cable
Cable weight: 223lb in air, 42lb in water.
Break strength 2400 lb
Speed 45-70 m/min
Load cap.: 470 lb bare drum, 300 lb full drum
6 gpm @1500 PSI

## Slide 5: Requirements for winch attachment
The winch must be securely attached to the deck to handle all sea states the Paragon operates in.
The winch can be attached and detached easily by two operators, using 1000 lb rated MBARI dock davit, and basic tools.
Hardware and required tools must be kept to a minimum
Winch must be positioned so the aft hold covers are accessible and so operators can move around it easily

## Slide 6: Suggested attachment design
-Two stainless steel plates are bolted to the bulkheads inside the hold
- 2” long coupling nuts are welded to the plates

## Slide 7: Suggested attachment design
Stainless steel frame is bolted on top of the hold covers.
4 holes in hold covers allows frame to be bolted. Can be bolted to LARS bar also.
Frame material: 2”x2”x3/16” SS
10 threaded holes welded to frame.
Weight: 74lb

## Slide 8: Suggested attachment design
Winch is lowered with dock davit and bolted to frame using 4 5/8” bolts.
Winch can be oriented to port or starboard, depending on operators need.

## Slide 9: CTD Boom Specifications
Deploy CTD or SBE 32 Carousel
  300 lb in air when full
  28” diameter x 38” tall
300 lb working load rating
5 to 1 safety factor for vertical pull and up to 45o from vertical pull.

## Slide 10: CTD boom features
316 Stainless steel tubing:
  2x2x3/16” for support frame
  2.5x2.5x1/4” inner boom
  3x3x3/16” for outer boom
UHMW bearings for telescoping boom
Handles for actuation
Recommended wire layout respected
4 locations for pin on the boom (0” to 24”)
Tie down for block to prevent motion during transit (TBD)

## Slide 11: Winch/ Boom Combination
Hydraulic whips
Deck Box cable

## Slide 12: Hydraulic System
Aft Capstan
Boom Capstan
Anchor Winch
CTD winch bulkhead

## Slide 13: Schematic
Scott Harlan, P.E. Mechanical Engineer Consultant
Rear Capstan
Boom Capstan
Anchor Winch
Reservoir
Motor/Pump
CTD winch bulkhead

## Slide 14: Hydraulics Specifications
  Motor (Honda GX390) w/ Electric Start
  11 hp Four Stroke
  Onboard Fuel and plumbing option
Pressure Compensated Pump
  8 GPM @ 1500 PSI (spec’ed for winch)
Reservoir – 20 Gal custom design
Plumbing – 3000 PSI (pressure ½”,return 5/8”)
    No drip QR fittings for CTD winch
    Hardlines inside cabin

## Slide 15: Hydraulics Status

## Slide 16: Hydraulics Status
Valves and pump painted
Old System Removed
Aft compartment cleaned and resurfaced
Motor, Filter and Manifold mounted to base plate
Pump mount machined to change orientation
Reservoir is built
Plan for install
Iterative ordering of connectors and parts
Custom motor exhaust fitting

## Slide 17: Hydraulics Plan
Installation- September 8 & 12-15 reserved
  Install
    Pump
    Reservoir
    Manifold
    Filter
    Valves
    Bulkhead Fittings
  Plumb
    Soft Lines
    Hard Lines

## Slide 18: Towing Setup
Regular AUV tow outs
Mooring recoveries
Vessel towing
Easily Removable
Lightweight
Strong

## Slide 19: Towing Setup
Larry has drawn a plan but doesn’t have time to follow up
Sanctuary Stainless booked through October
Francois on paternity leave

## Slide 21: Plans
V-berth redesign and cushions
Roof storage
Replace wiper motors
Clothes hooks
Logo and striping
Wiring cleanup
Fuel tank inspections
Directional VHF – AUV group spec
Mast repairs and Antennae Installation
Transducer pole modifications
Aft Capstan Roller design
Repair Anchor winch bearings
Freshwater Pump/ heater
Paragon Container
Dock Box for Survival Suits
Open ROV

## Slide 22
END

## Slide 23: FEA : displacement
Max displacement = 0.5”

## Slide 24: Structural analysis
FEA and calculations were performed for 1500lb (FEA results and calculations provided).
Vertical pull:
  Maximum stress in inner tube = 29400 PSI
  Maximum stress in outer tube 22600 PSI.
45o pull:
  Maximum stress in inner tube = 36800 PSI (too high?)
  Maximum stress in outer tube= 29600 PSI.
Wall thickness can be increase for inner tube. Max design load can be reduced for 45o pull. YS must be determined more accurately.
Stresses in the rest of the frame are below 20000 PSI. Bearings and attachment will be designed with same factor of safety.

## Slide 25: FEA : Stress
Max stress in inner boom = 29400PSI

## Slide 27: Block for CTD wire
Required minimum diameter: 15”
MBARI owns a sheave that we can used
Cheeks and attachment can be manufactured easily
3/8” shackle
Opening large enough for wire termination

## Slide 28: CTD boom features
If space is needed on the deck, the boom can be rotated and stored on top of the winch.

## Slide 29
Motor w/out controls
Wrong valve style
Valve not detent
Wrong Connectors
Missing Connectors