## Slide 1: GeoSense DAS Cable Design Review
Mechanical Engineering Team Review

## Slide 2: GeoSense Project Concept
Use Distributed Acoustic Sensing (DAS) to study marine sediment flows.

## Slide 3: GeoSense Project Concept
sea-level

## Slide 4: Review Goal
We have specified requirements for a cable (coming up in next slides)
We have solicited designs from 8 different manufacturers
Our goal today is to review the submitted designs /cable constructions toward the ultimate goal of selecting and purchasing our cable
We have our preference but would like your experienced opinions to confirm our selections
Due to the deployment strategy the cable is a critical part of the system design

## Slide 5: Deployment and Recovery Concept : The Paull Plan
Factors influencing cable survivability:
Weight of Electronics Package
Sea-state Conditions
Peak Loads (Heave Loads)
Currents in the water column
Current Vectors in the water column
R/V D. Packard's Dynamic Positioning

## Slide 6
Deployable from R/V David Packard using the existing MacArtney winch
Electronics package will be connected to 1km of armored fiber optic cable
Cable must be used to lower and recover electronics package
Location- A bench along Monterey Canyon ~390 meters depth
Payout the1km cable in a straight-ish line
Cable Requirements During Deployment

## Slide 7: Geo-Sense Preliminary Design
Instrument Package (Current Configuration)
Desired wet weight of 300 lbs.(~140 Kg)
Deployment Location:
Upper Canyon ~300 m

## Slide 8: Cable design – Simulation Results
Used DSA Oceans Proteus mooring simulation software used to estimate the load specifications for the DAS cable. A comparable cable (weight per meter) was used to simulate the strain in different sea states.
Electronics Package Data
Cable Data

## Slide 9: Simulations Results – 3m Wave Height/9 sec period

## Slide 10: Simulation Results – 2 m Wave Height/ 2 sec period

## Slide 11: Mechanical Requirements Submitted to Vendors
Armored Cable
Double wrap torque balanced galvanized steel wire
Minimum breaking strength ≥ 50kN
Outer Sheath (Polyethylene or Polyurethane)
Separate layer to make breaking out the fibers easier
Bend Radius
The winch that MBARI currently uses and has the capacity for 1km of cable is a MacArtney winch(Model No.*******) with a drum radius of 0.3 meters
Weight in Sea water
Cable weight ≥ .320 kg/m (negatively buoyant)
Other Desired Characteristics
Fiber breaking cable load ≥ 20kN
OD of Cable ≥ 15mm
Excess fiber in tube 0.1 - 0.3%
SWD minimum 2000m
Length 1000m

## Slide 12: Cable Options
We requested cable designs and quotes from over 8 companies including:
  Southbay, Winchester (Falmat), Rochester, Seven Valleys (Cortland), Hydrogroup, Concept Cables, Nova Cavi, Birns
  A couple quotes had prices or lead times that are not feasible for us- in one case we still don’t have a quote

## Slide 13: Concept Cables

## Slide 14: Hydrogroup

## Slide 15: Rochester

## Slide 16: Seven Valleys

## Slide 17: South Bay

## Slide 18: Winchester - Falmat

## Slide 19
Cable Characteristics | Hydrogroup Cable Characteristics | Hydrogroup Rank | Southbay Cable Characteristics | Southbay Rank | Winchester Cable Characteristics | Winchester Rank
Ultimate Breaking Strength | 50kN | 3 | 50kN | 3 | 50kN | 3
Working Load | 10kN | 2 | 12.5kN | 2 | 12.5kN | 2
Working Load Safety factor | 2.27 |  | 2.84 |  | 2.84 | 
Dynamic Bend Radius | 12 | 3 | 10 | 4 | 8 | 4
Density | 2.43 |  | 2.117 |  | 2.97 | 
Specific Gravity(Sea water) | 2.37 |  | 2.06 |  | 2.89 | 
Weight in Sea Water | 0.254 |  |  |  | 0.247 | 
Depth Rating(PSI) | 2500 |  | 5330 |  | 4350 | 
Torque Balanced (Y=2/N=1) | Yes | 0 | Yes | 0 | Yes | 0
Pull Test (Y=2/N=1) | No | 0 |  |  |  | 
Cost | $26K | 4 | $30k | 3 | $31k | 3
Lead time (Weeks) | 14-15 |  | 30-34 |  | 16-18 | 
Shipping Cost (International=2/Domestic=1) | International | 1 | Domestic | 2 | Domestic | 2
Rank |  | 13 |  | 14 |  | 14

## Slide 20
Cable Characteristics | Seven Valleys Cable Characteristics | Seven Valleys Rank | Rochester Cable Characteristics | Rochester Rank | Concept Cable Characteristics | Concept Cable Rank
Ultimate Breaking Strength | 60kN | 4 | 67kN | 5 | 80kN | 5
Working Load | 20kN | 5 | 21kN | 5 | 26.5kN | 5
Working Load Saftey factor | 4.5 |  | 4.8 |  | 6 | 
Dynamic Bend Radius | 12 | 3 | 12 | 3 | 11 | 3
Density | 2.9 |  | 3.12 |  | 3.03 | 
Specific Gravity(Sea water) | 2.82 |  | 3.04 |  | 2.945 | 
Weight in Sea Water | 0.27 |  | 0.37 |  | 0.377 | 
Depth Rating(PSI) | n/a |  | n/a |  | 4350 | 
Torque Balanced (Y=2/N=1) | Yes | 0 | Yes | 0 | Yes | 0
Pull Test (Y=2/N=1) | No | 0 |  |  |  | 
Cost | $43k | 2 |  |  | $24.3k | 4
Lead time (Weeks) | 14-15 |  |  |  |  | 
Shipping Cost (International=2/Domestic=1) | Domestic | 2 | Domestic | 2 | International | 1
Rank |  | 16 |  | 15 |  | 18

## Slide 21
DSA Oceans
Proteus Mooring Simulation Software
Results
Used the Proteus cable directory to simulate a comparable cable with similar (weight per meter)
Simulated E-Package …

## Slide 22
DSA Oceans
Proteus Mooring Simulation Software
Results(continued)

## Slide 23: MatLAB Analysis
Still a work in progress:

## Slide 24: Responses Of Different Sea-States
1M
2M
3M
4M

## Slide 25
Electronics Frame Dimensions

## Slide 26
Using the “diggers” to pick up the frame and place in the water
A-frame will lower frame to bottom using center sheave
SWL of center sheave is 6 tonne
Sheave Clearance ~20 ft