## Slide 1: Electrical Design
DAS Onyx Nano Specification
System Power, Data, and Communications
System Interconnects
Fiber Optic Connection

## Slide 2: DAS Details – Onyx Nano
Modification to commercial product in development
Preliminary design specifications:
  Fiber Range: 10 km
  Spatial Resolution: 2 m (possibly 1 m)
  Noise floor: Approx. -63 dB rad.Hz–½
  Acq. Sample Rates: 10, 20, 50 kHz
  O/P Sample Rate: 500 Hz, 1 kHz, 2 kHz
  Weight: c. 5 kg
  Dimensions: c. 300 x 200 x 75 mm
  Operating Temp: -10 °C to 50 °C
  Power: 20 V – 60 V DC, 40 W
  External I/O: 1 x 1 Gb Copper LAN
  Software ONYX standard SW

## Slide 3: Power Budget
DAS should run directly from 28 V main battery, so no DC-DC loss
Sintela estimates “less than 40 W” for DAS
Using waste heat from FPGA to warm laser, which must be kept at 25 degC
We will have 30 kWh of Li primary batteries
Batteries would last 31 days at 40 W, 42 days at 30 W
DAS will operate down to ~20 V, by which time the batteries are completely depleted

## Slide 4: Data Budget
At 200 Hz sampling with 2 m channel pitch, system will record 17.3 GB per day
In 42 days, this would be 727 GB, easily stored on a 1 TB SSD
Sintela is investigating the cost and power of adding a redundant SSD
System power only increases by ~1.5 W while recording, so not worth it to use triggered sampling to save on storage and possibly miss events

## Slide 5: Communications
Underwater comms during deployment provided by field-proven Deepsea Connect
Deck cable will provide power to DAS and DSC, and DSC will provide WiFi connectivity to DAS
Data offload can be done through DSC port on DAS sphere with hardwired GbE
Fallback for data offload is to open DAS sphere

## Slide 6
Electrical Interconnects