## Slide 1
Seasats Lightfish
Open Ocean Robotics DataXplorer
Liquid Robotics Wave Glider
PURCHASE REVIEW · OCTOBER 1, 2026
MBARI New ASV
Selecting a Autonomous Surface Vehicle
Erik Trauschke, Brian Kieft, Chris Wahl, Quinn Shemet

## Slide 2: History
Current fleet is obsolete
We currently have 3 Wave Glider SV3-200s: obsolete, but still functional.
Maintainability at risk
We have some spare parts, but long-term maintainability is not guaranteed.
Not suited to every use case
Works for current users, but not suitable for some potential users (e.g., mapping).
Requirements gathered from labs
Collected needs from MBARI labs that currently use, or want to use, an ASV.
MBARI's current Wave Glider SV3-200

## Slide 3: Requirements
Payload size, weight & power
90 × 30 × 30 cm (81 L), 30 kg, 120 W max, 2 kWh for payload
Duration
Up to 6 months; main usage under 1 month
Range
Up to 160 nm; main usage under 20 nm
Data needs
A few labs need a high-speed link (20 Mbps); most do not
Vehicle noise
As low as possible to support highly sensitive sonar payloads
Deployments outside Moss Landing
Needed by some labs; platform must ship easily
Self-operated by lab
Most prefer ops by ASO; some want to drive themselves
Maneuverability & speed
Keep up with AUV/glider; boat-less dock launch; consistent mapping speed
Event response
Rapid transit and high maneuverability to respond to events
Vendor relations
Low-level vehicle access needed for some use cases
Ship operations
Deployment / recovery with RV Paragon
Recommendation
To meet most of the requirements:
electric propeller-driven vehicle

## Slide 4: Payload Challenges
Water-property sensors
Most chemical and optical sensors (CTD, CO₂, fluorometer, etc.) work on any vehicle
ANY VEHICLE
Bioacoustics
Requires a low-noise vehicle and high pitch/roll stability
FAVORS WAVE GLIDER
Mapping
Requires maneuverability, consistent speed and enough battery power
PROP-DRIVEN ONLY
ESP
Large payload, likely doesn’t fit the Wave Glider; needs 2 kWh of battery (more if cooling is necessary)
PROP-DRIVEN
Data relay
Requires consistent speed; Wave Glider can barely keep up with LRAUV and would not work for Dorado
PROP-DRIVEN
AUV intervention / deployment / recovery
Needs towing capacity, high speed and high maneuverability
PROP-DRIVEN
Takeaway: only bioacoustics favors the Wave Glider; most other payloads need a prop-driven vehicle

## Slide 5: CHOICE 1 Seasats Lightfish
Hull concept (left) and Lightfish underway (top). Source: Seasats.
3.5 m
Length
4.0 kWh
Li-ion battery
4.5 kn
Sprint speed
6 mo
Endurance
Dimensions | 3.5 × 1.0 m (11.4 × 3.4 ft); 0.8 m draft
Weight | 132 kg base, up to 181 kg fully loaded
Payload | 77 L bay, up to 30 kg
Payload power | 20-30 W steady; bursts to 300+ W
Energy | 4.0 kWh Li-ion battery + 415 W solar (opt. methanol generator)
Speed | 4.5 kn sprint / 2 kn cruise
Range | ~575 nm on battery alone; 6,000+ nm with solar
Propulsion | Electric (Torqeedo, ~3 HP equiv.), weedless prop
Comms | LTE, Iridium SBD/Certus; optional Starlink, MANET
Vendor | Seasats (San Diego, CA)

## Slide 6: CHOICE 2 Open Ocean Robotics DataXplorer
Field assembly (left) and DataXplorer on the water (top). Source: Open Ocean Robotics.
3.7 m
Length
3.5-17.5 kWh
Battery options
6 kn
Max speed
500 nm
Range, max battery
Dimensions | 3.7 × 0.9 m (12.2 × 2.9 ft); 0.5 m draft
Weight | 143 kg (std. battery) to 204 kg (max battery)
Payload | Up to 50 kg
Energy | 3.5 kWh std., expandable to 17.5 kWh; 270 W solar
Speed | 2 kn cruise / 6 kn max
Range | ~100 nm on std. battery; up to 500 nm with max battery
Propulsion | Electric, ~3 HP equivalent
Hull | Patented self-righting design
Comms | 4G cellular, Iridium Certus-100, AIS Class B
Vendor | Open Ocean Robotics (Victoria, BC)

## Slide 7: CHOICE 3 Liquid Robotics Wave Glider SV3-300
Photo: one of MBARI's current Wave Glider SV3-200s.
Wave-driven: not the recommended electric-propeller design
1 yr
Endurance
45 kg
Max payload
1 kn
Typical speed
4.5 kWh
Max battery
Dimensions | 3.05 m float + 2.13 m sub, 4 m umbilical
Weight | ~150 kg (vehicle only)
Payload | Up to 45 kg / 93 L; up to 7 modular bays
Payload power | 5-20 W average; 360 W peak
Energy | 0.9-4.5 kWh battery + 150 W solar
Speed | ~0.8 - 1 kn typical / 3 kn max
Endurance | Up to 1 year at sea
Propulsion | Wave-powered fins + electric thruster backup
Comms | Iridium 9602/RUDICS, cellular option, WiFi, Starlink
Vendor | Liquid Robotics / Boeing (Sunnyvale, CA)

## Slide 8: Comparison of Vehicles
 | Seasats Lightfish | Open Ocean DataXplorer | Liquid Robotics Wave Glider SV3
Length | 3.5 m | 3.7 m | 3.05 m float + 2.13 m sub
Weight | 132-181 kg | 143-204 kg | ~150 kg
Payload | 77 L / up to 30 kg | Up to 50 kg | Up to 45 kg / 93 L
Energy storage | 4.0 kWh + 415 W solar | 3.5-17.5 kWh + 270 W solar | 0.9-4.5 kWh + 150 W solar
Speed | 4.5 kn sprint / 2 kn cruise | 6 kn max / 2 kn cruise | 3 kn max / 0.8 - 1 kn typical
Range / endurance | ~575 nm battery; 6,000+ nm w/ solar | ~100 nm std.; 500 nm max battery | Up to 1 year at sea
Propulsion | Electric propeller | Electric propeller | Wave energy + electric backup
Data link | LTE, Iridium SBD/Certus, Starlink | 4G, Iridium Certus-100 | Iridium 9602, cellular, WiFi, Starlink
Rough cost | ~$300K | ~$300K | ~$300K
Electric propeller (recommended) | ✓ Yes | ✓ Yes | ✕ No (wave-driven)

## Slide 9: Requirements & Feature Matrix
Seasats Lightfish
Open Ocean DataXplorer
Wave Glider SV3
Maneuverability & speed
Station keeping, mapping lines
MEETS
Electric propeller; no issues noted
MEETS
Electric propeller; no issues noted
FAILS
Speed not consistent; can't station keep or run mapping lines
Low noise
Sensitive sonar payloads
RISK
Possibly fails; unknown until payload is integrated
RISK
Possibly fails; unknown until payload is integrated
MEETS
Quiet, wave-driven platform
Payload bay
Must fit the ESP
STRONG
Large, open payload bay
ADEQUATE
Somewhat restricted, but large enough for ESP
WEAK
Small bay; likely can't fit the ESP
Data & user interface
Science data, command & control
GOOD
Good data and user interface
STRONG
Very sophisticated data and user interface
WEAK
Hard science data download; poor C2 user experience
Vendor support
Low-level access & modifications
STRONG
Very strong support for low-level vehicle access
ADEQUATE
Some openness to low-level access
WEAK
Little support beyond what we already do
Event response
Rapid transit to events
MEETS
High speed and agility
MEETS
High speed and agility
FAILS
~1 kn typical; slow to reach events, hard to use for intervention
Stability
Roll / platform stability
MODERATE
Keel improves stability
WEAK
Least roll stability of the three
STRONG
Best stability (glider design)

## Slide 10: Thank you! Questions?
www.mbari.org