## Slide 1: Linduino
Dan Eddleman

## Slide 2: DanTherm Download Reminder
Download DanTherm: https://intranet.linear.com/documents/4570/DanThermBeta001.zip
There’s an mp4 video tutorial inside the zipfile.

## Slide 3: Arduino The “Gateway” IDE?

## Slide 4: Arduino vs Linduino
C/C++ Programmable
Bootloader
Open-source
Add-on “shields”
AC adapter
USB serial port
All of that, plus…
QuikEval Connector
Isolated USB

## Slide 5: Arduino Integrated Development Environment (IDE) Edit, Compile, and Upload Firmware

## Slide 6: Arduino Hardware
Digital I/O
Digital or Analog I/O
Power to Shield
USB (Data and Power)
1) Upload Firmware (Your Program)
2) Serial Terminal Communication
12V Power
(Optional) Allows standalone operation without PC or USB connection

## Slide 7: Arduino “Shields” Extend Functionality
Stackable
Headers

## Slide 8: Linduino Adds Support for QuikEval Demo Boards

## Slide 9: Do Your Customers Ask for Drivers?
If you are a Linear FAE because you hate software:
  Direct customers to our ‘C’ libraries. Done.
If you are a little more adventurous:
  Run the QuikEval GUI with a Linduino and demo board.
  Then, fire up the Arduino IDE, upload the “demo code”, and watch it run.
  Look at the ‘C’ code and see how it works.

## Slide 10: Want More?
Write your own code
Design your own projects
  Multiple demo boards?
  Arduino shields are abundant
    Touchscreen, bluetooth, motor control, …
      http://store.arduino.cc
      https://www.sparkfun.com/
      http://adafruit.com/
      http://www.seeedstudio.com/
      http://www.pololu.com/
      http://www.shieldlist.org/
Try Atmel Studio
  Free Microsoft Visual Studio-based IDE
  In-circuit debugging possible with $50 AVR Dragon
http://www.adafruit.com/products/376

## Slide 11
If you are reading this on the big screen, you have done your homework and followed Demo Manual 2026 to Page 6, until the LTC2607 window pops up. This includes:
Installing Arduino 1.0.4 software
Updating QuikEval – The current version is K95 (upper left corner of welcome window)
Unzipping LTSketchbook onto your laptop
Verifying that your PC is talking to your Linduino
All required files are available at:
http://www.linear.com/designtools/linduino.php
Homework – Before FAE Meeting!

## Slide 12
Open the Arduino IDE
Select File → Preferences
Arduino IDE

## Slide 13: LTSketchbook Location Setup
Sketchbook Location:
  Browse to unzipped \LTSketchbook.
Click Open and enter OK

## Slide 14: Load DC590B Sketch
Navigate to File→Sketchbook→Utilities→DC590B

## Slide 15: Select Board
Select Arduino Uno as Board Type
  Tools→Board→Arduino Uno

## Slide 16: Select Serial Port
Select the appropriate COM port (trial-and-error is ok).
  Tools→Serial Port→COMx

## Slide 17: Upload
Press Upload Button
Verify that there are no error messages.

## Slide 18: Serial Monitor
Open the Serial Monitor
Set Baud Rate to 115200
Set NewLine “NL” & Carriage Return “CR”
Check that you receive “hello”

## Slide 19: Close Serial Terminal and Open QuikEval
Close Serial Terminal
(Important!)
Then, open QuikEval
and press “Collect”

## Slide 20: Collect Data
Verify QuikEval works.
Then, close application.

## Slide 21: DC934A Demo Code
Open Sketchbook → Part Number→ 2000→ 2600→ 2607→ DC934A

## Slide 22: DC934A Demo Code
Press Upload
Serial Monitor

## Slide 23: Open Serial Monitor and Give it a Try
Try option “7-Sweep”, 10 sample points.

## Slide 24: Simple Science Project
DC934A Demo Code demonstrates many features.
For something simpler, load FAE_April_2013.

## Slide 25: Block Diagram

## Slide 26: Science Project – Setup, Loop
Every Arduino “sketch” (*.ino filename) contains a setup() function and a loop() function. This is specific to Arduino.
  Setup()
  {
  // Runs once upon power-up or a reset
  }
  Loop()
  {
  // Repeats continuously.
  }
Advanced: Arduino convention hides C/C++ main(), which calls setup(), loop(), and the serial communication handler.

## Slide 27: Science Project – Serial
USB
Serial
5V RS-232

## Slide 28: Science Project – Arduino Serial Communication
Serial library (class) makes communication with the Arduino/Linduino, super-simple
  Serial.begin(115200) sets the baud rate to 115200
  Serial.print(“String”) prints “String”
  Serial.println(“String”) prints “String” plus newline
  Serial.available() checks if characters are waiting to be read
  Serial.read() reads one character
Advanced: the serial RX/TX are also connected to pins 0/1 of the shield header.

## Slide 29: #include Files
#include a header file for every library.
Linduino programs require “Arduino.h” and “Linduino.h”
“LT_I2C.h” is required for I2C, “LT_SPI.h” for SPI.
Part libraries are named “LTpart.h”
Advanced: Compiler automatically searches LTSketchbook/Libraries directory for matching *.cpp files. Arduino linker links libraries based on #include list in *.ino

## Slide 30: Open LTSketchbook/Linduino.html

## Slide 31: QuikEval Functions
Initialize I2C and SPI using
  quikeval_I2C_init()
  quikeval_SPI_init()
Switch between I2C and SPI
  quikeval_I2C_connect()
  quikeval_SPI_connect()
SPI Chip Select is defined as QUIKEVAL_CS (Arduino pin 10)
Advanced: *_connect() functions drive QUIKEVAL_MUX_MODE pin high or low to switch MUX. (Arduino pin 8)

## Slide 32: QuikEval Connector
QuikEval I2C/SPI
I2C/SPI MUX

## Slide 33: Pins – Configuring, Reading and Writing
Pins are numbered 0 to 13 and A0 to A5 (look at silkscreen)
PinMode can be set to OUTPUT, INPUT, or INPUT_PULLUP
To set pin high or low
  digitalWrite(pin#, HIGH or LOW) - Arduino standard
  output_low(pin#), output_high(pin#) – Linduino only
To read pin
  digitalRead(pin#)

## Slide 34: CONSTANTS
Constant bit settings, lsb weights, etc. are defined in the “LT_part.h” file in ALL_CAPS (by ‘C’ convention).
Use HTML browser to look at LTSketchbook\Linduino.html
  select Modules → LTC2607 → LTC2607.h
Bitwise operations are useful to combine settings
  OR => CONST1 | CONST2
  AND => CONST1 & CONST2

## Slide 35: #include <stdint.h> Datatypes
Defines fixed-length integer datatypes
  The number of bytes used to represent the integer types defined in <stdint.h> is guaranteed to be the same on any processor
Stdint.h | Translation
int8_t, uint8_t | signed/unsigned 8-bit integer
int16_t, uint16_t | signed/unsigned 16-bit integer
Int32_t, uint32_t | signed/unsigned 32-bit integer

## Slide 36: Bootloader? No external programmer required!
If the “bootloader” detects a special sequence on the serial port immediately after the uC is RESET, the subsequent serial data is loaded into nonvolatile program memory.
The Arduino IDE can force a RESET using the DTR line of the serial port.
If the sequence is not detected, the normal (previously loaded) program runs.

## Slide 37: Stuff you don’t need to know, yet…
#ifdef, #endif for compiler
  Don’t worry about it if you don’t understand
//!, /*!, // @xxx, comments are formatted for the automatically generated HTML documentation.
  Don’t worry about it unless you REALLY want to know.

## Slide 38: Caveats
We’re still in beta
  We’re writing software as fast as we can
  Help us find our bugs… and please forgive them
  Use good judgment. If you show the Linduino to your customers, make sure they understand it is beta.

## Slide 39: Fun!

## Slide 40
PINS 2,3,4
GND

## Slide 41: Troubleshooting your own hardware/software
Pins 0,1 are Serial Port TX/RX.
  Use other pins first.
If all else fails, run Arduino Blink Example.
  Check if LED blinks.

## Slide 42: Suggested References
Language: http://arduino.cc/en/Reference/HomePage
Atmel Specific:
  Forum: http://www.avrfreaks.net/
Advanced:
  Arduino Internals: http://www.apress.com/9781430238829
  Google C++ Style Guide: http://google-styleguide.googlecode.com/svn/trunk/cppguide.xml
  Embedded C Programming and the Atmel AVR (Barnett, Cox, and O’Cull)

## Slide 43: Pointer Review – It’s ok, everyone’s rusty…
If you want to read an ADC code, call the function: adc_read(&adc_code, …
    ‘&’ means the function can modify the value in adc_code
    ‘&’ means you are passing the memory address of adc_code
The person who wrote the function adc_read declared it as: adc_read(uint8_t* adc_code, … { i2c_start()… *adc_code=i2c_read(… }
  ‘*’ in ‘*adc_code’ means to modify the value at memory location “pointed to” by &adc_code
  If you don’t understand, just follow an example…