## Slide 1: NAL Modem Interference

## Slide 2: Summary of Efforts
April 3-4:
  Extensive testing to resolve that although good RSSI stats could be had, there was still interference Scott later identified as a “birdie”, or beat frequency of interference in the modem comms.
April 9-10:
  Scott comes onboard, helps we baseline and run some tests with spare modems and motherboards.
  Scott finds some noise and snubs it on the switching circuits
April 11-12:
  Test against the modded boards, improvements seen
  Try isolating the serial, make a new harness
April 15:
  Two tests, running on modded boards actually making calls, both seem to work much better than in the past.

## Slide 3: Test Overview

## Slide 4: Test B: Modem EXT Power in Closed Housing
Similar results were seen later in a test with the Rubbermaid bin, test I.

## Slide 5: Test G
Spare MB and modem, no housing
Latop serial comms
Good stats, but high up/down signal rates.

## Slide 6: Test H
Still using MB and harnesses, but fed ext 3V3 and 12V to disable switchers
Latop serial comms
Still drops, but longer uptime
First indication that there is a baseline up/down nature in the RSSI.

## Slide 7: Test J
Modded Board in the Rubbermaid
Longer uptime, cycling ~ 8 min

## Slide 8: Test K
Put it in the housing
RSSI Test
Clear Improvement
Housing Open

## Slide 9: Other Tests
From here, tests aimed to see improvements with isolation
Test P: Antenna moved far away, no impact
Test R: Isolated RS232 to CPF, no impact

## Slide 10: RUDICS Call Tests
April 11:
  Started making calls, so we can evaluate these different setups
  From the laptop, a simple state machine talks to the modem
  A little harder to assess call success at this time, but call lengths seem to mimic the up/down nature of the RSSI measurements
Three substantive tests:
  Spare modem & laptop
  CPF Power (modded) talking to laptop
  CPF Power talking to CPF micro

## Slide 11: Rudics Impressions
All three had calls that held up >2 minutes
Looking at UW floats, average profile size is ~80KB
At 2400bps transfer would take 270-seconds
Calls made from the float at present (need further testing) range from 180-s, 450-s, and one outlier at 45-minutes!
Downtimes between calls are not assessed yet.
Battling server upgrades yesterday.

## Slide 12: Next Steps
Scott’s improvement have helped greatly, call-times may be a function of environment on the deck more now.
Modify more motherboards, at least the one we took out of the float.
Contact MetOcean to discuss the call length issue, to gain some clarity on the up-time expectations on calls.
Need to fix up the rudics code, and simplify the shoreside server, but is easier now to test. (2-3 days)
I think we should consider a new harness, or more testing on the old one.