## Slide 1: Coastal Profiling Float Drop Weight
Summer 2022 Intern: Roy Gilboa
Mentor: Gene Massion

## Slide 2: Overview
Background
Requirements/Motivation
Engineering Process
Concept
Design
Fabrication
Testing
Future Work
Conclusion
Images: MBARI 2017

## Slide 3: Background/Motivation
From the original CPF proposal:
  "the widespread pattern of low returns along the West Coast for two species of salmon indicates an environmental anomaly [low nutrient production] occurred in the California Current in 2005.“
  “Further development of event-scale observing capacity (e.g., novel autonomous platforms) in all continental margin systems to better quantify impacts of episodic events on coastal carbon budgets”
    A Science Plan for Carbon Cycle Research in North American Coastal Waters 2016, Ocean Carbon and Bio. Program and NA Carbon Program
  NSF’s 10 Big Ideas: Navigating the New Arctic
    “Current Arctic observations are sparse and inadequate for enabling discovery or simulation … to assess their impacts on the broader Earth system”

## Slide 4: Background/Motivation
Depth control w/buoyancy engine
  2x Hydraulic bladders
Autonomously collect CTD profiles & more
Can land on seafloor
Regular deployments/recoveries with R/V Paragon for battery replacement
Emergency ROV recovery
Add drop weight as a recovery failsafe mechanism
Images: MBARI 2016

## Slide 5: Design Requirements/Goals
Requirements
  Release weight with CPF resting on seafloor
  4 kilogram mass
  Self–contained power supply
  Multiple independent triggers:
    Corrosive link
    Overpressure burst disk
    Timer/manual
  Testable prototype within internship time limits
Goals:
  Maximize reliability, manufacturability, and ease of reset/reuse
  Minimize mud-collecting volumes

## Slide 6: Engineering Design Process
Jumping between phases is expensive in effort/time
System design:
  ✔ Understand problem
  ✔ Define requirements
  ✔ Identify risks
  ✔ Generate test plan
  ❌ Iterate w/stakeholders
✔ Informal/quick design reviews w/appropriate colleagues
✔ Concept: Try multiple designs & mitigate risk
✔ Preliminary: Pick one design & move forward
❌ Critical: Finish final details & build
❌
❌
Drop weight design is still early in preliminary phase

## Slide 7: Concept
Metal ring around CPF external bellows bucket
  Concept 1: Lead wire/oil-filled Tygon hose
  Concept 2: Rolled stainless steel bar
Timed/controlled release mechanism secures ring until triggered
  Concept 1: External/wet burn wire
  Concept 2: Internal pin puller

## Slide 8: Design Comparison
Weight: Rolled stainless steel bar
  Use spring force to secure/release weight
  Analogous to SCUBA weight belt
Release mechanism
  Standalone burn wire: too fragile
  OTS shape memory alloy pin puller: too expensive
Custom Burn Wire-actuated Pin Puller
  Protects burn wire from shock/corrosion and reduces heat output requirement
  Simple O-ring seals
  Based on well-known technology

## Slide 9: Design - Weight
Rolled stainless steel bar springs open when released
  Held in tension and rests on metal “ramps” when armed
Also considered:
  Lead-filled tube: unclear long-term reliability
  Tungsten shot or cylindrical beads: expensive
Tunable mass
Easily manufacturable in-house
Non-toxic

## Slide 10: Design - Weight Mount
Sheet metal “ramps” mate with existing bolts on external bellows bucket
  Also considered: annular 3D-printed ramp, but was not time/cost-effective
Bends provide rest for secured weight tube & guide it outwards once released
Can be tuned to act as springs

## Slide 11: Design - Pin Puller
Spring-loaded titanium release pin
Secured by Spectra synthetic line & released by burn wire
Also considered: OTS EBAD subsea pin puller
  Cost >$11k/ea!
$$$$$$$$$$$$$$$$$$$$$$$$$
Burn wire
Spectra line

## Slide 12: Design - Pin Puller
18650 Li-ion battery
Clear PVC prototype pressure housing
3D-printed end cap w/OTS O-ring seals
  1x dynamic seal (pin)
  1x static seal (pressure housing)

## Slide 13: Fabrication

## Slide 14: Testing

## Slide 15: Final Adjustment & Tank Test
Reduced friction on pin by removing metal rod ends & replacing w/rope
Adjusted weight & ramps to reduce rope tension
Tested in tank to demonstrate function underwater

## Slide 16: Future Work
Increase spring force
Improve weight retention
Reduce rope-induced pin friction
Integrate electronics
Reduce housing diameter
Integrate corrosive link & burst disk
System design:
  ✔ Understand problem
  ✔ Define requirements
  ✔ Identify risks
  ✔ Generate test plan
  ❌ Iterate w/stakeholders
✔ Informal/quick design reviews w/appropriate colleagues
✔ Concept: Try multiple designs & mitigate risk
✔ Preliminary: Pick one design & move forward
❌ Critical: Finish final details & build

## Slide 17: Acknowledgements
Mentor: Gene Massion
Fabrication:
  Aaron Schnittger
  Roman Marin
  John Ferreira
  Frank Flores
  Ray Thompson
  James McClure
Additional advice:
  Thom Maughan
  Brent Jones
  Brett Hobson
  Scott Jensen
Photography
  Todd Walsh
  Jared Figurski
The MBARI Summer Internship Program is generously supported through a gift from the Dean and Helen Witter Family Fund and the Rentschler Family Fund in memory of former MBARI board member Frank Roberts (1920-2019) and by the David and Lucile Packard Foundation. Additional funding is provided by the Maxwell/Hanrahan Foundation.