## Slide 1: EVALUATION OF INERTIAL MEASUREMENT UNIT PERFORMANCE FOR WATER COLUMN VELOCITY ESTIMATION OF COASTAL PROFILING FLOATS.
August 10, 2016
1330 - 1345
Nick Raymond
~
Gene Massion

## Slide 2: Profiling Floats
High Spatial and Temporal Resolution
Low Cost but Robust (+5 year deployment)
Update with better image from Johnson publication
Image: soccom-float-visualization
Image: http://www.argo.ucsd.edu/
Image: http://www.argo.ucsd.edu/
Notes: Argo is a global array of more than 3,000 free-drifting profiling floats that measures thetemperature and salinity of the upper 2000 m of the ocean.
This allows, for the first time, continuous monitoring of the temperature, salinity, and velocity of the upper ocean, with all data being relayed and made publicly available within hours after collection.
Argo float profiling for temperature/salinity has completely transformed ocean observing over the past 10 years.
SOCOM project wants to do the same for the carbon system, nitrate and oxygen, and net community production (including sea ice regions) by measuring biogeochemical parameters (pH, nitrate, oxygen, optics)

## Slide 3: Coastal Profiling Floats
Coastal environments are highly variable
Critical for understanding
  Hypoxia
  Acidification
  Anthropogenic Waste
Chem Sensor Lab’s Mission:
  Measure biogeochemical parameters
  pH, nitrate, oxygen, optics
  “Is net production changing on the
  West Coast of the US?”
Tank Prototype
Sea
Prototype
Photo: Todd Walsh
Photo: Todd Walsh

## Slide 4: Overview
Engineering Challenge
  Prevent float from drifting onshore.
  If too close to shore, have CPF drift out to deeper water.
Proposed Approach
  Identify favorable underwater currents while float moves up the water column.
Internship Scope
  Model dynamics of float drifting in underwater currents
  Determine feasibility of using inexpensive IMU to estimate float velocity.
Photo: Gene Massion, MBARI.

## Slide 5: (Optional ) Project Goals
Model Motion of CPF Drifting in Currents
  Estimate acceleration + velocity while drifting
  Determine min/max acceleration values
  Use historic current velocity data (input to model)
Estimate Velocity of Benchtop Prototype
  Build and program data logger
  Characterize sensor noise
  Signal processing/ filtering + evaluate performance
  Compare different filters/ filter parameters
Photo: Gene Massion, MBARI 2016

## Slide 6: SYSTEM OVERVIEW
How CPF floats work
  Hydraulic ballast
  Sensors
  Data collection
Inertial measurement units
  Accelerometer
  Gyroscope
  Magnetometer
NOT used for position estimation.
Image: Gene Massion, MBARI.
Biogeochemical sensors
Microcontroller
Fluid reservoirs
Hydraulic bellows/bladder
Hydraulic pump
Add IMU

## Slide 7: MODELING MOTION OF CPF
Modeling Assumptions
  Model bluff body as a cylinder.
  Drag force is proportional to velocity.
  Upward velocity constant at 0.1 m/s (+Z), controlled by closed-loop dive engine.
  North/South and East/West velocity independent of each other
  Current profiles obtained from Acoustic Doppler Current Profiler (mooring motion corrected).
Table 7.3 Drag of 3D Bodies Re > 104
Reference: White 7th Ed, chapter 7.
Source: MBARI Live Access to DATA
Drag coefficient: Radial Flow
Axial Flow

## Slide 8: DYNAMIC MODEL
Calculate drag force
Fdrag
Ftotal = m*a
a = Ftotal /m
[m/s]
[N]
CPF Velocity
[m/s2]
[m/s]
CPF Velocity – feed back to drag force calculation
V = CPF vel.
U = current vel.
A* = L x D
CD = drag coeff.
= sea water density
Note: characteristic area (A*) is cross section of cylinder normal to flow.
Input
Output
Current Velocity Profiles
N/S & E/W
[U]
[V]

## Slide 9: DYNAMIC SIMULATION RESULTS
CPF Velocity [m/s]
CPF Acceleration [m/s2]
Accelerations range:
  0.2 – 1 mm/sec^2
Velocity range
0 – 250 mm/sec^2
Based on results, project much more difficult than expected.
Requires more signal processing to reduce noise.
Units?
Mm/sec^2, meter/sec^2, mg?
Notes: Need to create new plots, thicker lines and larger font. Update the units.
Line width 2pt, text size 18

## Slide 10: HARDWARE + SOFTWARE
GHI Raptor Dev. Board + SD Card + RTC.
Firmware written in C# in Visual Studio.
Update with block diagram of modules and connections.
Update to show block diagram of signal flow from Sensor to SD card.

## Slide 11: LINEAR TRANSLATION STAGE SETUP
Controller
Table
Sensor fixture

## Slide 12: EXPERIMENT SETUP
Run | Accel (mm/sec^2) | Velocity (mm/sec)
A | 150 | 200
B | 40 | 100
C | 10 | 50
D | 5 | 35
E | 1 | 16
V_max = 200 mm/sec
A = 150 mm/sec^2
Acceleration Profile
Velocity Profile

## Slide 13: Signal Processing
Import:
raw accelerometer data (XYZ)
Detrend: remove trend in accel. data
Filter 01:
Denoise
vs.
Moving Avg.
Numerical integration
Filter 02:
Freq. selective filtering of velocity estimate
Simulation of desired velocity profile
Velocity Estimate

## Slide 14: EXPERIMENTAL ACCELEROMETER DATA
Run E: A = 1mm/sec^2, V = 16 mm/sec

## Slide 15: SMALL ACCELERATION MEASUREMENTS
Run E: A = 1mm/sec^2, V = 16 mm/sec

## Slide 16: ERROR: LOW ACCELERATION MEASUREMENTS
Run E: A = 1mm/sec^2, V = 16 mm/sec
Update plot to show all five error plots
Notes: Hello these are notes – do you see me?

## Slide 17: BIG ACCELERATION MEASUREMENTS
Run A: A = 150 mm/sec^2, V = 200 mm/sec
Update to show velocity estimate with good filter settings for Run A

## Slide 18: ERROR: BIG ACCELERATION MEASUREMENTS
Run E: A = 1mm/sec^2, V = 16 mm/sec
Update plot to show all five error plots
Notes: Hello these are notes – do you see me?

## Slide 19: CONCLUSION
Dynamic simulation modeling CPF motion drifting in underwater currents was created to determine maximum expected acceleration of 0.2 – 1 mm/sec^2.
It was shown that it is possible to use $20 sensor to estimate velocity for slowly moving objects, near expected dynamic range of CPF.
Three types of filtering methods were tested, with denoise and moving average filter having the best results (for the range of parameters tested).
While possible, the high noise level and limited resolution of the inexpensive sensor requires signal processing before reliable velocity estimates can be made.
Testing on the linear translation stage was completed, but more random profiles should be tested and filter settings need to be optimized in for further application.
NEED TO SIMPLIFY TEXT AND ADD IMAGE!

## Slide 20: FUTURE WORK
Develop new motion paths for linear table to simulate vertical profiling motion given historic current velocity data.
Optimize band-pass filter (either IIR or FIR) to filter raw accelerometer data, as this avoids the need for the detrend() function.
Configure linear translation stage, determine minimum acceleration and rerun experiments over range of smaller accelerations.
Run experiments with sensor fusion data, and determine how to store onboard calibration offsets on the controller.
Design circuit board to integrate IMU into the Lemur board and mount to CPF float.

## Slide 21: ACKNOWLEDGEMENTS
Gene
Mike
Jim
Jose
Denis
Ken + Chem lab
George
Linda

## Slide 22: SOURCES

## Slide 23: SIMULINK MODEL – 1D
Input Current Velocity Profile
Calculate Drag Force
Calculate dynamics
Output acceleration, velocity and positon
Save state variables to workspace
Calculate Re
Note: this represents one axis, it is repeated three times for N/S, E/W, and +Z.

## Slide 24: DRAG FORCE BLOCK

## Slide 25: DYNAMICS BLOCK

## Slide 26: SIMULATION OUTPUTS
Position [m]
CPF Velocity [m/s]
CPF Acceleration [m/s2]
CPF Acceleration [mg]
Current Velocity [m/s]
Reynolds Number

## Slide 27: VERIFY FLATNESS OF LINEAR TABLE
Check flatness of linear table
Determine variability of static acceleration measurements
Movement interval of 50 mm
Velocity 25 mm/sec
Stationary for 20 seconds, then calculate average and Std.
Approximately 1 degree of sensor pitch, variable of 0.1 degree over 600 mm travel