## Slide 1: EVALUATION OF INERTIAL MEASUREMENT UNIT PERFORMANCE FOR WATER COLUMN VELOCITY ESTIMATION OF COASTAL PROFILING FLOATS.
August 10, 2016
1330 - 1345
Nick Raymond
~
Gene Massion

## Slide 2: Presentation Outline
Project Overview – Science > Engineering > Internship
Profiling Floats – How they work
Float Mission Cycle
Estimating float velocity
Internship Workflow - my methodology
Float Dynamics & Benchtop Simulator – the MATH
  FBD
  Translation stage
Simulation vs Experimental Data – what to expect, and what we measured
High End Accelerations – LOOK IT WORKS! “I am a stud”
Low End Accelerations – LOOK, it kinda works….?
Performance Metric – how we can compare performance of filter
Conclusions – what I learned and accomplished
Future work – everything I still want to work on!

## Slide 3: Project Overview
Monitor the health of the ocean
  How is net production changing on the West Coast of the US?
Biogeochemical measurements:
  CTD – standard measurements
  O2 –oxygen for supporting aerobic life
  Nitrate - nutrients for primary producers
  Fluorescence – proxy for chlorophyll
  Backscatter – turbidity of ocean water
  Radiation – nasty stuff in the water?
MODIS Chlorophyll June 28, 2011
http://podaac-tools.jpl.nasa.gov/soto/
Notes: Understanding complex coastal environments will require dense sensor networks.

## Slide 4: Profiling Float
How CPF floats profile
  Float starts neutral
  Pump oil into outer bladder, float volume increases, buoyancy increases, float rises
  Pump oil into inner bladder, float volume decreases, buoyancy decreases, float sinks
Inertial Measurement Unit (IMU)
  Includes accelerometer, gyroscopes, magnetometers in XYZ axes
  Can estimate orientation and velocity
Image: Gene Massion, MBARI.
Biogeochemical sensors
Microcontroller
Inner oil bladder
Hydraulic pump
Outer oil bladder
Add IMU
Tank Prototype

## Slide 5: Float Mission Cycle
High Spatial and Temporal Resolution
Low Cost but Robust (+5 year deployment)
Image: soccom-float-visualization
Image: http://www.argo.ucsd.edu/
6-12 hours at surface to transmit data to satellite.
Descends to depth
500 to 1000 m – drift 1 to 9 days
Float descends and “parks” in the mud.
Sensor readings recorded during ascent.
Obtain GPS location, send data to satellite.
Warning!
Dive down, ride strong current back to open water
Notes: Argo is a global array of more than 3,000 free-drifting profiling floats that measures thetemperature and salinity of the upper 2000 m of the ocean.
This allows, for the first time, continuous monitoring of the temperature, salinity, and velocity of the upper ocean, with all data being relayed and made publicly available within hours after collection.
Argo float profiling for temperature/salinity has completely transformed ocean observing over the past 10 years.
SOCOM project wants to do the same for the carbon system, nitrate and oxygen, and net community production (including sea ice regions) by measuring biogeochemical parameters (pH, nitrate, oxygen, optics)

## Slide 6: Estimating Float Velocity
What we
can measure
What we
want to know
Float Motion Underwater

## Slide 7: Workflow Overview
Model System
Evaluate Sensor
Build & Program Data Logger
Run Tests
Signal Processing
Evaluate Performance

## Slide 8: Float Dynamics & Benchtop Simulator
Drag force
Fdrag
Ftotal = m*a
CPF Velocity
Numerical Model of Float Dynamics
Acoustic Doppler Current Profile
Source: dods.mbari.org/lasOASIS
Benchtop Simulator
Run | Accel (mm/sec^2) | Velocity (mm/sec)
A | 150 | 200
B | 40 | 100
C | 10 | 50
D | 5 | 35
E | 1 | 16
Computer
Sensor
Microcontroller + SD Card
Table
Notes: Daily Average East-West velocioty (+E,/-W) True mooring motion correcter M1 buoy

## Slide 9: Simulation vs Experimental Data
Offset
Drift

## Slide 10: Simulation vs Experimental Data
(Zoom in)

## Slide 11: Signal Processing
Import:
accel. data
Detrend +
Filter
Filter
Numerical integration
Velocity Estimate
Filtering
  Results obtained with “denoise” filter, referenced from image processing literature
  Also tested:
    Moving average filter
    Frequencies selective filters (low-pass and band-pass)

## Slide 12: Velocity Estimate - Large Accelerations
Run A: Vel = 200 mm/sec^2; Accel = 150 mm/sec^2;

## Slide 13: Velocity Estimate - Small Accelerations
Run A: Vel = 16 mm/sec^2; Accel = 1 mm/sec^2;

## Slide 14: Performance Metric

## Slide 15: CONCLUSION
Dynamic simulation modeling CPF motion drifting in underwater currents was created to determine maximum expected acceleration of 0.2 – 1 mm/sec^2.
It was shown that it is possible to use $20 sensor to estimate velocity for slowly moving objects, near expected dynamic range of CPF.
Three types of filtering methods were tested, with denoise and moving average filter having the best results (for the range of parameters tested).
While possible, the high noise level and limited resolution of the inexpensive sensor requires signal processing before reliable velocity estimates can be made.
Testing on the linear translation stage was completed, but more random profiles should be tested and filter settings need to be optimized in for further application.
NEED TO SIMPLIFY TEXT AND ADD IMAGE!

## Slide 16: FUTURE WORK
Develop translation stage that better simulates the dynamic model result
  Lower velocity and accel
  Motion paths more representative of ocean current profiles
Optimize signal processing workflow
  Better filtering and detrending techniques

## Slide 17: ACKNOWLEDGEMENTS
Gene
Mike
Jim
Jose
Denis
Ken + Chem lab
George
Linda
Need to work on this!

## Slide 18: DYNAMIC MODEL
Calculate drag force
Fdrag
Ftotal = m*a
a = Ftotal /m
[m/s]
[N]
CPF Velocity
[m/s2]
[m/s]
CPF Velocity – feed back to drag force calculation
V = CPF vel.
U = current vel.
A* = L x D
CD = drag coeff.
= sea water density
Note: characteristic area (A*) is cross section of cylinder normal to flow.
Input
Output
Current Velocity Profiles
N/S & E/W
[U]
[V]

## Slide 19: Coastal Profiling Floats
Coastal environments are highly variable
Critical for understanding
  Hypoxia
  Acidification
  Anthropogenic Waste
Chem Sensor Lab’s Mission:
  Measure biogeochemical parameters
  pH, nitrate, oxygen, optics
  “How is net production changing on the
  West Coast of the US?”
Tank Prototype
Sea
Prototype
Photo: Todd Walsh
Photo: Todd Walsh

## Slide 20: Profiling Floats
High Spatial and Temporal Resolution
Low Cost but Robust (+5 year deployment)
Image: soccom-float-visualization
Image: http://www.argo.ucsd.edu/
Image: http://www.argo.ucsd.edu/
6-12 hours at surface to transmit data to satellite.
Descent to depth – 6 hours
1000 m – drift appx. 9 days
Float descends to begin profile from greater depth – 2000 m.
Sensor readings recorded during ascent.
Obtain GPS location, send data to satellite.
Notes: Argo is a global array of more than 3,000 free-drifting profiling floats that measures thetemperature and salinity of the upper 2000 m of the ocean.
This allows, for the first time, continuous monitoring of the temperature, salinity, and velocity of the upper ocean, with all data being relayed and made publicly available within hours after collection.
Argo float profiling for temperature/salinity has completely transformed ocean observing over the past 10 years.
SOCOM project wants to do the same for the carbon system, nitrate and oxygen, and net community production (including sea ice regions) by measuring biogeochemical parameters (pH, nitrate, oxygen, optics)

## Slide 21: MODELING MOTION OF CPF
Modeling Assumptions
  Model bluff body as a cylinder.
  Drag force is proportional to velocity.
  Upward velocity constant at 0.1 m/s (+Z), controlled by closed-loop dive engine.
  North/South and East/West velocity independent of each other
  Current profiles obtained from Acoustic Doppler Current Profiler (mooring motion corrected).
Table 7.3 Drag of 3D Bodies Re > 104
Reference: White 7th Ed, chapter 7.
Source: MBARI Live Access to DATA
Drag coefficient: Radial Flow
Axial Flow

## Slide 22: DYNAMIC SIMULATION RESULTS
CPF Velocity [m/s]
CPF Acceleration [m/s2]
Accelerations range:
  0.2 – 1 mm/sec^2
Velocity range
0 – 250 mm/sec^2
Based on results, project much more difficult than expected.
Requires more signal processing to reduce noise.
Units?
Mm/sec^2, meter/sec^2, mg?
Notes: Need to create new plots, thicker lines and larger font. Update the units.
Line width 2pt, text size 18

## Slide 23: HARDWARE + SOFTWARE
GHI Raptor Dev. Board + SD Card + RTC.
Firmware written in C# in Visual Studio.
Update to show block diagram of signal flow from Sensor to SD card.

## Slide 24: LINEAR TRANSLATION STAGE SETUP
Controller
Table
Sensor fixture

## Slide 25: EXPERIMENT SETUP
Run | Accel (mm/sec^2) | Velocity (mm/sec)
A | 150 | 200
B | 40 | 100
C | 10 | 50
D | 5 | 35
E | 1 | 16
V_max = 200 mm/sec
A = 150 mm/sec^2
Acceleration Profile
Velocity Profile

## Slide 26: Signal Processing
Import:
raw accelerometer data (XYZ)
Detrend: remove trend in accel. data
Filter 01:
Denoise
vs.
Moving Avg.
Numerical integration
Filter 02:
Freq. selective filtering of velocity estimate
Simulation of desired velocity profile
Velocity Estimate

## Slide 27: EXPERIMENTAL ACCELEROMETER DATA
Run E: A = 1mm/sec^2, V = 16 mm/sec
Notes: Show with the offset, and show with the drift ---- explain that this is the challenge

## Slide 28: BIG ACCELERATION MEASUREMENTS
Run A: A = 150 mm/sec^2, V = 200 mm/sec
Update to show velocity estimate with good filter settings for Run A

## Slide 29: SMALL ACCELERATION MEASUREMENTS
Run E: A = 1mm/sec^2, V = 16 mm/sec

## Slide 30: Performance metric
Run E: A = 1mm/sec^2, V = 16 mm/sec
Notes: Explain source of error

## Slide 31: ERROR: BIG ACCELERATION MEASUREMENTS
Run E: A = 150mm/sec^2, V = 200 mm/sec
Notes: Hello these are notes – do you see me?

## Slide 32: SOURCES

## Slide 33: SIMULINK MODEL – 1D
Input Current Velocity Profile
Calculate Drag Force
Calculate dynamics
Output acceleration, velocity and positon
Save state variables to workspace
Calculate Re
Note: this represents one axis, it is repeated three times for N/S, E/W, and +Z.

## Slide 34: DRAG FORCE BLOCK

## Slide 35: DYNAMICS BLOCK

## Slide 36: SIMULATION OUTPUTS
Position [m]
CPF Velocity [m/s]
CPF Acceleration [m/s2]
CPF Acceleration [mg]
Current Velocity [m/s]
Reynolds Number

## Slide 37: VERIFY FLATNESS OF LINEAR TABLE
Check flatness of linear table
Determine variability of static acceleration measurements
Movement interval of 50 mm
Velocity 25 mm/sec
Stationary for 20 seconds, then calculate average and Std.
Approximately 1 degree of sensor pitch, variable of 0.1 degree over 600 mm travel