## Slide 1: Evaluation of inertial measurement unit performance for water column velocity estimation of coastal profiling floats.
Nick Raymond & Gene Massion
Summer Internship 2016

## Slide 2: Overview
Research goal
  Prevent float from beaching itself.
  If float is too close to shore, have it drift out to deeper water.
Approach
  Identify favorable underwater currents while float drifts up to surface.
Internship Scope
  Estimate dynamics of float using current velocity profiles.
  Identify range of accelerations and determine feasibility of using IMU.

## Slide 3: ACKNOWLEDGEMENTS

## Slide 4: Profiling Floats

## Slide 5: Coastal Profiling Floats

## Slide 6: Project Goals
Model Motion of CPF Drifting in Currents
  Estimate acceleration + velocity while drifting
  Determine min/max acceleration values
  Use historic current velocity data (input to model)
Estimate Velocity of Benchtop Prototype
  Build and program data logger
  Characterize sensor noise
  Signal processing/ filtering + evaluate performance
  Compare different filters/ filter parameters

## Slide 7: SYSTEM OVERVIEW
How floats work
  Hydraulic ballast
  Sensors
  Data collection
Inertial measurement units
  Accelerometer
  Gyroscope
  Magnetometer
  Sensor fusion
IMU strapdown measurements
  Measure accelerations
  Calculate speed + direction of CPF
  NOT ATTEMPTING TO ESTIMATE POSITION
Image of CPF parts
+ Image of IMU

## Slide 8: MODELING MOTION OF CPF
Physical Parameters
  Model bluff body as a cylinder.
  L/D = 8
  CD ≈ 0.788 flow normal to radius
  CD ≈ 0.99 axially
Assumptions about Motion
  Upward velocity constant at 0.1 m/s (+Z), controlled by closed-loop dive engine.
  North/South and East/West velocity independent of each other (XY).
  Current profiles obtained from Acoustic Doppler Current Profiler (mooring motion corrected).
Table 7.3 Drag of 3D Bodies Re > 104
Reference: White 7th Ed, chapter 7.
Reference: MBARI Live Access to DATA
Radial Flow
Axial Flow

## Slide 9: DYNAMIC MODEL
Calculate drag force
Fdrag
F = m*a
a = F/m
[m/s]
[N]
CPF Velocity
[m/s2]
[m/s]
CPF Velocity – feed back to drag force calculation
V = CPF vel.
U = current vel.
A* = L x D
CD = drag cof.
= sea water density
Note: characteristic area (A*) is cross section of cylinder normal to flow.
Input
Output
Current Velocity Profiles
N/S & E/W
[U]
[V]

## Slide 10: SIMULATION RESULTS
Position [m]
CPF Velocity [m/s]
CPF Acceleration [m/s2]
CPF Acceleration [mg]
Current Velocity [m/s]
Reynolds Number

## Slide 11: HARDWARE+ SOFTWARE
GHI Raptor Dev. Board + SD Card + RTC.
Firmware written in C# in Visual Studio.

## Slide 12: EXPERIMENT SETUP
Run | Accel (mm/sec^2) | Velocity (mm/sec)
A | 150 | 200
B | 40 | 100
C | 10 | 50
D | 5 | 35
E | 1 | 16
V_max = 200 mm/sec
A = 150 mm/sec^2
Acceleration Profile
Velocity Profile

## Slide 13: LINEAR TRANSLATION STAGE SETUP
Controller
Table
Sensor fixture

## Slide 14: Signal Processing
Import:
raw accelerometer data (XYZ)
Detrend: remove trend in accel. data
Filter 01:
Denoise
vs.
Moving Avg.
Numerical integration
Filter 02:
Freq. selective filtering of velocity estimate
Simulation of desired velocity profile
Velocity Estimate

## Slide 15: EXPERIMENTAL ACCELEROMETER DATA

## Slide 16: EXPERIMENT VELOCITY ESTIMATE
Oscillating signal with 600 second period, 0.0017 Hz
Apply non-linear signal by subtracting 12th order polynomial curve.

## Slide 17: CHECK PLOTS

## Slide 18: SIMULINK MODEL – 1D
Input Current Velocity Profile
Calculate Drag Force
Calculate dynamics
Output acceleration, velocity and positon
Save state variables to workspace
Calculate Re
Note: this represents one axis, it is repeated three times for N/S, E/W, and +Z.

## Slide 19: DRAG FORCE BLOCK

## Slide 20: DYNAMICS BLOCK

## Slide 21: SIMULATION OUTPUTS
Position [m]
CPF Velocity [m/s]
CPF Acceleration [m/s2]
CPF Acceleration [mg]
Current Velocity [m/s]
Reynolds Number