## Slide 1: From Prototype to Platform: Making Better Engineering Decisions Through Testing

## Slide 2
Overview
Understand how testing works on the CPF
Use understanding to build a motor testbench software and answer questions about potential motors for the buoyancy engine
Results!

## Slide 3
Introduction to the CPF
Coastal profiling float – designed to work in shallow waters up to 350 meters deep
Closed Loop buoyancy system that controls platform velocity and depth

## Slide 4
Testing Done on the CPF
Benchtop testing

## Slide 5
Benchtop Pressure Simulator
Goal: simulate an actual deployment on the bench and inject problems
Used a pressure simulator to simulate scenarios
Uncovered a CTD communication problem

## Slide 6
Subsystem test – CTD
CTD stopped communicating with CPF controller
Built test cables and test fixture to verify CTD was communicating properly
Plugged CTD back up to the controller and it worked fine

## Slide 7
Characterizing Performance - Buoyancy Engine Testbench
Question 1: What motor controller + motor combination is most efficient for powering the buoyancy engine?
ELMO Twitter
MAXON EC90
MAXON EC60
Motor Controller + Motor Combinations
ELMO Twitter + EC90
ELMO Twitter + EC60
ST Micro + EC60

## Slide 8
Building a testbench
Easy to modify setup
WAGO Blocks
Multiple Motor Plates
Spacers to accommodate various shaft couplers
Results (ex time to swap motors)

## Slide 9
Designing a LabVIEW program
Easy to add other motor controllers
Simple commands and workflow
All in one (communication, logging, plotting, analysis)

## Slide 10
Method for testing continuous motor current draw
Use INA229 current monitoring module to measure current
4 kHz Sampling frequency, run for 5 seconds (20,000 samples)
Run test at 10 different load pressures (ranging from 0 to 420 dBar)
Gather average current over 20,000 samples for each load pressure
Repeat test for different motor + motor controller configs

## Slide 11
Results – Continuous Motion: Current Draw

## Slide 12
Characterizing Performance and mitigatimg risk
Performance: between the Maxon EC60 and the Maxon EC90, which motor uses the least energy on startup (de-anchoring from seafloor)?
Risk: Can we even provide the required power to start up at depth?

## Slide 13
Method for testing energy required for startup at 350dbar
ELMO Twitter
Accelerate to 1000RPM over 0.1 seconds
ELMO + Maxon EC60
Accelerate to 1000RPM over 1 second
ELMO + Maxon EC90
Accelerate to 1000RPM over 0.1 seconds
Accelerate to 1000RPM over 1 second
ELMO + Maxon EC90

## Slide 14
Results – Peak is within limits

## Slide 15
Results – Performance and Significance
3x performance difference
Insignificant relative to total energy available

## Slide 16
Conclusion – What we learned

## Slide 17
Questions?

## Slide 18: CUT SLIDES

## Slide 19
Building testbench control software
What are the goals?
  Supportable by other users
  Able to control motor …
What are the options?
Python
LabVIEW
Terminal
C/C++
What we decided
Labview (nice GUI driven real time control system very quickly)
  Easily learned by non-programmers
Easily modifiable

## Slide 20
Refining the LabVIEW Program
Message 1
Message 2
Message 3

## Slide 21
Procedure for testing
Message 1
Message 2
Message 3

## Slide 22
Questions?
Message 1
Message 2
Message 3

## Slide 23
State of the CPF 10 weeks ago
Done dozens of missions
gone through a set of engineering improvements to reduce power consumption.
The last test showed a high humidity alarm.
Discovered broken O-ring