## Slide 1: Coastal Profiling Float Software Design Review
June 26, 2013

## Slide 2: Profiler Software Ecosystem
A decision was taken to use Microsoft’s NETMF/Gadgeteer toolkit, C# and COTS hardware to develop embedded software for the Coastal Profiler.
This portion of the CPF design review will
  Thumbnail the NETMF software environment
  Present an overview of the application software architecture for the Coastal Profiler

## Slide 3: NETMF
A subset of Microsoft “Dot Net” environment
  Developed by Microsoft Labs for embedded systems
  Completely open source, except for tools and certain drivers (WiFi). No license required for use.
  Arguably “best of breed” tools for embedded software development.
  Tools are freely downloadable from Microsoft.
NETMF provides useful software components
  A FAT32 file system
  TCP/IP networking
  Threads
  Timers

## Slide 4: Gadgeteer
Gadgeteer is a toolkit for building systems from COTS hardware, NETMF and C#.
A Gadgeteer system is composed of a
  Mainboard containing an embedded processor
  Variety of hardware modules which connect to the mainboard through a simple interface
  Embedded software that implements the application using C# and NETMF software components.

## Slide 5: Gadgeteer Mainboard and Modules

## Slide 6: Gadgeteer Main Program
namespace FTP_Test
using Gadgeteer;
using GTM = Gadgeteer.Modules;
public partial class Program : Gadgeteer.Program {
private Gadgeteer.Modules.GHIElectronics.WiFi_RS21 wifi_RS21;
private Gadgeteer.Modules.GHIElectronics.SDCard sdCard1;
public static void Main() {
// Initialize the Mainboard first
Program.Mainboard = new GHIElectronics.Gadgeteer.FEZSpider();
Program p = new Program();
p.InitializeModules();
p.ProgramStarted();
// Starts Dispatcher
p.Run();
}
private void InitializeModules() {
this.sdCard1 = new GTM.GHIElectronics.SDCard(5);
this.wifi_RS21 = new GTM.GHIElectronics.WiFi_RS21(6);
}
}
}

## Slide 7: NETMF, The Good
C# is intended to be a “simple” language for object oriented programming.
Relatively easy to port code from C/C++
Download and debug code over Bluetooth
  An elegant mechanism (“delegates/events”) for implementing callbacks

## Slide 8: NETMF, the Bad…
“C# is sort of Java with reliability, productivity and security deleted.” – James Gosling
NETMF systems are byte code interpreters
  C# translated to CLR (common language runtime).
  10X to 100X loss of performance compared with native C/C++ code for simple integer math.
A C# “char” is Unicode not ASCII,
  尽快学习普通话！(Learn Mandarin soon!)
  Nothing inherently wrong, just surprising to the ignoscenti

## Slide 9: NETMF, The Ugly
C# is a managed (aka garbage collected) language,
  Impacts deterministic code execution.
  Little or no control over GC’s execution.
The NETMF libraries are confusing to use
  Poor documentation, that’s often out of date
  Hard to determine which assemblies(object code libraries) are needed for linking
Existing NETMF COTS hardware isn’t really that “low power” (0.25 watts running, 0.1 watt standby)

## Slide 10: Mine is not to reason why…
Despite the known and unknown problems with C#, NETMF and Gadgeteer; one team member (GM) has made very rapid progress using it.
The impact of byte code performance and non determinism introduced by garbage collection is believed to be modest. Control loops only run at 1 to 10 Hertz.
Standby power consumption (100 mW) of the COTS Gadgeteer might be the most challenging problem to overcome (or not).

## Slide 11: The back up plan…
C# will be written to allow an easy (if tedious) back port to C++ .
Freescale’s FRDM evaluation board running MBED will be used as target.
MBED avoids having to write our own TCP/IP stack and FAT32 file system.
A C++ class emulating C# delegates was developed to facilitate a hasty retreat.
Most of the hardware can be re-used without modification but the motherboard will probably be different.

## Slide 12: Profiler Software Components
A collection of Hierarchical State Machines implement the overall mission, PID loop and instrument control (one HSM per instrument).
A scheduler that determines when to sample and power manages instruments.
FTP and Telnet servers running in their own threads.
An event queue that contains events waiting to be processed by the HSMs.
A logger that saves science and engineering data on an SD card.

## Slide 13: Hierarchical State Machines
Shamelessly stolen from Miro Samek’s QP framework and textbook. Code generation for C#, not supported by the graphical HSM tools only C/C++.
No NETMF C# implementation available, so one was developed.
Minimize the “state explosion” that can result from modeling complex behavior using flat Finite State Machines.
Roughly analogous to Brook’s “layered control”.
A number of Hierarchical State Machines (HSMs) implement the desired mission behavior
  One HSM runs the “mission” (ascend, descend, etc.)
  Another HSM runs the PID depth control loop
  One HSM per instrument implement that instrument’s driver
HSMs can send events to themselves or other HSMs via an event queue.

## Slide 14: A simple HSM example
Blind-Well’s Microwave Toaster Oven

## Slide 15: HSM Implementation
States.cs
namespace HSM
{
public enum Signal
{
Null = 0,
Init = 1,
Entry = 2,
DeepHistory = 3, // Record Deep History
Exit = 4,
User = 5
};
public class Event
{
public Event(Signal signal)
{
m_signal = signal;
}
public Signal m_signal;
}
public delegate State State(Event e);
}
HSM.cs
namespace HSM
{
public class Hsm
{
protected void Initialize(State topState);
protected Boolean IsParent(State parentState, State childState);
protected void TransitionState(State newState, bool toDeepHist);
protected void TransitionState(State newState);
protected void InitTransitionState(State newState) ;
public void SignalCurrentState(Event e);
protected Boolean IsInState(State state) ;
private History StateHistory = new History();
private State curState = null;
private State topState = null;
}
}

## Slide 16: HSM Test Code and Output
using HSM;
namespace CPF_Test
{
public enum OvenEvents {
OpenDoor = Signal.User, CloseDoor, Toasting, Baking };
// Oven State Hierarchy
// oven
// heating
// toasting
// baking
// doorOpen
class Program
{
static void Main()
{
OVEN_HSM oven = new OVEN_HSM();
oven.SignalCurrentState(new Event((Signal) OvenEvents.Baking));
oven.SignalCurrentState(new Event((Signal) OvenEvents.OpenDoor));
oven.SignalCurrentState(new Event((Signal) OvenEvents.CloseDoor));
}
}
}
Entering Oven State
Initializing Oven State
Entering Heating State
Initializing Heating State
Entering Toasting State
Initializing Toasting State
Heating: BAKING signal!
Exiting Toasting State
Entering Baking State
Heating: OPEN_DOOR signal!
Exiting Toasting State
Exiting Heating State
Entering Door Open State
Door Open: CLOSE_DOOR signal!
Exiting Door Open State
Entering Heating State
Entering Baking State

## Slide 17: The “Door Open” State in C#
State doorOpen(Event e)
{
switch (e.m_signal)
{
case Signal.Entry:
Debug.Print("Entering Door Open State");
return null;
case Signal.Init:
return null;
case Signal.Exit:
Debug.Print("Exiting Door Open State");
return null;
case (Signal) OvenEvents.CloseDoor:
Debug.Print("Door Open: CLOSE_DOOR signal!");
TransitionState(heating, true);
return null;
}
return ovenOff;
}

## Slide 18: Event Queue
If the event queue is not empty, a dispatch thread
  Removes the oldest event in the queue
  Calls an appropriate HSM to the handle the event.
The dispatch thread will block whenever the event queue is empty.
HSMs run to completion minimizing problems with concurrency.
Gadgeteer’s “Program.Run()” method is hijacked and used as the System’s event dispatcher.
Gadgeteer’s “Program.CheckAndInvoke()” method is used to send signals to all software components.

## Slide 19: Events
An event is a
  Pointer to an instance of an HSM with a member function to be called (RX UART register full)
  Ancillary data (RX character received) for that event.
Events include
  UART RX interrupt with received character
  Timeouts
  HSM to HSM communication
  Telnet/FTP server to HSM communication
Whenever an event is placed in or remove from the event queue, it is time stamped and logged

## Slide 20: Scheduler
Profiler’s mission is described in a internal form, generated from an Excel spreadsheet.
Scheduler thread
  Reads the mission profile from a configuration file
  Observes the depth and time as reported by the PID HSM
  Sends “sample”, “power on” and “power off” events to the appropriate HSM as specified by the mission configuration file at the specified depth and/or time.

## Slide 21: Logger
A (very) tiny implementation of the “log4j” API
FAT32 used for expediency
  Provided natively NETMF
  Supports SD cards out of the box
But…
  NETMF FAT32 implementation is not thread safe
  FAT32 loses data during power failures
  I/O transfer rates are still not known

## Slide 22: Communications
Bluetooth
  Facilitates code download and debug
  NETMF doesn’t support TCP/IP debug 
WiFi for engineering deployments
  FTP Server for file transfer
  Telnet server for user interface
Iridium for science missions
  Uses existing shore based infrastructure
  ZMODEM to “push” files to shore via shell
  Bandwidth too limited for anything other than the simplest debugging and observation.