## Slide 1: The coastal profiling float: depth and velocity control
Laughlin barker
Chemical sensors lab
Mentor: gene massion

## Slide 2: Outline
In the global carbon budget, coastal waters matter
Profiling floats can scale as a monitoring solution
Existing floats are not suited for shallow waters
An MBARI float & buoyancy engine for shallow waters
Simulation & tests of buoyancy system
Looking toward a regional deployment

## Slide 3: Motivation: carbon cycle
Coastal (shelf) waters:
  7-10% ocean surface area1,2
  10-30% marine primary production2
  40-50% net primary production3
Google Earth
Notes: Net primary protection: carbon fixed by photosynthesis that’s not subsequently respired back into environment
e.g. in other words, the carbon being removed at the appropriate time scale
  ~10% global carbon4
Affecting coastal waters
upwelling,
landuse changes,
precip events,
pollution,
anthropogenic climate change
MODIS from Sunday (8-day average)

## Slide 4: Challenge: scale
Cascadiaresearch.org
Cruises
Mbari.org
Moorings
“Because of the large degree of heterogeneity in the main coastal subsystems and concomitant lack of data, most carbon fluxes in these subsystems have relatively high uncertainties.”
(“The changing carbon cycle of the coastal ocean” Bauer, J., et al, Nature, 2013)
Historical
Approaches
Notes: Historical long term monitoring
Moorings:
coarse
instrument suite at each depth
ship time (expensive)
Cruises:
good spatial resolution,
poor temporal resolution
costly

## Slide 5: Scalable approaches
http://nasa.gov/ (June 2014 MODIS)
Remote Sensing
AUVs
Auvac.org
Profiling Floats
Argo.ucsd.edu
Marts, T. OCB Floats and Gliders Workshop 2009.
2 gliders: $300 k
MRO: $60 k/yr
5 yrs: $600k
WHOI REMUS Shark Cam
Notes: Remote Sensing (satelite pictures).
calibrated algorithms approximate Chl a
1km resolution daily, with monthly composites to create cloud-free datasets.
Gliders
programmed sawtooth profiles
> 1000m range
sensor agnostic, modular
Floats
oil-filled buoyancy engine  change density  up/down
argo  1999  ocean heat content
3600 floats, 2000m, every 10 days
AUVs: costs roughly $150K, approx $60K/yr operate (numbers from CPF project proposal, convos with O. Schofield, C. Lee and D. Rudnick
Floats: Explain what float is. Need picture of float. Argo program is THE model. Largest ocean sensor network in the world. Started in 1999, and has deployed over 3600 floats to date

## Slide 6: Apex (ARGO) floats
Not suitable for coastal environments
Excessive drift
Coarse depth control
Chart: Float 5903610 DepthMAX
Google Earth
860 km
1,020 d
8 Aug 2014
Notes: 160 2000 m profiles battery
$30,000 per float with data and other external costs
~$24 million for global project

## Slide 7: The coastal profiling float
  Chemical Sensors Lab Hardware
    500 m capable
    ~350 profile battery life
    6 (soon 9) instrument/sensor ports
    “Anchor” between profiles (minimize drift)
    Precise depth control (shallow water ops)
Closed-Loop Buoyancy Engine
DC motor with piston pump
3 kg adjustable ballast
Tank
Prototype
Sea
Prototype
Photos: Todd Walsh
(Not to scale)

## Slide 8: Modeling the cpf
linearization
Free Body Diagram
Equation of Motion
& Linearized
Transfer Function
Dynamic Model
Root Locus Design:
PID Velocity Controller
DRAG
BUOYANCY
a
v
d
Notes: For 0.05 m/s velocity ~20g of force on 40kg float (factor of 2,000)
To put that in perspective, that’s like pushing a car with ones index finger

## Slide 9: Implementation & Results
Cascade Control
Chart: Simulated vs. Actual Response
Notes: Need to control velocity and depth
help in sampling at chosen depths with accuracy
don’t want to contact bottom at maximum speed
--Changing Velocity set point.
--bands

## Slide 10: Recommended next steps
Improve neutral buoyancy routine (mid-water parking)
Identify & mitigate source of bellows compressibility
Maximize motor runtime at maximum efficiency

## Slide 11: Acknowledgements
Gene Massion
Paul Coenen, Jonny Ferreira and Jim Montgomery
Ken Johnson & Chemical Sensors Lab
George Matsumoto & Linda Kuhnz
MBARI & George and Lucile Packard Foundation

## Slide 12: Sources
1: Laruelle, G. G. et al. Global multi-scale segmentation of continental and coastal waters from the watersheds to the continental margins. Hydrol. Earth Syst. Sci. 17, 2029–2051 (2013).
2: Mackenzie, F. T., Andersson, A. J., Lerman, A. & Ver, L. M. in The Sea Vol. 13 (eds Robinson, A. R. & Brink, K. H) 193–225 (Harvard Univ. Press, 2005).
3: Ducklow, H. H. & McCallister, S. L., in The Sea Vol. 13 (eds Robinson, A. R. & Brink, K. H) 269–305 (Harvard Univ. Press, 2004).
4: Geider et al. Primary productivity of planet earth: biological determinants and physical constraints in terrestrial and aquatic habitats. Global Change Biology. 7, 849-882 (2001).
5: UW Float data: http://runt.ocean.washington.edu/argo/homographs/index/7138.html

## Slide 13: Root Locus PID + Filter

## Slide 14: Step response - velocity

## Slide 15: Discrete (z-plane) stability
Ts = 1s
Zero-order hold

## Slide 16: linearization