## Slide 1: Overall ESP-Sampler Functional Blocks
pump
Microcontroller
carousel/
cylinder
valves
Cell/Sat
Linux
host
ESP control
WiFi/
BT/
wired
Sampler
Instrument
AWS
Big Bad Wolf Security

## Slide 2
Air
RNA Later
(preservative)
Bleach
(cleaner)
Intake
Exhaust
Flow
meter
Puck
CLAMP
Duckbill valve
manifold
Waste
Valves / Pumps for
Fluidic and Air lines
Arm
suction
cups
Vacuum pump
Pump
Pump
External
Sample Pump
Vacuum valve
Suction cup
valve
Force
Sensor
(Compressed)
Cup break
valve
Vacuum
sensor

## Slide 3: Process Flow diagrams
Complete cycle
Sample
End
Filter type
Date/Time
Deployment #
Decon system
Purge step
Select Tube
Load Puck
Filter Water
Preserve
Purge
Unload Puck
Write to puck
Write to puck
Volume filtered
start/stop time

## Slide 4: Process Flow diagram I
Purge
system
Select Tube
Load Puck
Arm in decon position
Open Intake/exhaust valves
Determine current position
External pump ON
for xx time
Close intake valve
Purge enviro water
with compressed air
Close all valves
Calc distance to new tube
Perform movement
End
Move arm to grab puck
Close clamp until clamp force = threshold
Move puck to clamp
Sample
End
Decon system
Select Tube
Load Puck
Purge System
Filter Water
Preserve
Purge
Unload Puck
Write to puck
Write to puck

## Slide 5: Process Flow diagram II
Filter Water
Preserve
Purge
All valves closed except
vacuum pump; pulls vacuum
Intake valve opens
Close intake & exhaust
External pump starts
Close vacuum
Open Exhaust
Open to waste
Flood puck w/ RNALater
End
Close RNALater
Pump air to clear puck
Open Air
Sample
End
Decon system
Select Tube
Load Puck
Purge System
Filter Water
Preserve
Purge
Unload Puck
Write to puck
Write to puck

## Slide 6: Process Flow diagram III
Decon system
Unload Puck
Move arm to decon position
Close clamp until clamp
force = threshold
Close all valves
reacquire puck
move puck to bucket
open clamp
Move arm to engage puck
End
Sample
End
Decon system
Select Tube
Load Puck
Purge System
Filter Water
Preserve
Purge
Unload Puck
Write to puck
Write to puck
Close exhaust, vacuum, and waste valves. Open intake valve.
Pump bleach ‘upstream’
Close intake valve bleach ‘upstream’