## Slide 1: Environmental DNA (eDNA)
Labor-intensive, weather-dependent, boring
Difficult access, logistically complicated
Notes: Who here has heard of eDNA?
…
As organisms move through the water, they continuously shed genetic material. This leaves a physical trace that we can collect and analyze to identify what species are present, instead of trying to catch or observe organisms directly.
eDNA analysis starts with sample collection, and traditionally, this has been labor-intensive, weather-dependent, and frankly, quite boring work.
This is made even more complicated by difficult access, and complicate logistics.

## Slide 2
Notes: Our partners at The United States Geologic Survey (USGS) came to us with a problem.
Part of their mission is to understand and monitor the biological health of water resources within the United States.
In this context, that means early detection of invasive species.
To do this effectively they need to sample, ideally, daily at the scale of the entire united states.
The combined space and time scales of their goals far exceed their personnel.
What they do have is infrastructure.
Take the largest continental US watershed , the Missouri. About 1000 square km.
Ignore the trees… the dots on this map represent sites where USGS has field sites.

## Slide 3: Instrument Overview
FIDO Instrument
Sample Puck with RFID Tag
144 Sample Cylinder
Notes: At the start of this year, we completed our production design.
The instrument at its core is quite simple - it's designed to filter water and apply a preservative to the collected sample.
FIDO expands on the puck concept of the second generation ESP.
Samples are collected using small cylindrical pucks that contain standard 47mm filter paper and an RFID tag to store sample metadata.
144 of these pucks are held within a 3D printed interchangeable cylinder.
This cylinder is loaded into the FIDO instrument which is constructed using sheet metal panels and 3D printed components.
By keeping the mechanism cost low, we were able focus our spending on the components directly responsible for collection and preservation, the valves, pumps and pucks.

## Slide 5: FIDO: Instrument Overview
Waste
Container
Used Puck
Storage
Reagent Storage
Sample Cylinder
2G ESP Not FIDO
Washing Machine Not FIDO
Notes: FIDO fits within a ½ cubic meter and was designed to be accessed by users from the front and to fit into tight spaces like the gauge houses I showed earlier.
2G installed inside a big one…
From the front, users can install pucks, access reagents, removed collected samples, and dispose of waste.

## Slide 6: FIDO: Instrument Overview
Sample Outlet &
Flow sensor
Puck
Manipulation
Micropython
Motherboard
Vacuum System
Rock Pi
Notes: If you need to work on FIDO…
The back of the instrument allows access to its electronics and plumbing.

## Slide 9
Prepare
Install
Operate
Service
Recover
Notes: Now that you have an idea of what FIDO is, I think the best way to complete the picture is to walk through how it will actually be used using the USGS use case as an example.

## Slide 10: FIDO: Pucks
Prepare
Notes: Everything starts in the lab.
Pucks are cleaned, assembled, and installed into a cylinder.
Reagent are made and bottled.
This is also where the pucks have their first bit of meta data written to them (serial number, filter porosity, etc)
I mention this because
Important, can be time consuming, can require lots of training (3G)
---
Emphasis on the puck system

## Slide 11
Install
Notes: Once you have everything ready, you need to carry (quite literally) everything out into the field and hook it up.
This could be its own presentation, and is very application specific, so I’m not going to dive into much. I’d be very happy to talk more about this later with anyone who is interested.

## Slide 12
Operate
Notes: Once the instrument is installed, you drop in the cylinder and reagents, close the lid and walk away.

## Slide 13: FIDO: System Architecture
Micropython
Rock Pi
Notes: Users interact with FIDO through a web interface on any device that they have.
Each instrument can be accessed locally or through the cloud. This interface to communicates with a Rock Pi that handles interfacing with the instrument controller running Micropython.
This system lets users plan and schedule sampling as well as collect manual samples.

## Slide 14: FIDO: Instrument Overview
Operate
Grab
Pinch
Filter
Preserve
Notes: When the instrument collects a sample, the following sequence occurs.
The instrument indexes the cylinder to the first tube.
It turns on the vacuum system, and grabs a puck.
Moves it into the clamp and pinches it between two manifolds.

## Slide 15: FIDO: Fluid System & Reagents
Filter
Preserve
Notes: It then collects a sample, letting water flow through the instrument and back to the source.
Sampling ends biased on flow rate, time, or volume.
Once enough water has been sampled, we apply a preservative

## Slide 16
Store
Decontaminate
Operate
Release
Sweep
Decontaminate
Notes: Next we release the used puck and sweep it into storage.
The clamp then closes on itself and decontaminates the flow path using bleach and waits for the next sample.

## Slide 17
Service
Notes: When you’ve collected enough samples, you visit the instrument and retrieve them and reload the instrument with more pucks and reagents.
Back at the lab you start processing.
I highlight this because…
Like preparation… emphasis on the puck system

## Slide 18
Recover
Notes: When your totally done, you get to haul all that stuff out of there.

## Slide 19: Next Steps
Validation is continuing
10 production units are currently being built
Open to collaborate on field deployments
Looking to license to commercial vendor
Notes: Hopefully that gives you a good sense of FIDO and how it works.
Looking forward…
We're continuing validation work
We're currently building 10 production units that will be deployed throughout the United States this year and next as part of the READI-Net pilot program.
Beyond that, we're actively seeking collaborations for field deployments to expand our understanding of FIDO's capabilities across different environments.
Ultimately, we're looking to license this technology to a commercial partner who can make it widely available to the research community. If you're interested in collaborating or learning more, please find me after the presentation.

## Slide 20: Acknowledgments
Notes: This work wouldn't be possible without our fantastic team at MBARI and our partners at USGS. Special thanks to Adam Sepulveda for leading the READI-Net initiative. Funding came from the United States Geological Survey.

## Slide 21: Questions?
Waste
Container
Used Puck
Storage
Reagent Storage
144 Sample Cylinder
Sample Outlet &
Flow sensor
Puck
Manipulation
Micropython
Motherboard
Vacuum System
Roc Pi
Notes: Thank you for your attention, and I'm happy to take questions.